## Slide 1: CCSv6 Tips & Tricks
Embedded Development Tools

## Slide 2: Tips and Tricks
General
  Workspaces
  Getting Started views
  ‘Simple’ Perspective
  Windows and Views (basics)
  Installing Eclipse Plug-ins
Projects
  Working Sets
  Editor Tips
  Indexer
  Useful CCS Edit Views
Debugging
  Debug Configurations
  Debugging Without a Project
  Useful Debug Views

## Slide 3: General
Notes: 3

## Slide 4: Eclipse Concept: Workspaces
Main working folder for CCS
Contains information to manage all the projects defined to it
  The default location of any new projects created
User preferences, custom perspectives, cached data for plug-ins, etc are all stored in the workspace
Multiple workspaces can be maintained
  Only one can be active within each CCS instance
  The same workspace cannot be shared by multiple running instances of CCS
  It is not recommended to share workspaces amongst users
Notes: 4

## Slide 5: Use Multiple Workspaces
Multiple Users: Keep separate workspaces for each user on a shared machine
  Custom preferences, layouts, etc will be maintained on a per user basis
  Each user can be working on specific project(s) that would only be applicable to a their workspace
Project Organization: Break up all your CCS projects into separate workspaces for better maintenance
  A workspace for each software release
  A workspace for each module/feature of a release
Performance: The larger the contents of the workspace (number of open projects), the greater the impact on performance of CCS
Notes: 5

## Slide 6: (Occasionally) Clean Your Workspace
The workspace folder can get corrupted over time
Good idea to periodically clean your workspace for best CCS (Eclipse) performance and stability
To clean workspace, either:
  Delete the .metadata folder in workspace folder
  Use a new workspace folder
Before cleaning, save current workspace settings so they can be imported into the new workspace
  Save settings: File->Export...->General->Preferences->To preference file
  Import Settings: File->Import...->General->Preferences->From preference file
Any projects will have to be re-imported after cleaning the workspace
Notes: 6

## Slide 7: View: Getting Started
Access a variety of resources from the Getting Started page:
  Code examples
  Support forums
  Training material
  CCS Videos
  Additional TI content (App Center)
  Create/Import projects
Available from the View menu

## Slide 8: View: TI Resource Explorer
Easily access a broad selection of software packages including:
  controlSUITE
  MSP430ware
  TivaWare
  TI-RTOS
Guides you step by step through using examples
Browse resources:
  Documentation
  Videos

## Slide 9: View: App Center
Access a variety of TI content from the CCS App Center page
  Browse/install additional content (plug-ins, compilers, code examples)
  Check for additional updates to installed content
  Available from the View menu

## Slide 10: Perspective: Simple
Single perspective that combines just the most common features of the CCS Edit and CCS Debug perspectives
  Simplifies the environment for new users
  Avoid perspective switching when starting a debug session
Open the Simple perspective from the Getting Started page

## Slide 11: Windows and views
Notes: 11

## Slide 12: Window Types
Tab Group: Several windows grouped together
Editor: Only editor windows are part of this group
Detached: Floating window not tied to Workbench
Fast view: Hidden until you click on the button to restore them. Click on another window to hide.
Notes: 12

## Slide 13: Windowing Tips
Double-clicking on the title bar of a window will maximize the window
  Double-clicking again will restore it to its previous size
Fast-view windows are great for windows you use infrequently but need a lot of space when you do use them
The window that has focus is indicated by a blue border and heading
Current window
Notes: 13

## Slide 14: Customizing Perspectives
You can customize the menu items and toolbars in your perspective
  Right click on the toolbar and select Customize Perspective
Notes: 14

## Slide 15: Using the Keyboard…
All key bindings can be viewed and modified: Window -> Preferences -> General -> Keys
Key bindings are part of the general preferences that can be exported to a preferences file and imported

## Slide 16: Accessing Views
To open a new view go to the View menu
  List the most commonly used views with CCS
To access views that are not listed select Other…
Many useful “hidden” views…
Notes: 16

## Slide 17: Quick Access Field
Global search field that will search all of CCS
Search for:
  Views
  Commands
  Menu items
  Preferences

## Slide 18: Filter Field
Use it to find options/properties faster in the scope of a specific dialog/view
  Narrows list of options down depending on characters entered in the field
Available in many dialogs
  Project Properties
  Window Properties
  Workspace Properties..
  Target Configuration view

## Slide 19: Eclipse Plug-ins
Notes: 19

## Slide 20: Eclipse Plug-ins - Basics
CCSv6 is based on Eclipse and is able to leverage many of the huge selection of 3rd party Eclipse plug-ins available
  http://marketplace.eclipse.org/
CCSv6.0 is based off Eclipse 4.3 and CDT 8.2
  Look for plug-ins that support this version for best compatibility
CCS App Center focuses on TI specific content and only shows a tiny fraction of available Eclipse plug-ins

## Slide 21: Eclipse Plug-ins - Marketplace
Find additional Eclipse plug-ins from within CCS with the Eclipse Marketplace plug-in
  Help -> Eclipse Marketplace…
  Browse through a list of featured or popular plug-ins
  Search for plug-ins with a keyword search
  Easy install of any plug-in found in the marketplace

## Slide 22: Eclipse Plug-ins - Installation
Use the Eclipse Update Manager to install plug-ins if the plug-in update site is already known
  Help -> Install New Software for new updates to install (specify remote site (URL) or local site (directory) )
Drop-in plugins manually
  Many plug-ins can be simply downloaded as an archive and copied into the .\ccsv6\eclipse\dropins folder

## Slide 23: Projects
Notes: 23

## Slide 24: Working Sets (1)
Use working sets to group projects inside the Project Explorer
  Useful for multi-core environments to clearly differentiate projects by which core they are for
Change the select to selected working sets. Then click the New… button
Notes: 24

## Slide 25: Working Sets (2)
Select C/C++ as the type of working set and click Next
Give your working set a name and select the projects that you want to be part of it. Click Finish
Notes: 25

## Slide 26: Working Sets (3)
Then go through the process again for the next working set. Once you have the both created make sure they are checked and the click OK
Now you need to change the project explorer to organize by the working set
Notes: 26

## Slide 27: Parallel Builds
Have a multi-core PC? Take advantage of all those cores to speed up your CCS project builds with parallel builds!
In the project properties, under the Behavior tab under Build, turn on the Enable parallel build option
Notes: 27

## Slide 28: Source Code Editor
CCS comes with an excellent, feature rich editor
Code Completion (CTRL+SPACE for suggestions)
Editor tabs
Collapse and expand functions
Outline view displays lists structural elements for the selected source file
Notes: 28

## Slide 29: Advanced Editor Features
Code Completion
  Complete word
  Auto-member information
  Auto-parameter information
Navigation
  Back/Forward buttons
  Back to last edit button
  Go to definition
  Go to declaration
Code Folding
  Collapse functions
Notes: 29

## Slide 30: Advanced Editor Features
Right-click in the editor margin to:
  Toggle line numbers in the editor margin
  Enable/Disable code Folding
  Enable/Disable Quick Diff
  Open editor Preferences… to access more options to configure:
    Content Assist (Code Completion)
    Folding
    Syntax Coloring
    Hovers (Cursor "hover over" behavior)
    Typing behavior
    etc
Notes: 30

## Slide 31: Edit Markers
If you have the line number column on, it also indicates changes in your source file since your last save
Modified lines
Deleted lines
Inserted lines
Notes: 31

## Slide 32: Variable Highlighting
Highlighting a variable in the editor will highlight all instances of the variable in the editor
Notes: 32

## Slide 33: Source Templates
CCS provides code templates
  Ex: Hello World
    Type in h in the editor and use Content Assist by pressing CTRL+SPACE keys (can also right-click in the editor and select Content Assist from the context menu)
  Create custom templates for commonly used source code blocks or customize existing templates
    Window->Preferences…->C++->Editor->Templates
Notes: 33

## Slide 34: Indexer
The advanced editor features rely on a database of the source and header files of the project that provides the basis for C/C++ search, navigation features and parts of content assist (code completion)
The C/C++ Indexer creates this database by parsing all of the source and header files of the projects open in the workspace
Configure the Indexer:
  Window -> Preferences -> C/C++ -> Indexer
Notes: 34

## Slide 35: Indexer
The Indexer can also be configured on a per project basis in the project properties
  Must click on the Show Advanced Settings link in the lower left corner of the project properties dialog to expose the options for the Indexer
  C/C++ General -> Indexer
Notes: 35

## Slide 36: Performance Tip: Turn off the Indexer
Don’t use the CCS editor or don’t need the advanced editor features?
Turn off the Indexer!
  The indexer constantly scans all open projects to support some advanced editor features
  The indexer can use a decent amount of system resources, causing CCS to appear sluggish
    This is most evident with large projects or many open projects in the workspace (or both)
  The default CCS setting is to have the indexer enabled
Notes: 36

## Slide 37: Troubleshooting Tip: Rebuild the Index
Advanced editor feature not working right?
  Code completion not working or bringing up the wrong suggestions?
  Open declaration not finding the declaration?
  Outline/Hierarchy views showing incorrect information?
Indexed database/cache may have gotten corrupted or is out of date!
Rebuild it!
  Right-click on a project and select Index -> Rebuild to rebuild the indexed database for that project
Notes: 37

## Slide 38: View: History
CCS keeps a local history of source changes
  Switch to the CCS Edit perspective
  Right-click on a file in the editor an select Team -> Show Local History
    Opens History view
Use the History view to compare the current source file against any previous version or replace it with any previous version
  Double-click on a revision to open it in the editor
  Right-click on a revision to compare that revision to the current version
CCS also keeps project history
  Recover files deleted from the project
  Right-click on the project and select “Recover from Local History” in the context menu
History view
File Comparer
Notes: 38

## Slide 39: Local History - Project
CCS keeps a local history of files for the project
  Recover files deleted from the project
  Right-click on the project and select Recover from Local History in the context menu
Notes: 39

## Slide 40: View: Outline
Displays an outline of a structured file that is currently open in the editor area, and lists structural elements
View -> Outline

## Slide 41: View: Include Browser
Which header files is this source file including? Who is including this header file? Directly? Indirectly?
Show hierarchy of included header files for a source file
View -> Other… -> C/C++ -> Include Browser

## Slide 42: View: Call Hierarchy
Displays callers and callees for a selected function
Right-click on a function and then select Open Call Hierarchy in the context menu
Notes: 42

## Slide 43: Debugging
Notes: 43

## Slide 44: Debug Configurations
Debug information created when a debug session is first launched for a project or target configuration
  Information stored includes which target configuration to use, debug settings…
Both project and project-less debug sessions launch debug sessions using a debug configuration
  A debug session can be started by explicitly launching a debug configuration
To configure: Use drop-down menu next to the Debug As button and select Debug Configurations…

## Slide 45: Debug Configurations
Interface to manage existing configuration or to create new ones
Existing debug configurations are configurable

## Slide 46: Debug Configurations – Main Options
Use the Main tab to:
  Which target configuration to use
  Use the Initialization Script field to specify a DSS JavaScript for target initialization
  Specify which devices on the JTAG scan chain will be visible by in the Debug view by default
  Specify if all CPUs share the same console for C I/O (for multi-core debug)
    C I/O will be interleaved in the same console (preceded with the CPU name)
    Uncheck the option to create a separate C I/O console for each CPU

## Slide 47: Debug Configurations – Program Options
Use the Program tab to:
  Specify which CPU to load the executable on (for multi-core devices)
    Can specify different programs for each CPU
  Specify to load the program (default) or just symbols only (to debug code in flash, etc)

## Slide 48: Debug Configurations – Target Options
The Target tab can be used to set a variety of debug options like auto-run to main, auto-connect to a HW target, real-time options, program verification on load, etc…
Flash Programmer options are available for applicable devices

## Slide 49: Debug Configurations – Source Options
The Source tab allows you to add additional source lookup search paths
  Specify paths on a per CPU granularity (for multi-core devices)
  All paths to any source files in your project are automatically added by default

## Slide 50: Debug Configurations – Common Options
The Common tab contains a collection of miscellaneous options
  Can specify the debugger to send all CIO to a file instead of the console
  Specify character encoding

## Slide 51: Troubleshooting Tip: Debug Configuration
Having some strange debugger issues?
  Having problems launching a debug session?
  Can’t connect to the target anymore?
  Is the debug session unstable?
Debug Configuration may have gotten corrupted!
Delete it and have CCS generate a new one
  Select the Debug Configuration to delete in the Debug Configurations dialog and press the delete button
Notes: 51

## Slide 52: Troubleshooting Tip: Test Connectivity
Having target connection issues?
Validate your physical JTAG connection to the device from the driver
Use the Test Connection button in the Advanced tab of the target configuration
  Will test both the target configuration file and the JTAG connectivity between CCS and the target by running some diagnostics
  If all test pass, then the physical connection between the device and the driver is fine and the issue is with the debugger
  If there are failures, send the results to TI support
Not all emulators support this feature
  http://processors.wiki.ti.com/index.php/Debugging_JTAG_Connectivity_Problems

## Slide 53: Debugging Without a Project
For project-less debug sessions, CCS will look for source files using relative path information stored in the debug symbols
  CCS will find the source files if the executable and source files are in the exact same location as when the executable was originally built
If the location of the executable file or source (or both) has changed, CCS may not be able to find the source files
CCS can be instructed where to find the source files one of two ways:
  Tell CCS where the first file is and let CCS find the rest of the files using relative path information in the symbols (recommended method)
  Set Source Lookup Paths for CCS to scan when looking for source files:
    Set for current debug session
    Set for Debug Configuration - apply for every debug session launched by the debug configuration (under the Source options}
    Set at global (workspace) level – apply for any debug session started with this workspace
Notes: 53

## Slide 54: Method #1 (Recommended)
If a source file cannot be found during debug, it will be indicated in the editor
Use Locate the Source File… button to browse to the location of the source file
  The debugger can then find other source files in the same location or use relative path information to find files relative to the current file
  Location is remembered for future loads of the same program
This method has the best performance for finding source files
Notes: 54

## Slide 55: Method #2 – Debug Context (CCSv6.0.x)
Source lookup paths can also be explicitly specified for each debug context
Right-click in the Debug view and select Edit Source Lookup… in the context menu
To add a file system path, select File System Directory to browse to and add paths
For multi-core debugging, each debug context has its own set of source lookup paths
NOTE: This option is only available for CCSv6.0.x
Notes: 55

## Slide 56
The Source tab in the debug configuration allows you to add additional source lookup search paths
  All paths to any source files in your project are automatically added by default
  Debug Configurations may also be accessed during an active debug session by right-clicking in the debug view and select "Edit <Debug Configuration>“ in the context menu
Method #3 – Debug Configuration

## Slide 57: Method #4 – Global (Workspace)
Source lookup paths can also be set globally to apply for all debug contexts (in a multi-core environment) and debug sessions
  Windows -> Preferences -> C/C++ -> Debug -> Source Lookup Path
Notes: 57

## Slide 58: More Debugging: Source Lookup Paths
Once the path is known to the debugger (using any method), the source file will be opened in the debugger
Method #1 is recommended due to having the best performance
The other methods will do recursive searches inside the specified directories when searching for files. If the directories have many subfolders and many files inside, the search may be slow and thus lead to slow performance when looking for the source files
Notes: 58

## Slide 59: View: Modules
Provides information for all loaded symbol files
View -> Modules

## Slide 60: View: Terminal
Terminal emulator that can connect to a remote target via a serial port or over TCP/IP using the TELNET or SSH protocol.
View -> Other… -> Terminal -> Terminal

## Slide 61: View: Remote Systems
Remote Systems Explorer (RSE) is an Eclipse plug-in that provides:
  Drag-and-drop access to the remote file system
  Remote shell execution
  Remote terminal
  Remote process monitor
RSE must be enabled in the workspace preferences (Window -> Preferences )
Access Remote Systems view via View -> Other… -> Remote Systems -> Remote Systems