## Slide 1: Code Composer Studio
MSP430 Energy Trace Lab Material
TM

## Slide 2: LaunchPad: Hardware Setup
Agenda …
Connect mini-USB cable
from PC to board

## Slide 3: Lab Files
Make sure the lab files, containing the code necessary for all labs has been unzipped and is ready. The recommendation is to keep it (as will be assumed in the following steps) in c:/ti/ccs_workshop/etracelab
This could create a directory structure as shown below

## Slide 4: LAB conventions
Lab steps are numbered for easier reference
  …
  …
Explanations, notes, warnings are written in blue
  Warnings are shown with
  Information is marked with
  Tips and answers are marked with
  Questions are marked with
Notes: 4

## Slide 5: Lab 1: Energy trace Basics 30 minutes
Open CCS and select the default workspace
You can close the TI Resource Explorer View (it will not be used)
Notes: 5

## Slide 6: Lab 1: Exercise Summary
Key Objectives
  What is energy trace
  Using energy trace in ccs
Tools and Concepts Covered
  Energy Trace
Notes: 6

## Slide 7: Workspace
Launch CCS and select a workspace folder
  Defaults to your user folder
Notes: 7

## Slide 8: Create the Project
Create a new project in the CCS Workspace by going to menu Project  New CCS Project
Fill in the boxes as shown in the image. Select the “Blink the LED” example
Click Finish

## Slide 9: ULP Advisor Message
A message highlighting the ULP Advisor may appear on project creation
This message can be ignored
Use the “Do not show this again” checkbox if you do not wish to see this message again

## Slide 10: Debug ‘lab1’ Project
Click on the “green bug” button – make sure the project is selected!

## Slide 11: Debug ‘lab1’ Project
Should the ULP message appear (which can be disabled with the ”do not show again” tickbox) simple select “proceed”

## Slide 12: Build, Load/Flash the Program
Notes: 12

## Slide 13: Open Energy Trace
Not all MSP devices support the full energy trace feature set
Open the Energy Trace view
  View  Other->MSP430-EnergyTrace
Select “Energy Trace”
Select “ok”
Notes: 13

## Slide 14: Energy Trace now available
Notes: 14

## Slide 15: Configure Energy Trace
The buttons on the console in order from left to right are:
  Enable/Disable Energy Trace
  Set capture Time
  Save EnergyTrace Data
  Load Energy Trace Data
  Advanced Options
  Toggle between Energy Only Mode and Full Mode (showing state data)
Notes: 15

## Slide 16: Configure Energy Trace
Select the “Set Capture Time Button”
  Set the capture time to 30s for this example/lab
Notes: 16

## Slide 17: Run the code
Press Run to start the code and energy trace (which is by default in energy only mode)
You will see energy trace start up doing a live count and capture
Notes: 17

## Slide 18: Run the code
When 30 Seconds have elapsed, double click on energy trace to get full view
Notes: 18

## Slide 19: Examine the Data and Views
Examine the data and view available! Main View
Notes: 19

## Slide 20: Examine the Data and Views
Energy View
Notes: 20

## Slide 21: Examine the Data and Views
Power View
Notes: 21

## Slide 22: Terminate the Debug Session
Minimize EnergyTrace and click on the terminate button to end this session
This will kill the debugger and return you to the Edit perspective
We will now move on to part 2 where we will look at the full feature (state capture) mode
We will use the same project!

## Slide 23: Debug ‘lab1’ Project
Click on the “green bug” button once again– make sure the project is selected! Our terminating the session should have brought you back here!

## Slide 24: ULP Advisor Message
A message highlighting the ULP Advisor may appear on project creation
This message can be ignored
Use the “Do not show this again” checkbox if you do not wish to see this message again

## Slide 25: Debugging a second Time
Note energy trace is still available
Notes: 25

## Slide 26: Configure Energy Trace
Select the “Advanced Button” and set preferences as shown
Notes: 26

## Slide 27: Run the code
Press Run to start the code and energy trace (which is by default in energy only mode)
You will see energy trace start up doing a live count and capture as previously
Notes: 27

## Slide 28: Examine the State View
Maximize and examine the data and view available! State View
Notes: 28

## Slide 29: Notes
Explore the energy trace + views and data!

## Slide 30: Terminate the Debug Session
Minimize EnergyTrace and click on the terminate button to end this session
This will kill the debugger and return you to the Edit perspective
We are finished lab1!

## Slide 31: Lab 2: Energy trace – comparing data 30 minutes
Open CCS and select the default workspace
You can close the TI Resource Explorer View (it will not be used)
Notes: 31

## Slide 32: Lab 2: Exercise Summary
Key Objectives
  More advanced energy trace look
  Capturing and comparing data to asses the affect of code changes
Tools and Concepts Covered
  Advanced energy trace
Notes: 32

## Slide 33: Workspace
Launch CCS and select a workspace folder
  Defaults to your user folder
Notes: 33

## Slide 34: Create the Project
Create a new project in the CCS Workspace by going to menu Project  New CCS Project
Fill in the boxes as shown in the image. Select the “Empty Project” template
Click Finish

## Slide 35: ULP Advisor Message
A message highlighting the ULP Advisor may appear on project creation
This message can be ignored
Use the “Do not show this again” checkbox if you do not wish to see this message again

## Slide 36: Add code for lab2
Drag and drop “first.c” and “second.c” into the empty project just created
Leave the default “copy files” selected as shown and ensure the c files are now in the project
You should now have the file as part of your project.

## Slide 37: Setup Project
Exclude “second.c” from the build, we will use this later
Right click on “second.c” and select “Exclude from build”
You should now have the file excluded

## Slide 38: Debug ‘lab2’ Project
Click on the “green bug” button once again– make sure the project is selected! Our terminating the session should have brought you back here!
Enter Debug mode as before

## Slide 39: ULP Advisor Message
A message highlighting the ULP Advisor may appear on project creation
This message can be ignored
Use the “Do not show this again” checkbox if you do not wish to see this message again

## Slide 40: Debug Lab2
Notes: 40

## Slide 41: Open Energy Trace
Not all MSP devices support the full energy trace feature set
Once in Debug mode, open the Energy Trace view
  View  Other->MSP430-EnergyTrace
Select “Energy Trace”
Select “ok”
Notes: 41

## Slide 42: Energy Trace now available
Notes: 42

## Slide 43: Configure Energy Trace
Select the “Set Capture Time Button”
  Set the capture time to 30s for this example/lab
Notes: 43

## Slide 44: Run the code
Press Run to start the code and energy trace (which is by default in energy only mode)
You will see energy trace start up doing a live count and capture
Notes: 44

## Slide 45: Save Energy Trace Data
Once the 30s capture is done, select “save current energy profile”
You will be asked to name and locate your file, leaving the default is fine, so select “save”, but remember where it is!
Notes: 45

## Slide 46: Terminate the Debug Session
Minimize EnergyTrace and click on the terminate button to end this session
This will kill the debugger and return you to the Edit perspective
We will now use the other more energy efficient piece of code we pasted and compare! This version does not use delays and does use low power modes.

## Slide 47: Setup Project
Exclude “first.c” from the build, we already have the data
Right click on “first.c” and select “Exclude from build”
You should now have the file excluded

## Slide 48: Setup Project
Include “second.c” from the build, we will use this later
Right click on “second.c” and select “Exclude from build” again to reinclude the file.
You should now have the file included and ready to capture this data

## Slide 49: Debug Lab2
Notes: 49

## Slide 50: Run the code
Press Run to start the code and energy trace (which is by default in energy only mode)
You will see energy trace start up doing a live count and capture
Note energy trace is still set to 30s
Notes: 50

## Slide 51: Save Energy Trace Data
Once the session reaches the 30s, select “save current energy profile”
You will be asked to name and locate your file, leaving the default is fine, so select “save” but remember where!
Notes: 51

## Slide 52: Load Energy Trace Data
Open the previous data from the non efficient version which we just saved by selecting “load reference energy profile”
You will be asked to select and locate your file, so select the file we just created with “first.c”
Notes: 52

## Slide 53: Examine the Data and Views
Double click to expand energy trace to full view and see the views/comparison
Notes: 53

## Slide 54: Examine the Data and Views
See how much more efficient the second.c code is
Notes: 54

## Slide 55: Examine the Data and Views
See how much more efficient the second.c code is
Notes: 55

## Slide 56: Terminate the Debug Session
Minimize EnergyTrace and click on the terminate button to end this session
This will kill the debugger and return you to the Edit perspective
We are finished lab2!