This is an implementation of ITU G.722.1 recommendations on TI C55x processor

Mixed C and C55x assembly code implementation

eXpressDSP™ compliant

Bit-exact with all ITU G722.1 test sequences

description

ITU-T G.722.1 is the coder for wideband speech operating at bit rates of 24 and 32 kbps. The Annex-C of the codec supports super wideband speech operating at bit rates of 24, 32 and 48 kbps. It is a low complexity encoder and decoder that may be used for 7 kHz and 14 kHz bandwidth audio signals working at 24 kbit/s, 32 kbit/s or 48 kbit/s.

Encoder takes linear PCM input signals (14, 15 or 16 bit 2’s complement) sampled at 16 kHz sampling rate and encodes using Modulated Lapped Transform (MLT) technology to give 24 kbit/s or 32 kbit/s bit-rates. The Annex-C encoder supports PCM input signals sampled at 32 kHz sampling rate to give encoded signals at 24 kbit/s, 32 kbit/s or 48 kbit/s.

Codec operates at 20ms frames

Bit Compliant with ITU-T G.722.1 specifications

Optimized for TI C55x DSP

C callable interface for encoder and decoder

Re-entrant multi channel implementation

Implementation Compatible with TI XDAIS rules

Fully interruptible Code

Relocatable tables

Efficient Scratch memory management with reduced stack requirements

The implementation support run time data buffers relocation & table relocation

Fully validated on TMS320C5510 DSK, using CCS version 3.3 with the code generation tools version 2.74

Summary of performance

Configuration Table

| Configuration | ID |
| --- | --- |
| Encoder – 20ms | G722_1_001 |
| Decoder – 20ms | G722_1_002 |
| Full Duplex – 20ms | G722_1_003 |

Cycles Information – TMS320C5510 TEB

| Configuration ID | Performance Statistics (IN MEGACYCLES/SEC) 1 |
| --- | --- |
|  | wideband | superwideband |
| G722_1_001 | 2.03 | 4.2 |
| G722_1_002 | 1.93 | 3.89 |
| G722_1_003 | 3.96 | 8.09 |

Measured with frame size= 320 samples (20ms)

Memory Statistics - Generated with Code Generation Tools Version 2.74

| Configuration | Memory Statistics2 |
| --- | --- |
|  | Program MEMORY | Data Memory | Total |
|  |  | Internal | External | Stack |  |
| G722_1_001 | 4.328 | 41.052 | 0 | 0.104 | 45.484 |
| G722_1_002 | 4.395 | 41.876 | 0 | 0.216 | 46.487 |
| G722_1_003 | 8.723 | 44.78 | 0 | 0.328 | 53.831 |

2 All memory requirements are expressed in kilobytes (1 kilobyte = 1024 8-bit bytes).

Internal Data Memory Split-up

| Configuration | Data Memory – Internal3 |
| --- | --- |
|  | Shared | Instance4 |
|  | Constants | Scratch |  |
| G722_1_001 | 31.34 | 6.808 | 2.904 |
| G722_1_002 | 31.34 | 6.808 | 3.728 |
| G722_1_003 | 31.34 | 6.808 | 6.632 |

3 All memory requirements are expressed in kilobytes (1 kilobyte = 1024 8-bit bytes)

4 Does not include I/O buffers

notes

- Total Data Memory for N Non-Pre-Emptive Instances =

Constants + Runtime Tables + Scratch + N*(Instance + I/O buffers + Stack)

- Total Data Memory for N Pre-Emptive Instances =

Constants + Runtime Tables + N*(Instance + I/O buffers + Stack + Scratch)

references

ITU Recommendation G.722.1

glossary

Constants	Elements that go into .const memory section

Scratch	Memory space that can be reused across different instances of the algorithm

Shared	Sum of Constants and Scratch

Instance	Persistent-Memory that contains persistent information - allocated for each instance of the algorithm

acronyms

ITU	International Telecommunication Union

ITU-T	Telecommunication Standardization Sector of ITU

REVISION HISTORY

Scope: Applicable updates to the G722.1 on TMS320C5510 have been incorporated.

| DATE | VERSION | ADDITIONS/CHANGES/DELETIONS |
| --- | --- | --- |
| 14 APR 2008 | 1.0 | Initial Version |

# IMPORTANT NOTICE

Texas Instruments Incorporated and its subsidiaries (TI) reserve the right to make corrections, modifications, enhancements, improvements, and other changes to its products and services at any time and to discontinue any product or service without notice. Customers should obtain the latest relevant information before placing orders and should verify that such information is current and complete. All products are sold subject to TI's terms and conditions of sale supplied at the time of order acknowledgment.

TI warrants performance of its hardware products to the specifications applicable at the time of sale in accordance with TI's standard warranty. Testing and other quality control techniques are used to the extent TI deems necessary to support this warranty. Except where mandated by government requirements, testing of all parameters of each product is not necessarily performed.

TI assumes no liability for applications assistance or customer product design. Customers are responsible for their products and applications using TI components. To minimize the risks associated with customer products and applications, customers should provide adequate design and operating safeguards.

TI does not warrant or represent that any license, either express or implied, is granted under any TI patent right, copyright, mask work right, or other TI intellectual property right relating to any combination, machine, or process in which TI products or services are used. Information published by TI regarding third- party products or services does not constitute a license from TI to use such products or services or a warranty or endorsement thereof. Use of such information may require a license from a third party under the patents or other intellectual property of the third party, or a license from TI under the patents or other intellectual property of TI.

Reproduction of information in TI data books or data sheets is permissible only if reproduction is without alteration and is accompanied by all associated warranties, conditions, limitations, and notices. Reproduction of this information with alteration is an unfair and deceptive business practice. TI is not responsible or liable for such altered documentation.

Resale of TI products or services with statements different from or beyond the parameters stated by TI for that product or service voids all express and any implied warranties for the associated TI product or service and is an unfair and deceptive business practice. TI is not responsible or liable for any such statements.

# Text boxes

DSP

GPP

Customer Application

Alg

Alg

G722.1

Alg

Alg

Alg

FRAMEWORK

PSP