- Mixed C and C55x assembly code implementation

- Bit-exact with ITU G.726 specification

- Fully re-entrant code

- C callable and XDAIS( compliant

Description

TI’s G.726 ADPCM voice coder is an implementation of the ITU G.726 voice coder for the TMS320C55x. The implementation works at 4 different bit rates namely 16/24/32/40 kbps.

Summary of MIPS utilization for TI G726

The DSP C5510 is operating at 200 MHz. The data shown was obtained by profiling the code on C5510 Rev2.0 Silicon.

Details of DSP (’C55x) resources required

[Memory in words]

|  | Average MIPs | Peak MIPs | Program Memory | Scratch* | Persistent* | Table (const) | Stack (worst-case) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| On 5510 Daughter | Program – in internal memory Data – Scratch, Stack, Static and tables in internal memory |
| Encoder | 3.3883 | 3.4863 | 1860 | 80 | 90 | 736 | 615 |
| Decoder | 3.8965 | 3.9831 | 1902 | 80 | 90 | 736 | 616 |
| Full Duplex | 7.2848 | 7.4694 | 2888 | 80 | 180 | 736 | 616 |

* Per Channel Memory

Program Memory size – split up

[Memory in words]

|  | Source Code | XDAIS Wrapper | Total |
| --- | --- | --- | --- |
| Encoder | 1492 | 368 | 1860 |
| Decoder | 1534 | 368 | 1902 |
| Full Duplex | 2390 | 498 | 2888 |

Encoder Buffers

| Block No | Block Name | Attribute | Accessed by B Bus | Size in words | Alignment | Place-ment |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | ADPCM_INSTANCE_BUFN | STATIC | NO | 24 | 2 | SARAM |
| 1 | ADPCM_CODER_BUF_SIZE | STATIC | NO | 66 | 2 | SARAM |
| 2 | ADPCM_CODER_SCRATCH_BUF_SIZE | SCRATCH | NO | 80 | 2 | DARAM |

Decoder Buffers

| Block No | Block Name | Attribute | Accessed by B Bus | Size in words | Alignment | Place-ment |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | ADPCM_INSTANCE_BUFN | STATIC | NO | 24 | 2 | SARAM |
| 1 | ADPCM_CODER_BUF_SIZE | STATIC | NO | 66 | 2 | SARAM |
| 2 | ADPCM_CODER_SCRATCH_BUF_SIZE | SCRATCH | NO | 80 | 2 | DARAM |

IMPORTANT NOTICE

Texas Instruments (TI) reserves the right to make changes to its products or to discontinue any semiconductor product or service without notice, and advises its customers to obtain the latest version of relevant information to verify, before placing orders, that the information being relied on is current.

TI warrants performance of its semiconductor products and related software to the specifications applicable at the time of sale in accordance with TI’s standard warranty. Testing and other quality control techniques are utilized to the extent TI deems necessary to support this warranty. Specific testing of all parameters of each device is not necessarily performed, except those mandated by government requirements.

Certain applications using semiconductor products may involve potential risks of death, personal injury, or severe property or environmental damage (“Critical Applications”).

TI SEMICONDUCTOR PRODUCTS ARE NOT DESIGNED, INTENDED, AUTHORIZED, OR WARRANTED TO BE SUITABLE FOR USE IN LIFE-SUPPORT APPLICATIONS, DEVICES OR SYSTEMS OR OTHER CRITICAL APPLICATIONS.

Inclusion of TI products in such applications is understood to be fully at the risk of the customer. Use of TI products in such applications requires the written approval of an appropriate TI officer. Questions concerning potential risk applications should be directed to TI through a local SC sales office.

In order to minimize risks associated with the customer’s applications, the customer to minimize inherent or procedural hazards should provide adequate design and operating safeguards.

TI assumes no liability for applications assistance, customer product design, software performance, or infringement of patents or services described herein. Nor does TI warrant or represent that any license, either express or implied, is granted under any patent right, copyright, mask work right, or other intellectual property right of TI covering or relating to any combination, machine, or process in which such semiconductor products or services might be or are used.

Copyright © 2003, Texas Instruments Incorporated

# Text boxes

# Customer Application

Alg

Alg

Alg

Alg

G.726

Alg

DSP/BIOS™

# Customer Application

Alg

Alg

Alg

Alg

G726

Alg

DSP/BIOS™