## Slide 1: IPC Training
Processor Communication Link

## Slide 2: Agenda
Overview
IPC Modules
Configuration
Scalability
Optimization
Footnotes

## Slide 3: Overview
Inter-Processor Communication (IPC)
  Communication between processors
  Synchronization between processors
Two modes
  Peer-to-peer
    All cores running TI-RTOS
  Master-slave
    Master core running HLOS (e.g. Linux, QNX, Android)
    Slave cores running TI-RTOS
Notes: Communication: sending messages between processors
Synchronization: protect critical sections shared between processors

## Slide 4: Overview
Rich device support
  Homogeneous devices
    C6472, C6678, ...
  Heterogeneous devices
    OMAP5, DRA7XX, TCI6638K2X, OMAP-L138, F28M35, ...

## Slide 5: Overview
Flexible design supports many use cases
  Many thread combinations (Task, Swi, Hwi)
  Two types of messaging: notification, message queuing
  Multi- or uni-processor environments
Hardware abstraction
  Device-specific support for hardware spinlocks, inter-processor mailbox
  IPC APIs are same across devices (e.g. GateMP implemented with hardware spinlock or software Peterson algorithm as needed)
OS-agnostic
  Same APIs on all operating systems

## Slide 6: Overview - Architecture
Hardware
IPC
SYS/BIOS
Application

## Slide 7: Overview
Top-level modules, used by application
Ipc
MessageQ
Notify
MultiProc
SharedRegion
GateMP
NameServer
HeapMemMP
HeapBufMP
ti.sdo.ipc
ti.sdo.utils

## Slide 8: Overview – create/open
Create/open model used to share instances of IPC modules
Shared objects are “created” by the owner and “opened” by the user(s)
  Some objects may be opened multiple times (e.g. MessageQ, GateMP).
  Objects must have system-wide unique names
Delete/close methods are used to finalize objects
  Owner should not delete until all users have closed

## Slide 9: Overview
Cache Management
  Cache coherency operations are performed by the module when shared state is accessed/modified
  Shared data is padded to prevent sharing cache line with other data
Data Protection
  Shared data is protected by a multi-processor gate when accessed/modified

## Slide 10: Agenda
Overview
IPC Modules
  Lab 1 – ex01_hello
Configuration
Scalability
Optimization
Footnotes

## Slide 11: IPC Modules
Ipc – IPC Manager
MessageQ – send and receive messages
NameServer – distributed name/value database
Notify – send and receive event notifications
MultiProc – processor identification
SharedRegion – shared memory address translation
GateMP – protect a critical section
HeapMemMP, HeapBufMP – multi-processor memory allocator
Notes: List of important modules; not complete list of all modules.

## Slide 12: Ipc Module
Ipc – IPC Manager
  Used to initialize IPC and synchronize with other processors.
  Application must call Ipc_start and Ipc_attach.
Two startup protocols
  Ipc.ProcSync_ALL - all processors start at same time
  Ipc.ProcSync_PAIR – host processor starts first
Configuration
    Ipc.procSync configures startup protocol
    When using Ipc.ProcSync_ALL, Ipc_attach is called internally from Ipc_start. Application does not call Ipc_attach.

## Slide 13: Ipc Module – Ipc.ProcSync_ALL
DSP1
Ipc_start()
Log_print("IPC ready")
IPU1
Ipc_start()
Log_print("IPC ready")
HOST
Ipc_start()
Log_print("IPC ready")
Reserved
Header
Flags
Heap
SR_0
handshake
completes
var Ipc = xdc.useModule('ti.sdo.ipc.Ipc');
Ipc.procSync = Ipc.ProcSync_ALL;
var MultiProc = xdc.useModule('ti.sdo.utils.MultiProc');
MultiProc.setConfig(proc, ["HOST", "IPU1", "DSP1"]);
app.cfg
host is owner of SR_0
Notes: main – single thread, busy wait; no interrupts
thread level – task never blocks, idle task will not run

## Slide 14: IPC Module – Ipc.ProcSync_PAIR
DSP1
Ipc_start()
do {
status = Ipc_attach(HOST)
} while (status == Ipc_E_NOTREADY)
Log_print("IPC to HOST ready")
IPU1
Ipc_start()
do {
status = Ipc_attach(HOST)
} while (status == Ipc_E_NOTREADY)
Log_print("IPC to HOST ready")
HOST
Ipc_start()
do {
status = Ipc_attach(IPU1)
} while (status == Ipc_E_NOTREADY)
Log_print("IPC to IPU1 ready")
do {
status = Ipc_attach(DSP1)
} while (status == Ipc_E_NOTREADY)
Log_print("IPC to DSP1 ready")
Reserved
Header
Flags
Heap
SR_0
handshake
completes
var Ipc = xdc.useModule('ti.sdo.ipc.Ipc');
Ipc.procSync = Ipc.ProcSync_PAIR;
host is owner of SR_0

## Slide 15: Ipc Module
Topology
  Topology expresses which processors communicate with IPC
Transport created between two processors when they attach
  In previous example, HOST attached to IPU1 and DSP1.
  If IPU1 and DSP1 need to communicate with IPC, they must also attach to each other.
Using Ipc.ProcSync_ALL creates transports between all processors.
HOST
IPU1
DSP1
transport
IPU1 and DSP1 must attach to create their own transport

## Slide 16: Ipc Module
Why have two modes?
  Because some applications are static and some are dynamic.
Static System
  In a static system all processors are started at the same time. Once the processor is loaded, same application runs forever. IPC startup is part of device boot phase. This is typical for homogeneous devices.
  Base station, telecommunication, single purpose application.
Dynamic System
  In a dynamic system, host processor boots first. Slave processors are booted later depending on application. Slave is shut down when application terminates. Slave reloaded many times, possibly with different executable.
  Consumer electronics, cell phone.

## Slide 17: Ipc Module - API
API Summary
  Ipc_start – reserve memory, create default gate and heap
  Ipc_stop – release all resources
  Ipc_attach – setup transport between two processors
  Ipc_detach – finalize transport

## Slide 18: Ipc Module - ROV
ROV screen shot

## Slide 19: MessageQ
DSP1
MessageQ – send and receive messages
A message queue receives messages
  Single reader, multiple writers on same message queue
Message queue instance created by reader, opened by writers
cmdQ:MessageQ
msg
msg
msg
msg
IPU1
writer
IPU2
writer
reader
writer
Notes: Reader must first create a message queue instance. Then, writers would open the same message queue instance to get a handle to it.
There are no “outbound” queues. All queues are “inbound”. Not like email (i.e. Outlook) where you’re outbound email goes to your Outbox and the system delivers the message to the recipient’s Inbox. The writer must have a handle to the recipient’s queue.

## Slide 20: MessageQ — transport
IPU1
Transport-independent API, works with local memory, shared memory, copy based transport (SRIO)
Default transport offers zero-copy transfers via shared memory
MessageQ
Transport
Application
IPU2
MessageQ
Transport
Application

## Slide 21: MessageQ
Message structure
  Every message contains an embedded message queue header followed by the payload. Application is responsible for the header allocation.
  Message size must include header and payload sizes.
    Actual message size is typically padded
typedef struct {
Bits32 reserved0; /* reserved for List.elem->next */
Bits32 reserved1; /* reserved for List.elem->prev */
Bits32 msgSize; /* message size */
Bits16 flags; /* bitmask of different flags */
Bits16 msgId; /* message id */
Bits16 dstId; /* destination queue id */
Bits16 dstProc; /* destination processor id */
Bits16 replyId; /* reply id */
Bits16 replyProc; /* reply processor */
Bits16 srcProc; /* source processor */
Bits16 heapId; /* heap id */
Bits16 seqNum; /* sequence number */
Bits16 reserved; /* reserved */
} MessageQ_MsgHeader
MessageQ_MsgHeader
Payload
message
size
typedef struct {
MessageQ_MsgHeader reserved;
char payload[50];
} App_Msg;
Notes: Message size might be padded for cache alignment or heap alignment.

## Slide 22: MessageQ
Message types
  MessageQ_MsgHeader is structure type definition.
    typedef struct { ... } MessageQ_MsgHeader;
  MessageQ_Msg is pointer to structure type definition.
    typedef MessageQ_MsgHeader *MessageQ_Msg;
Message Allocation
  Message allocation must be large enough to hold the embedded message queue header and your payload. See Message structure.

## Slide 23: MessageQ – reader/writer
IPU  DSP
  Send a message from IPU to DSP (one-way message)
  Both processors register a heap with MessageQ module
  Receiving processor creates a message queue (DSP)
  Sending processor opens the message queue (IPU)
Sending processor will...
  allocate a message
  write the payload
  send message
Receiving processor will...
  get message
  read the payload
  free the message

## Slide 24: MessageQ – reader/writer
IPU  DSP
Reserved
Header
sr0: HeapMemMP
MessageQ
HeapId | IHeap Handle
2 | sr0: HeapMemMP
MessageQ
IPU
DSP
DSP.workq: MessageQ
MessageQ_alloc
MessageQ_put
Writer
HeapId | IHeap Handle
2 | sr0: HeapMemMP
Reader
MessageQ_get
MessageQ_free
msg
msg
msg
SharedRegion #0

## Slide 25: MessageQ – reader/writer
#include <xdc/std.h>
#include <ti/ipc/MessageQ.h>
#include <ti/ipc/SharedRegion.h>
#define HEAP_ID 2
#define MSG_SZ sizeof(MessageQ_MsgHeader) + 50
Ptr heap;
MessageQ_Msg msg;
MessageQ_QueueId qid;
heap = SharedRegion_getHeap(0);
MessageQ_registerHeap(HEAP_ID, heap);
do {
status = MessageQ_open("DSP1.workq", &qid);
Task_sleep(1);
} while (status == MessageQ_E_NOTFOUND);
while (running) {
msg = MessageQ_alloc(HEAP_ID, SIZE)
/* write payload */
MessageQ_put(qid, msg)
}
IPU (writer)

## Slide 26: MessageQ – reader/writer
#include <xdc/std.h>
#include <ti/ipc/MessageQ.h>
#include <ti/ipc/SharedRegion.h>
#define HEAP_ID 2
Ptr heap;
MessageQ_Handle que;
MessageQ_Msg msg;
heap = SharedRegion_getHeap(0);
MessageQ_registerHeap(HEAP_ID, heap);
que = MessageQ_create("DSP1.workq", NULL);
while (running) {
MessageQ_get(que, &msg, MessageQ_FOREVER);
/* read payload */
MessageQ_free(msg);
}
DSP (reader)

## Slide 27: MessageQ – client/server
IPU  DSP  IPU
  Send a message from IPU to DSP and back again (round trip message)
  Both processors create a message queue
IPU processor will...
  allocate a message
  write the payload
  send message
  wait for return message
  read payload
  free the message
DSP processor will...
  wait for message
  read the payload
  write new payload
  send message

## Slide 28: MessageQ – client/server
IPU  DSP  IPU
Reserved
Header
sr0: HeapMemMP
SharedRegion #0
MessageQ
MessageQ
IPU
DSP
DSP.workq: MessageQ
MessageQ_staticMsgInit
MessageQ_setReplyQueue
MessageQ_put
Client
Server
MessageQ_get
MessageQ_getReplyQueue
MessageQ_put
msg
msg
msg
MessageQ_get
Memory_free
msg
Memory_alloc
msg
n: MessageQ
msg
Notes: Note that message is allocated using Memory_alloc, not MessageQ_alloc. No need to register a heap.

## Slide 29: MessageQ – client/server
#include <xdc/std.h>
#include <xdc/runtime/IHeap.h>
#include <xdc/runtime/Memory.h>
#include <ti/ipc/MessageQ.h>
#include <ti/ipc/SharedRegion.h>
#define MSG_SZ sizeof(MessageQ_MsgHeader) + 50
IHeap_Handle heap;
MessageQ_Handle ipuQ;
MessageQ_Msg msg;
MessageQ_QueueId dspQ;
heap = (IHeap_Handle)SharedRegion_getHeap(0);
ipuQ = MessageQ_create(NULL, NULL);
do {
status = MessageQ_open("DSP.workq", &dspQ);
} while (status == MessageQ_E_NOTFOUND);
msg = Memory_alloc(heap, SIZE, 0, NULL);
MessageQ_staticMsgInit(msg, SIZE);
MessageQ_setReplyQueue(ipuQ, msg);
/* write payload */
MessageQ_put(dspQ, msg);
MessageQ_get(ipuQ, &msg, MessageQ_FOREVER);
/* read payload */
Memory_free(heap, msg, SIZE);
IPU (client)
Notes: Cannot use this method with copy based transports.

## Slide 30: MessageQ – client/server
#include <xdc/std.h>
#include <ti/ipc/MessageQ.h>
#include <ti/ipc/SharedRegion.h>
MessageQ_Handle dspQ;
MessageQ_QueueId qid;
MessageQ_Msg msg;
dspQ = MessageQ_create("DSP.workq", NULL);
while (running) {
MessageQ_get(dspQ, &msg, MessageQ_FOREVER);
/* process payload */
qid = MessageQ_getReplyQueue(msg);
MessageQ_put(qid, msg);
}
DSP (server)

## Slide 31: MessageQ
MessageQ works with any SYS/BIOS threading model:
  Hwi: hardware interrrupts
  Swi: software interrupts
  Task: threads that can block and yield
Variable size messages
Timeouts are allowed when a Task receives messages
Message Ownership Rules
  Acquire ownership with MessageQ_alloc, MessageQ_get
  Loose ownership with MessageQ_free, MessageQ_put
  Do not dereference a message when you don’t have ownership

## Slide 32: MessageQ
Uses an IHeap heap implementation to support MessageQ_alloc and MessageQ_free.
Heaps are coordinated across processors by a common index which is registered using MessageQ_registerHeap API
Heap ID is stored in message header

## Slide 33: MessageQ - API
API Summary
  MessageQ_create – create a new message queue
  MessageQ_open – open an existing message queue
  MessageQ_alloc – allocate a message from the pool
  MessageQ_free – return message to the pool
  MessageQ_put – send a message
  MessageQ_get – receive a message
  MessageQ_registerHeap – register a heap with MessageQ

## Slide 34: MessageQ - ROV
ROV screen shot

## Slide 35: Lab ‒ ex01_hello
Please open the PowerPoint slide named IPC_Lab_1_Hello

## Slide 36: NameServer Module
NameServer – distributed name/value database
  Manages name/value pairs
  Used for registering data which can be looked up by other processors
API Summary
  NameServer_create – create a new database instance
  NameServer_add – add a name/value entry into database
  NameServer_get – retrieve value for given name

## Slide 37: NameServer
IPU – create NameServer instance
DSP – query IPU for name/value pair
IPU
DSP
NameServer_create
Application
email: NameServer
NameServer_add
Application
NameServer_create
NameServer_get
email: NameServer
JohnDoe
johndoe@mm.com

## Slide 38: NameServer
IPU – create NameServer instance
DSP – query IPU for name/value pair
#include <string.h>
#include <xdc/std.h>
#include <ti/ipc/NameServer.h>
NameServer_Handle ns;
Char buf[];
Int len;
ns = NameServer_create("email", NULL);
strcpy(buf, “johndoe@mm.com");
Int len = strlen(buf);
NameServer_add(ns, “JohnDoe", buf, len);
#include <xdc/std.h>
#include <ti/ipc/NameServer.h>
NameServer_Handle ns;
Char buf[32];
Int len;
ns = NameServer_create("email", NULL);
NameServer_get(ns, “JohnDoe", buf, &len, NULL);
IPU
DSP

## Slide 39: NameServer Module
ROV screen shot

## Slide 40: Notify Module
Notify – send and receive event notifications
  Inter-processor notifications
  Multiplex 32 events using single interrupt line
  Some events are used by IPC
  Notification is point-to-point
Callback functions
  Register for a specific procId + lineId + eventId triplet
  Callback can be reused (use procId and lineId to de-multiplex)
  Callbacks can be chained (all callbacks are invoked)
  Callback function receives procId, eventId, arg, payload
API Summary
  Notify_sendEvent – raise an event
  Notify_registerEvent – register a callback for an event
  Notify_registerEventSingle – register for exclusive use of event
  Notify_FnNotifyCbck – callback function type definition

## Slide 41: Notify
IPU  DSP
  IPU sends a notification to the DSP
IPU processor will...
  Send a NOP event to test the connection (optional)
  Send periodic event to the DSP
DSP processor will...
  Create a semaphore to synchronize between callback and task
  Register for event notification
  Notify callback will post the semaphore
  Task will run

## Slide 42: Notify
IPU  DSP
IPU
DSP
Application
n: Semaphore
n: Task
notifyCB
CPU
Mailbox
ipc: Hwi
IPC
Notify_sendEvent
IPC
Semaphore_post
raise interrupt
Application

## Slide 43: Notify
#include <xdc/std.h>
#include <ti/ipc/MultiProc.h>
#include <ti/ipc/Notify.h>
#define EVT 12
#define NOP 0
UInt16 dsp = MultiProc_getId("DSP");
UInt32 payload;
do {
s = Notify_sendEvent(dsp, 0, EVT, NOP, TRUE);
if (s == Notify_E_EVTNOTREGISTERED) {
Task_sleep(1);
}
} while (s == Notify_E_EVTNOTREGISTERED);
do {
/* work */
payload = ...;
Notify_sendEvent(dsp, 0, EVT, payload, TRUE);
} until(done);
IPU
Notes: Only using payload and arg. If same callback is shared with other processors or event, use procId and eventId to setup proper context.
LineId is rarely used. Only needed on devices with multiple interrupt lines.

## Slide 44: Notify
#include <xdc/std.h>
#include <ti/sysbios/knl/Semaphore.h.
#include <ti/ipc/MultiProc.h>
#include <ti/ipc/Notify.h>
#define EVT 12
#define NOP 0
UInt16 IPU = MultiProc_getId("IPU");
Semaphore_Handle sem;
sem = Semaphore_create(0, NULL, NULL);
Notify_registerEvent(IPU, 0, EVT, notifyCB, (UArg)sem);
do {
Semaphore_pend(sem, BIOS_WAIT_FOREVER);
/* work */
} until(done);
Void notifyCB(UInt16 procId, UInt16 lineId,
UInt32 eventId, UArg arg, UInt32 payload)
{
Semaphore_Handle sem = (Semaphore_Handle)arg;
if (payload != NOP) {
Semaphore_post(sem);
}
}
DSP
Notes: Only using payload and arg. If same callback is shared with other processors or event, use procId and eventId to setup proper context.
LineId is rarely used. Only needed on devices with multiple interrupt lines.

## Slide 45: Notify Module
ROV screen shot

## Slide 46: MultiProc Module
MultiProc – processor identification
  Stores processor ID of all processors in the multi-core application
  Stores processor name
Processor ID is a number from 0 – (n-1)
Processor name is defined by IPC
  IPC Release Notes > Package Reference Guide > ti.sdo.utils.MultiProc > Configuration Settings > MultiProc.setConfig
  Click on Table of Valid Names for Each Device
API Summary
  MultiProc_getSelf – return your own processor ID
  MultiProc_getId – return processor ID for given name
  MultiProc_getName – return processor name

## Slide 47: SharedRegion Module
SharedRegion – shared memory address translation
  Manages shared memory and its cache configuration
  Manages shared memory using a memory allocator
  SRPtr is a portable pointer type
Multiple shared regions are supported
Each shared region has optional HeapMemMP instance
  Memory is allocated and freed using this HeapMemMP instance
  HeapMemMP_create/open and managed internally at IPC initialization
  SharedRegion_getHeap API to get this heap handle

## Slide 48: SharedRegion Module
SharedRegion #0 is special
  Always contains a heap
  Contains global state that all cores need to access (reserved header)
  Must be placed in memory that is accessible by all BIOS cores in the system
API Summary
  SharedRegion_getHeap – return the heap handle
  SharedRegion_getId – return region ID for given address
  SharedRegion_getPtr – translate SRPtr into local address
  SharedRegion_getSRPtr – translate local address into SRPtr

## Slide 49: SharedRegion Module
ROV screen shot

## Slide 50: SharedRegion
0xA0000000
Sometimes, shared memory has different address on different processors.
  Use SharedRegion to translate addresses.
2: SharedRegion
0x80000000
IPU
DSP

## Slide 51: SharedRegion
ipu.cfg
dsp.cfg
    var SharedRegion = xdc.useModule('ti.sdo.ipc.SharedRegion');
    var sr2 = new SharedRegion.Entry(
    { name: "SR_2", base: 0xA0000000, len: 0x400000, ownerProcId: 0, isValid: true, cacheEnable: false };
    SharedRegion.setEntryMeta(2, sr2);
    var SharedRegion = xdc.useModule('ti.sdo.ipc.SharedRegion');
    var sr2 = new SharedRegion.Entry(
    { name: "SR_2", base: 0x80000000, len: 0x400000, ownerProcId: 0, isValid: true, cacheEnable: false };
    SharedRegion.setEntryMeta(2, sr2);

## Slide 52: SharedRegion
#include <xdc/std.h>
#include <ti/ipc/SharedRegion.h>
Ptr ptr = 0xA0004000;
SRPtr srptr = SharedRegion_getSRPtr(ptr, 2);
/* Write SRPtr into message payload
* and send message to DSP.
*/
msg->srptr = srptr;
MessageQ_put(q, msg);
#include <xdc/std.h>
#include <ti/ipc/SharedRegion.h>
/* Receive message, translate
* embedded SRPtr into local pointer.
*/
MessageQ_get(q, &msg);
SRPtr srptr = msg->srptr;
Ptr ptr = SharedRegion_getPtr(srptr);
/* ptr = 0x80004000 */
IPU
DSP

## Slide 53: GateMP Module
GateMP – protect a critical section
  Multiple processor gate that provides context protection against threads on both local and remote processors
API Summary
  GateMP_create – create a new instance
  GateMP_open – open an existing instance
  GateMP_enter – acquire the gate
  GateMP_leave – release the gate

## Slide 54: GateMP
Use GateMP instance to protect buffer from concurrent access
IPU processor will...
  create a GateMP instance
  enter the gate
  modify shared memory
  leave the gate
DSP processor will...
  open the GateMP instance
  enter the gate
  modify shared memory
  leave the gate

## Slide 55: GateMP
2: SharedRegion
IPU
DSP
/* modify buffer */
GateMP_leave
Application
buf
GateMP_enter
buf: GateMP
GateMP_create
/* modify buffer */
GateMP_leave
Application
GateMP_enter
GateMP_open

## Slide 56: GateMP Module
#include <xdc/std.h>
#include <ti/ipc/GateMP.h>
GateMP_Params params;
GateMP_Handle gate;
GateMP_Params_init(&params);
params.name = "BufGate";
params.localProtect = GateMP_LocalProtect_NONE;
params.remoteProtect = GateMP_RemoteProtect_SYSTEM;
gate = GateMP_create(params);
GateMP_enter(gate);
/* modify buffer */
GateMP_leave(gate);
#include <xdc/std.h>
#include <ti/ipc/GateMP.h>
GateMP_Handle gate;
GateMP_open("BufGate", &gate);
GateMP_enter(gate);
/* modify buffer */
GateMP_leave(gate);
IPU
DSP

## Slide 57: HeapMemMP HeapBufMP Modules
HeapMemMP, HeapBufMP – multi-processor memory allocator
  Shared memory allocators that can be used by multiple processors
  HeapMemMP – variable size allocations
  HeapBufMP – fixed size allocations, deterministic, ideal for MessageQ
IPC’s versions of HeapBuf, adds GateMP and cache coherency to the version provided by SYS/BIOS.
All allocations are aligned on cache line size.
  Warning: Small allocations will occupy full cache line.
Uses GateMP to protect shared state across cores.
HeapBufMP. All buffers are same size (per instance)
Every SharedRegion uses a HeapMemMP instance to manage the shared memory

## Slide 58: HeapMemMP HeapBufMP Modules
API Summary
  HeapMemMP_create – create a heap instance
  HeapMemMP_delete – delete a heap instance
  HeapMemMP_open – open a heap instance
  HeapMemMP_close – close a heap instance
  HeapMemMP_alloc – allocate a block of memory
  HeapMemMP_free – return a block of memory to the pool
  HeapBufMP_create – create a heap instance
  HeapBufMP_delete – delete a heap instance
  HeapBufMP_open – open a heap instance
  HeapBufMP_close – close a heap instance
  HeapBufMP_alloc – allocate a block of memory
  HeapBufMP_free – return a block of memory to the pool

## Slide 59: HeapMemMP Module
ROV screen shot

## Slide 60: HeapMemMP
Create a heap and share it between IPU and DSP
IPU processor will...
  Creates a heap instance
  Use Memory module to allocate memory
DSP processor will...
  Open the heap instance
  Use Memory module to allocate memory

## Slide 61: HeapMemMP Module
DSP
IPU
SharedRegion
data: HeapMemMP
Application
HeapMemMP_create
Memory_alloc
Application
HeapMemMP_open
Memory_alloc

## Slide 62: HeapMemMP Module
#include <xdc/std.h>
#include <xdc/runtime/IHeap.h>
#include <xdc/runtime/Memory.h>
#include <ti/ipc/HeapMemMP.h>
#include <ti/sdo/ipc/heaps/HeapMemMP.h>
HeapMemMP_Params params;
HeapMemMP_Params_init(&params);
params.name = "DataHeap";
params.regionId = 0;
params.sharedBufSize = 0x100000;
HeapMemMP_Handle handle;
handle = HeapMemMP_create(&params);
IHeap_Handle heap;
heap = HeapMemMP_Handle_upCast(handle);
ptr = Memory_alloc(heap, size, align, NULL);
#include <xdc/std.h>
#include <xdc/runtime/IHeap.h>
#include <xdc/runtime/Memory.h>
#include <ti/ipc/HeapMemMP.h>
#include <ti/sdo/ipc/heaps/HeapMemMP.h>
HeapMemMP_Handle handle;
HeapMemMP_open("DataHeap", &handle);
IHeap_Handle heap;
heap = HeapMemMP_Handle_upCast(handle);
ptr = Memory_alloc(heap, size, align, NULL);
Casting the heap handle is one of the few places you need to call an IPC Package API.
IPU
DSP

## Slide 63: Agenda
Overview
IPC Modules
Configuration
Scalability
Optimization
Footnotes

## Slide 64: IPC Configuration
The RTSC configuration phase is when components are integrated. Each component uses its configuration parameters to express its system requirement.
The application configuration script is the starting point. It defines which components are needed by the application and configures those components depending on its needs.
MessageQ
Application
var MessageQ = xdc.useModule('ti.sdo.ipc.MessageQ');
MessageQ.maxNameLen = 48; /* default = 32 */
app.cfg
Application will use MessageQ
Create long message queue names
A rule of thumb: If you include the header file in your C code, then you need to "use" the module in the configuration script.

## Slide 65: IPC Configuration – documentation
Navigate to the IPC product folder
    C:\Products\ipc_3_30_pp_bb
Open the release notes
    ipc_3_30_pp_bb_release_notes.html
Scroll down to the documentation section
  Click on Package Reference Guide (cdoc)
  Tip: the Package Reference Guide is also available in CCS Help.
  Tip: the Package Reference Guide is also available on-line.
Open 'all modules' section
Click on a module (e.g. MessageQ)
Click on Configuration settings link

## Slide 66: IPC Configuration - documentation
  The documentation shows how to include the module in the application configuration script.
  Scroll down to the 'module-wide config parameters' for a list of all configuration parameters.

## Slide 67: IPC Configuration - documentation
When a config param has a default value, it will be indicated after the type.
If the config param does not have a default value, this is indicated by the keyword undefined. Sometimes default values are computed during the configuration phase.
Scroll down to the 'module-wide functions' section. Sometimes you will need to use these to set a config param.

## Slide 68: IPC Configuration - documentation
Instance Configuration Parameters
  Some config params are specified when creating an instance. These are listed in the 'per-instance config parameters' section.
However, IPC modules only support instance creation at run-time. You will need to find the equivalent create parameter in the IPC API Reference Guide.
  Open the release notes
    ipc_3_30_pp_bb_release_notes.html
  Scroll down to the documentation section.
    Click on IPC Application Programming Interface (API) Reference Guide (HTML)
    Tip: the IPC API Reference Guide is also available in CCS Help.
    Tip: the IPC API Reference Guide is also available on-line.

## Slide 69: Ipc Module Configuration
IPC configuration requires the following modules
  ti.sdo.ipc.Ipc
  ti.sdo.utils.MultiProc
  ti.sdo.ipc.SharedRegion
Define Ipc startup protocol
  Ipc.procSync – controls attach behavior
    Ipc.ProcSync_ALL – Attach to all processors simultaneously.
    Ipc.ProcSync_PAIR – Attach to remote processor one-by-one.
All processors must use the same startup protocol.
  var Ipc = xdc.useModule('ti.sdo.ipc.Ipc'); Ipc.procSync = Ipc.ProcSync_PAIR;

## Slide 70: Ipc Module Configuration
SharedRegion #0 Memory Setup
  On some systems, the SR_0 memory may not be available at boot time. Host processor might map the memory into the slaves MMU. This configuration flag is used to block the slave until the memory is available. Ipc_start will spin until this flag is set true by host.
  Ipc.sr0MemorySetup = true;
    Ipc_start will access SR_0 memory immediately.
  Ipc.sr0MemorySetup = false;
    Ipc_start will spin until host sets flag to true. Requires symbol address access from host.

## Slide 71: Ipc Module Configuration
Attach and detach hooks
  You can register hook functions to be called during each attach and detach call. Use the hook function to perform application specific tasks.
    var Ipc = xdc.useModule('ti.sdo.ipc.Ipc'); var fxn = new Ipc.UserFxn; fxn.attach = '&userAttachFxn'; fxn.detach = '&userDetachFxn'; Ipc.addUserFxn(fxn, arg);
  The hook functions have the following type definitions.
    Int (*attach)(UArg arg, UInt16 procId); Int (*detach)(UArg arg, UInt16 procId);

## Slide 72: MultiProc Configuration
Define the processors in the IPC application.
  This example defines three processors: CORE0, CORE1, CORE2.
  Name order defines MultiProc ID (zero based counting number)
  CORE0 configuration
    var procNameAry = ["CORE0", "CORE1", "CORE2" ]; var MultiProc = xdc.useModule('ti.sdo.utils.MultiProc'); MultiProc.setConfig("CORE0", procNameAry);
  CORE1 configuration
    var procNameAry = ["CORE0", "CORE1", "CORE2" ]; var MultiProc = xdc.useModule('ti.sdo.utils.MultiProc'); MultiProc.setConfig("CORE1", procNameAry);
  CORE2 configuration
    var procNameAry = ["CORE0", "CORE1", "CORE2" ]; var MultiProc = xdc.useModule('ti.sdo.utils.MultiProc'); MultiProc.setConfig("CORE2", procNameAry);
Notes: Note the same processor list is used by all executables. Only the local processor name changes. This code is typically placed in a common file used by all executables.

## Slide 73: SharedRegion Configuration
Define number of shared regions in the system.
  This config param must be the same across all processors in the system. Increasing the number of regions reduces the maximum size of each region.
    var SharedRegion = xdc.useModule('ti.sdo.ipc.SharedRegion'); SharedRegion.numEntries = 8;

## Slide 74: SharedRegion Configuration
Define number of shared regions in the system.
  This config param must be the same across all processors in the system. Increasing the number of regions reduces the maximum size of each region.
    var SharedRegion = xdc.useModule('ti.sdo.ipc.SharedRegion'); SharedRegion.numEntries = 8;
Cache Line Size
  This value is used to align items on a cache line boundary. For example, memory allocations from the shared region heap will be aligned and sized on this boundary. It must be the same value for all processors using the shared region. It must be the worst case value
    SharedRegion.cacheLineSize = 128;

## Slide 75: SharedRegion Configuration
Define SharedRegion #0
  The shared region base and size are defined in the platform memory map.
    config.bld Build.platformTable["ti.platforms.evm6678:core0"] = { ... externalMemoryMap: [ ["SR_0", { name: "SR_0", space: "data", access: "RW", base: 0x84000000, len: 0x200000, comment: "SR#0 Memory (2 MB)" }],
  Reference the memory map from platform to configure SR_0
    app.cfg var SR0Mem = Program.cpu.memoryMap["SR_0"]; SharedRegion.setEntryMeta(0, new SharedRegion.Entry({ name: "SR_0", base: SR0Mem.base, len: SR0Mem.len, ownerProcId: 0, isValid: true, cacheEnable: true }) );

## Slide 76: SharedRegion Configuration
Cache setting for a shared region.
  Reports memory cache setting
    This config param does not control the cache behavior, it reflects the cache behavior. In other words, if the shared memory is eligible for caching, then this parameter must be set true.
  Controls IPC cache operations
    When set to true, IPC will perform the necessary cache operations.
  Processor relative
    It may be different on each processor using the same shared region. This comes about because each processor defines its cache behavior.

## Slide 77: Build Configuration
Build module used to configure library type.
  var Build = xdc.useModule('ti.sdo.ipc.Build'); Build.LibType = Build.LibType_NonInstrumented;
Build.LibType
  Build.LibType_Instrumented – Prebuild library supplied in IPC product. Optimized with logging and asserts enabled.
  Build.libType_NonInstrumented – Prebuilt library supplied in IPC product. Optimized without instrumentation.
  Build.libType_Custom – Rebuilds IPC libraries from source for each executable. Optimized by default. Use Build.customCCOpts to modify compiler options.
  Build.libType_Debug – Rebuilds IPC libraries from source for each executable. Non-optimized, useful for debugging IPC sources.

## Slide 78: Build Configuration
Build module used to configure library type.
  var Build = xdc.useModule('ti.sdo.ipc.Build'); Build.LibType = Build.LibType_NonInstrumented;
Build.LibType
  Build.LibType_Instrumented – Prebuild library supplied in IPC product. Optimized with logging and asserts enabled.
  Build.libType_NonInstrumented – Prebuilt library supplied in IPC product. Optimized without instrumentation.
  Build.libType_Custom – Rebuilds IPC libraries from source for each executable. Optimized by default. Use Build.customCCOpts to modify compiler options.
  Build.libType_Debug – Rebuilds IPC libraries from source for each executable. Non-optimized, useful for debugging IPC sources.
  Build.libType_PkgLib – Links with package libraries in the IPC product. These libraries to not ship with the product. You must rebuild the IPC product to generate the package libraries. Useful for development and sharing custom libraries.

## Slide 79: MessageQ Configuration
Message Queue Name Length
  The maximum length of a message queue name is set at configuration time.
    var MessageQ = xdc.useModule('ti.sdo.ipc.MessageQ'); MessageQ.maxNameLen = 48;
Number of message queue heaps
  The MessageQ module maintains a table of registered heap handles. The size of this table is set at configuration time. The heapId field in the message queue header is used to index into this table. The heapId must be system wide unique. For example, if ProcA and ProcB share a heap, it might be registered with heapId = 0. If ProcC and ProcD share a different heap, their registered heapId cannot be 0. Keep this in mind when configuring the size of the heap table.
    MessageQ.numHeaps = 12;

## Slide 80: Notify Configuration
Number of events supported by Notify
  By default, the Notify module will support the maximum number of possible events. You can reduce this to conserver on memory footprint.
    var Notify = xdc.useModule('ti.sdo.ipc.Notify'); Notify.numEvents = 16;
Number of reserved events
  Use this config param to reserve events for middleware modules. IPC already reserves some number, so do not reduce this value. You can increase the value to reserve additional events for your middleware.
    Notify.reservedEvents = 8;

## Slide 81: Notify Configuration
Number of events supported by Notify
  By default, the Notify module will support the maximum number of possible events. You can reduce this to conserver on memory footprint.
    var Notify = xdc.useModule('ti.sdo.ipc.Notify'); Notify.numEvents = 16;

## Slide 82: GateMP Configuration
Maximum Name Length
  The maximum name length for a GateMP instance is controlled by this config param. Although this is a module-wide config parameter, it is used by the GateMP module when creating its private NameServer instance.
    var GateMP = xdc.useModule('ti.sdo.ipc.GateMP'); GateMP.maxNameLen = 48;
Device-specific gate delegates offer hardware locking to GateMP
  GateHWSpinlock for OMAP4, OMAP5, TI81XX, Vayu
  GateHWSem for C6474, C66x
  GateAAMonitor for C6472
  GatePeterson, GatePetersonN for devices that don’t have HW locks

## Slide 83: GateMP Configuration
GateMP has three proxies
  RemoteSystemProxy RemoteCustom1Proxy RemoteCustom2Proxy
Each proxy is assigned a delegate module. The delegate is the one which actually implements the gate. Typically, the system delegate will use hardware support if available and the custom delegates are software implementations.
  GateMP.RemoteSystemProxy = xdc.useModule('ti.sdo.ipc.gates.GateHWSpinlock'); GateMP.RemoteCustom1Proxy = xdc.useModule('ti.sdo.ipc.gates.GatePeterson'); GateMP.RemoteCustom2Proxy = xdc.useModule('ti.sdo.ipc.gates.GateMPSupportNull');
Note: GatePeterson works for only two clients. Use GatePetersonN for three or more clients.
Notes: Use GateMPSupportNull if you don’t need a proxy and want to save on memory.

## Slide 84: GateMP Configuration
The hardware spinlocks are reused as GateMP instances are deleted and re-created.
When creating a GateMP instance, the remoteProtect create parameter specifies which proxy to use.
  #include <ti/ipc/GateMP.h> GateMP_Params params; GateM_Handle gate; GateMP_Params_init(&params); params.name = "BufGate"; params.remoteProtect = GateMP_RemoteProtect_CUSTOM1; gate = GateMP_create(&params);
Notes: TODO: show mapping of remote protect to proxies

## Slide 85: GateMP Configuration
On Vayu, GateHWSpinlock is the default remote system delegate. It has a config parameter for specifying the base address of the hardware spin locks. It does not have a default value because it is set internally based on the device. You can override the default by setting it in your config script.
  var GateHWSpinlock = xdc.useModule(‘ti.sdo.ipc.gates.GateHWSpinlock’); GateHWSpinlock.baseAddr = 0x4A0F6800;
The number of hardware spinlocks to use is set by an internal config parameter (look at the xdc file to see this). This is also set internally based on the device. However, it is possible to override this in your config script. Warning: this is not a common practice.
  GateHWSpinlock.numLocks = 64;

## Slide 86: Agenda
Overview
IPC Modules
Configuration
Scalability
Optimization
Footnotes

## Slide 87: Scalability
IPC scalability allows you to include as little or as many modules as you need.
Scalability allows you to manage the IPC footprint (data and code) contributed to your executable.
Scalability options
  Utilities only
  Notify only
  IPC full

## Slide 88: Scalability — Utilities only
Application provides its own IPC framework. The utilities package provides foundational support.
The application uses only the MultiProc module. Do not use the Ipc module.
  var MultiProc = xdc.useModule('ti.sdo.utils.MultiProc');
To use the NameServer module, application must provide an INameServerRemote impementation. (Advanced topic.)
  ti.sdo.utils.INameServerRemote

## Slide 89: Scalability — Notify only
At this scalability level, the Notify and MultiProc modules are the only IPC modules used by the application.
Do not use the Ipc module. No calls to Ipc_start or Ipc_attach.
Call Notify_attach per transport to enable notify. After this call, the processor is able to receive notify events.
If needed, the application is responsible to "handshake" between sender and listener.
Only supported with notify mailbox driver.

## Slide 90: Scalability — Notify only
Notify only configuration
  var MultiProc = xdc.useModule('ti.sdo.utils.MultiProc'); var Notify = xdc.useModule('ti.sdo.ipc.Notify');
Notify attach example
  #include <ti/sdo/ipc/Notify.h> #include <ti/sdo/utils/MultiProc.h> Int procId; procId = MultiProc_getId("EVE1"); Notify_attach(procId, 0);

## Slide 91: Scalability — IPC full
This is the default scalability level
Must configure the following modules
    ti.sdo.ipc.Ipc ti.sdo.ipc.SharedRegion ti.sdo.utils.MultiProc
Application is entitled to use all IPC modules.

## Slide 92: Lab ‒ ex13_notifypeer
Please open the PowerPoint slide named IPC_Lab_3_Sclability

## Slide 93: Agenda
Overview
IPC Modules
Configuration
Scalability
Optimization
Footnotes

## Slide 94: IPC Optimization — wiki page
Through configuration parameters, IPC can be optimized for a given application. There is a good wiki topic on this.
  http://processors.wiki.ti.com/index.php/IPC_Users_Guide/Optimizing_IPC_Applications
Using dedicated GateMP instances can reduce runtime contention.
There are a few transports available. They have different restrictions and runtime performance.

## Slide 95: IPC Optimization — heap + gate
Heaps will use the default gate. When creating two independent heap instances, there would be unnecessary contention for the same gate. To reduce contention for this gate, use a dedicated GateMP instance for your heap.
  Create the GateMP instance
  Assign gate instance in heap create parameter
  Create the heap
  The dedicated gate is used automatically

## Slide 96: IPC Optimization — heap + gate
When using the default gate, two independent heaps will contend for the same gate.
SharedRegion
a: HeapBufMP
b: HeapBufMP
default: GateMP
IPU
Application
HeapMem_create
DSP
Application
HeapMem_open

## Slide 97: IPC Optimization — heap + gate
When using a dedicated gate for each heap, there is no contention for the gate (between the heaps).
SharedRegion
a: HeapBufMP
b: HeapBufMP
default: GateMP
IPU
Application
HeapMem_create
DSP
Application
HeapMem_open
heapA: GateMP
heapB: GateMP

## Slide 98: IPC Optimization — heap + gate
This example creates a heap to be used by MessageQ. A dedicated GateMP instance is used for the heap.
#include <xdc/std.h>
#include <ti/ipc/GateMP.h>
#include <ti/ipc/HeapBufMP.h>
HeapBufMP params;
HeapBufMP_Params_init(&params);
params.name = "HeapA";
params.blockSize = 128;
params.numBlocks = 32;
params.gate = GateMP_create(NULL);
HeapBufMP_Handle heap;
heap = HeapBufMP_create(params);
MessageQ_registerHeap(0, heap);
No need to specify a name for the gate. The default protection will be used.

## Slide 99: IPC Optimization — message transport
The MessageQ module uses a transport for actual message delivery. There are three available transports, each with different runtime performance characteristics.
  TransportShm – slowest, largest data footprint, most robust (default)
  TransportShmCirc – medium, fixed length transport buffer
  TransportShmNotify – fastest, may cause sender to busy wait
Each transport has a corresponding setup module. To use a given transport, configure the MessageQ module with the transport’s setup module.
  TransportShmSetup – the setup module
  TransportShmCircSetup – the setup module
  TransportShmNotifySetup – the setup module
Message transport are in the following folder.
  ipc_3_xx_pp_bb/packages/ti/sdo/ipc/transports
All MessageQ modules must be configured to use the same transport.

## Slide 100: IPC Optimization — message transport
Example configuration
  var MessageQ = xdc.useModule('ti.sdo.ipc.MessageQ'); MessageQ.SetupTransportProxy = xdc.useModule('ti.sdo.ipc.transports.TransportShmNotifySetup');

## Slide 101: IPC Optimization — notify driver
The Notify module uses a low-level driver to implement the actual signaling between processors. Each driver has a corresponding setup module. To use a given driver, configure the Notify module with the driver’s setup module.
Generic (i.e. software) notify drivers are in the following folder.
  ipc_3_xx_pp_bb/packages/ti/sdo/ipc/notifyDrivers
  NotifyDriverShm – (default) NotifyDriverCirc
Device specific (i.e. hardware) notify drivers are in the family folder.
  ipc_3_xx_pp_bb/packages/ti/sdo/ipc/family
  ti81xx/NotifyDriverMbx vayu/NotifyDriverMbx
All Notify modules must be configured to use the same driver.
Notify driver list is constantly changing as we add new device support.
Notes: Not all families have hardware driver implementations.

## Slide 102: IPC Optimization — notify driver
The setup modules are always device specific, even when using a generic driver. Look in the family folder to see which setup modules are available for your device.
  ipc_3_xx_pp_bb/packages/ti/sdo/ipc/family
Here is an example for the C647x device.
  ipc_3_xx_pp_bb/packages/ti/sdo/ipc/family/c647x
  NotifySetup.xdc – (default) NotifyCircSetup.xdc
Here is an example for ti81xx device.
  ipc_3_xx_pp_bb/packages/ti/sdo/ipc/family/ti81xx
  NotifySetup.xdc – (default) NotifyCircSetup.xdc NotifyMbxSetup.xdc

## Slide 103: IPC Optimization — notify driver
Example configuration for C647x
  var Notify = xdc.useModule('ti.sdo.ipc.Notify'); Notify.SetupProxy = xdc.useModule('ti.sdo.ipc.family.c647x.NotifyMbxSetup');

## Slide 104: IPC Optimization — Vayu notify driver
Vayu notify driver configuration is different!
There is only one notify setup module for Vayu.
  ti.sdo.ipc.family.vayu.NotifySetup
Available notify drivers on Vayu.
  ti.sdo.ipc.notifyDrivers.NotifyDriverShm – (default) ti.sdo.ipc.family.vayu.NotifyDriverMbx
Notify driver configuration is specified for each connection.
Notes: You can use different driver for each connection. Warning: the default might change!

## Slide 105: IPC Optimization — Vayu notify driver
Example configuration for Vayu (on DSP1)
  var NotifySetup = xdc.useModule('ti.sdo.ipc.family.vayu.NotifySetup'); NotifySetup.connections.$add( new NotifySetup.Connection({ procName: "EVE1", driver: NotifySetup.Driver_MAILBOX }) ); NotifySetup.connections.$add( new NotifySetup.Connection({ procName: “DSP2", driver: NotifySetup.Driver_SHAREDMEMORY }) );
Notes: No need to configure Notify.SetupProxy; already assigned for given device.
Unspecified connections use the default driver (NotifyDriverShm).

## Slide 106: Agenda
Overview
IPC Modules
Configuration
Scalability
Optimization
Footnotes

## Slide 107: Footnotes — Examples
Examples are provided in the following location.
  ipc_3_xx_pp_bb/examples/<platform>
Examples are platform and OS-specific. Not all examples are provided for all environments.
  Makefile-based, demonstrating multicore-friendly build model
  Developed independent of specific SDKs, so memory maps don’t always align.
Use DRA7xx_bios_elf for Vayu platform
  DRA7xx = platform
  bios = host operating system (i.e. SYS/BIOS on all processors)
  elf = ELF tool chain

## Slide 108: Footnotes – Error Handling
Many of the IPC APIs return an integer as a status code. All error values are negative; all success values are zero or positive. You can use a simple test to check for error.
  Int status; status = MessageQ_get(...); if (status < 0) { /* error */ }
Some APIs return a handle. If the handle is NULL, an error has occurred.
  MessageQ_Handle queue; queue = MessageQ_create(...); if (queue == NULL) { /* error */ }
IPC status codes come in two groups: success and error. The ‘S’ and ‘E’ in the status code tells you if it is success or error.
  MessageQ_S_ALREADYSETUP
  MessageQ_E_NOTFOUND

## Slide 109: Footnotes – Online Resources
IPC Documentation
  IPC API Reference (Doxygen) – latest release
  IPC Configuration Reference (Cdoc) – latest release
External wiki articles that will continue to evolve:
  Overview - http://processors.wiki.ti.com/index.php/IPC_3.x
  Users Guide - http://processors.wiki.ti.com/index.php/IPC_Users_Guide
  Migration - http://processors.wiki.ti.com/index.php/IPC_3.x_Migration_Guide
Development Repo/products:
  Development Repository - http://git.ti.com/cgit/cgit.cgi/ipc/ipcdev.git/
  Development Flow - http://git.ti.com/ipc/pages/Home
Product download
  http://software-dl.ti.com/dsps/dsps_public_sw/sdo_sb/targetcontent/ipc/index.html

## Slide 110: Thank You!

## Slide 111: AMMU Configuration
On Vayu, when the IPU needs to access the EVE’s mailboxes, the mailbox physical address overlaps the ARM memory map bit-banded region. To avoid this problem, we use a virtual address for the EVE mailboxes and program the AMMU to map the virtual address to the physical address.
  /* map L3/L4 peripherals (mailbox, spinlock) into ammu (non-cacheable) */ var entry = AMMU.largePages[3]; entry.pageEnabled = AMMU.Enable_YES; entry.translationEnabled = AMMU.Enable_YES; entry.logicalAddress = 0x60000000; entry.translatedAddress = 0x40000000; entry.size = AMMU.Large_512M; entry.L1_cacheable = AMMU.CachePolicy_NON_CACHEABLE; entry.volatileQualifier = AMMU.Volatile_FOLLOW; entry.executeOnly = AMMU.Enable_NO; entry.readOnly = AMMU.Enable_NO; entry.prefetch = AMMU.Enable_NO; entry.exclusion = AMMU.Enable_YES; entry.L1_cacheable = AMMU.CachePolicy_NON_CACHEABLE; entry.L1_posted = AMMU.PostedPolicy_NON_POSTED; entry.L1_allocate = AMMU.AllocatePolicy_NON_ALLOCATE; entry.L1_writePolicy = AMMU.WritePolicy_WRITE_THROUGH;

## Slide 112: GateMP Configuration
As a consequence of the AMMU mapping, the base address of the hardware spin locks must be configured with a virtual address.
  var GateHWSpinlock = xdc.useModule('ti.sdo.ipc.gates.GateHWSpinlock'); GateHWSpinlock.baseAddr = 0x6A0F6800;
This does not happen automatically. The application config script must do this.

## Slide 113: IntXBar Configuration
The interrupt crossbar module is not a member of IPC. However, as a consequence of the AMMU mapping for the mailboxes (on IPU only), the module requires IPC configuration. You must configure the crossbar base address to a virtual address compatible with the AMMU mapping.
  var IntXbar = xdc.useModule('ti.sysbios.family.shared.vayu.IntXbar'); IntXbar.mmrBaseAddr = 0x6A002000;