## Slide 1: Getting Started With the Stellaris® EK-LM4F120XL LaunchPad Workshop
Version 1.10
Notes: This workshop has been constructed to be extensively hands-on, and the overwhelming majority of your time will be spent working with the tools and writing code. If you don't already have some experience with embedded microcontrollers and using the C programming language, you need to acquire that experience before proceeding. There are many resources online that you can use to obtain that knowledge.
In case you didn't know it already, this workshop is available at http://www.ti.com/stellarislaunchpadworkshop. That wiki site has links to all of the material you'll need to run this workshop.

## Slide 2: Agenda
Portfolio ...
Introduction to ARM® Cortex™-M4F and Peripherals
Code Composer Studio
Introduction to StellarisWare, Initialization and GPIO
Interrupts and the Timers
ADC12
Hibernation Module
USB
Memory
Floating-Point
BoosterPacks and grLib
Synchronous Serial Interface
UART
µDMA
Notes: Chapter one is an introduction to TI's Stellaris LM4F series microcontroller and its peripherals and tools. In this chapter, you'll take a look at the Stellaris roadmap and the wider TI embedded processor portfolio. You'll also examine the architecture and features of the device and the design of the LaunchPad board.

## Slide 3: TI Embedded Processing Portfolio
Roadmap ...
Notes: TI has an extensive embedded processing portfolio, from the low end with our 16-bit, ultralow power microcontrollers like the MSP430, all the way up to multicore DSPs like the C6000 and our ultralow power DSPs like the C5000. In the middle, we have our 32-bit, real-time microcontrollers, like the C2000, the Delfino, Concerto, and Piccolo, which are very capable at motor control, digital power, lighting, renewable energy. I'll skip the Stellaris for a moment.
Our Hercules devices are 32-bit, ARM, safety-directed microcontrollers containing M3s and cortex R4Fs. Those are primarily used in safety, transportation, industrial, and medical where two cores run in lockstep on the single pice of silicon.
Next up is our 32-bit, ARM microprocessors, like the Sitara A8 and A9 series. These are for high-end industrial automation, portable data terminals, places where you would be likely to see high-end operating systems.
Then we get to our very, very high-performance devices, like the C6000, the Integra, DaVinci, and our C6000 parts up to ten gigahertz multicore devices with fixed and floating point end accelerators. These are for video, voice, telecom, medical, base station, lots of amazing thing.
You'll notice that in the middle of the chart here are all of our ARM microcontrollers. TI is one of the largest suppliers of ARM microcontrollers in the world. What we'll be dealing with today is the Stellaris ARM cortex M4Fs. Cortex M4 is a specification by ARM. The F is a floating point unit that is added to the device. In the cortex M4 specification, that's optional, but all of TI's M4 devices are M4Fs. All of them contain the floating point device.
Our parts are currently up to 80 megahertz. Our flash goes to 512 kilobytes. We have peripherals like USB, Ethernet on many of these. It's the Ethernet mac and fi, CAN ports, ADCs, PWMs, spy ports, and lots of other serial connectivity. These are being used in motion control, human interface, industrial automation, smart grid, robotics, an amazing number of places. A buck to eight bucks.

## Slide 4: Stellaris® Roadmap
Series ...
Fixed Point ENET MAC & PHY USB & CAN options
ARM Cortex-M3
Fixed Point USB H/D/OTG CAN options
LM3S2000
LM3S1000
LM3S800
Fixed Point General Purpose CAN options
ARM Cortex-M4F Floating-Point
LM4F23x
LM4F13x
RTP Feb ‘13 (TMX Now)
USB H/D/OTG + CAN
80 MHz
256K Flash / 32K SRAM
Low-power hibernate
2 x 1 Msps 12-bit ADCs
Motion control options
LM4F21x
LM4F12x
LM4F11x
RTP Feb ‘13 (TMX Now)
80 MHz
256K Flash / 32K SRAM
Low-power hibernate
2 x 1 Msps 12-bit ADCs
Up to 2 x CAN
Motion control options
TMS / RTP 2H13
Ethernet + USB + CAN
120 MHz
1MB Flash, 256KB SRAM
10/100 ENET MAC + PHY
USB H/D/OTG w/FS PHY & HS ULPI
Up to 2 x CAN
Parallel Bus Interface (EPI)
Crypto
LM4F29x
LM4F29x
TMS / RTP 2H13
USB + CAN
120 MHz
1MB Flash, 256KB SRAM
USB H/D/OTG w/FS PHY & HS ULPI
Up to 2 x CAN
Parallel Bus Interface (EPI)
Crypto
Production
Sampling
Development
LM3S9000
LM3S8000
LM3S6000
LM3S5000
LM3S3000
Notes: The Stellaris roadmap includes our legacy ARM cortex M3 devices from the LM3S800 all the way up to the LM3S9000. These are all fixed-point devices from the general-purpose devices with basically no major peripherals on them to some that contain CAN, some that contain CAN and USB host device and on-the-go ports, and some may contain versions of that, including Ethernet mac and fi on them.
Currently, in TMX or being released for sampling right now are our LM4F11X, 12X, 21X, 13X, and 23X devices. The one that we're dealing with today is the LM4F120H5QR. That was released ... that will be released to production in February 2013. 80 megahertz devices, 256 K of flash, 32 K of SRAM, low-power hibernate modes, two one mega sample per second, 12-bit ADCs, as many as two CAN ports on them, and some of the devices have motion control modules on them as well.
The LM4F13X and 23X have USB ports that have host device and on-the-go and include CAN ports on them. 80 megahertz, 256 K flash, 32 K of SRAM, low-power hibernate, two one mega sample per second, 12-bit ADCs, and motion control.
In development right now are our LM4F29X series that have USB and CAN on them, and they may also ... the parts also can have Ethernet USB and CAN with speeds to 120 megahertz, flash sizes to one megabyte, 256 K of SRAM, up to two CAN ports on there. They also include a nice, wide, 32-bit parallel BUS interface, and a cryptographic module on them as well.

## Slide 5: Stellaris® LM4F120 Series MCUs
Connectivity features:
CAN, USB Device, SPI/SSI, I2C, UARTs
High-performance analog integration
Two 1 MSPS 12-bit ADCs
Analog and digital comparators
Best-in-class power consumption
As low as 370 µA/MHz
500µs wakeup from low-power modes
RTC currents as low as 1.7µA
Solid roadmap
Higher speeds
Larger memory
Ultra-low power
Core and FPU ...
Notes: The Stellaris LM4F120 series microcontrollers have a wide range of peripherals and capabilities. If we take a look at the diagram on the left-hand side, we can see the ARM cortex M4F core, which sports JTAG access for testability, as well as serial wire debug for testability.
We have the NVIC, Nested Vectored Interrupt Controller. We have the memory protection unit. We have the floating point unit, and we have the embedded trace macrocell for extended testing on the device. For memory, we have 256K of flash, 32K of SRAM. We have an onboard ROM. I'll talk about the contents in a moment. And 2K of double E PROM.
On the analog side, we have a LDO voltage regulator for regulating the CPU voltage on the device, a series of analog comparators. We have two, 12-bit ACDs. That's up to 24 channels through 12 shared inputs, one mega sample A to D conversion, and a temperature sensor onboard.
On the left bottom side there, we have a series of serial interfaces. Depending on how you decide to use the IO on the device, you could have as many as eight UARTs, four SSI spy ports, a USB device port, a CAN port, or as many as six I-squared C ports. For the system control, we have the normal, very flexible clock system, preset, and system control. We also have a systick timer on board. That timer is many times used as a real-time operating system heartbeat timer, although you can use it as a regular timer resource on the device.
We have 12 general-purpose timers capable of PWM and capture and compare. There are six each 32-bit or two 16-bit. The other six are 64-bit or two 32-bit. We also have two watchdog timers, each of them driven by a separate clock domain for safety. GPIOs. We have ... I'll talk more about GPIOs in a moment. 32 channels of DMA, a precision oscillator onboard, and a battery-backed hibernate module that offers real-time clock, as well as battery-backed SRAM.
So, we offer best-in-class power consumption as low as 370 microamps per megahertz, 500 microseconds wake-up from low power modes, and realtime clock currents as low as 1.7 microamps. It's a solid roadmap to higher speeds, larger memory, and ultralow power.

## Slide 6: M4 Core and Floating-Point Unit
32-bit ARM® Cortex™-M4 core
Thumb2 16/32-bit code: 26% less memory & 25 % faster than pure 32-bit
System clock frequency up to 80 MHz
100 DMIPS @ 80MHz
Flexible clocking system
  Internal precision oscillator
  External main oscillator with PLL support
  Internal low frequency oscillator
  Real-time-clock through Hibernation module
Saturated math for signal processing
Atomic bit manipulation. Read-Modify-Write using bit-banding
Single Cycle multiply and hardware divider
Unaligned data access for more efficient memory usage
Privileged and unprivileged modes
  Limits access to MPU registers, SysTick, NVIC & possibly memory/peripherals
IEEE754 compliant single-precision floating-point unit
JTW and Serial Wire Debug debugger access
  ETM available through Keil and IAR emulators
Memory ...
Notes: Stellaris LM4F devices have a 32-bit ARM cortex M4 core inside them. The M4 core runs the thumb to instruction set. That instruction set is a combination of 16 and 32-bit code. Combining those offers ... or allows you to use 26 percent less memory and is 25 percent faster than pure 32-bit code.
The system clock frequency on these devices is up to 80 megahertz. At 80 megahertz, we offer 100 dhrystone MIPS. The device has very flexible clocking system onboard, an internal precision oscillator, an external main oscillator that can drive a phase lock loop, an internal low-frequency oscillator, and a realtime clock through the hibernation module. The instruction set and hardware offer saturated math for signal processing. We have atomic bit manipulation or read-modify-write capability using bit banding.
We have a single-cycle multiply and hardware divider onboard. Data access here is unaligned for more efficient memory usage. We have both privileged and unprivileged modes. The unprivileged mode limits access to the MP registers, the cystic, the nested vectored interrupt controller, and possibly some of the memory and peripheral, primarily to promote safety in terms of thread access and sometimes RTOSs, Realtime Operation Systems, require that.

## Slide 7: LM4F120H5QR Memory
256KB Flash memory
  Single-cycle to 40MHz
  Pre-fetch buffer and speculative branch improves performance above 40 MHz
32KB single-cycle SRAM with bit-banding
Internal ROM loaded with StellarisWare software
  Stellaris Peripheral Driver Library
  Stellaris Boot Loader
  Advanced Encryption Standard (AES) cryptography tables
  Cyclic Redundancy Check (CRC) error detection functionality
2KB EEPROM (fast, saves board space)
  Wear-leveled 500K program/erase cycles
  10 year data retention
  4 clock cycle read time
Peripherals ...
0x00000000 Flash
0x01000000 ROM
0x20000000 SRAM
0x22000000 Bit-banded SRAM
0x40000000 Peripherals & EEPROM
0x42000000 Bit-banded Peripherals
0xE0000000 Instrumentation, ETM, etc.
Notes: Stellaris LM4F devices have a 32-bit ARM cortex M4 core inside them. The M4 core runs the thumb to instruction set. That instruction set is a combination of 16 and 32-bit code. Combining those offers ... or allows you to use 26 percent less memory and is 25 percent faster than pure 32-bit code.
The system clock frequency on these devices is up to 80 megahertz. At 80 megahertz, we offer 100 dhrystone MIPS. The device has very flexible clocking system onboard, an internal precision oscillator, an external main oscillator that can drive a phase lock loop, an internal low-frequency oscillator, and a realtime clock through the hibernation module. The instruction set and hardware offer saturated math for signal processing. We have atomic bit manipulation or read-modify-write capability using bit banding.
We have a single-cycle multiply and hardware divider onboard. Data access here is unaligned for more efficient memory usage. We have both privileged and unprivileged modes. The privileged mode can limit ... or excuse me. The unprivileged mode limits the access to the MP registers, the cystic, the nested vectored interrupt controller, and possibly some of the memory and peripheral, primarily to promote safety in terms of thread access and sometimes RTOSs, Real Time Operating Systems, require that.
An IEEE 754 compliant, single-precision floating point unit is on all TI M4F devices. We also have JTAG and serial wired debugger access to the Stellaris microcontrollers. The embedded trace macro is currently accessible through the Keil and IAR emulators.

## Slide 8: LM4F120H5QR Peripherals
Battery-backed Hibernation Module
  Internal and external power control (through external voltage regulator)
  Separate real-time clock (RTC) and power source
  VDD3ON mode retains GPIO states and settings
  Wake on RTC or Wake pin
  16 32-bit words of battery backed memory
  5 µA Hibernate current with GPIO retention. 1.7 µA without
Serial Connectivity
  USB 2.0 (Device)
  8-UART
  4-I2C
  4-SSI/SPI
  CAN
More ...
Notes: To continue the peripherals, we have a battery-backed hibernation module, which offers internal and external power control through an external voltage regulator, a separate realtime clock and power source. The VDD3 on mode can retain the GPIO states and its settings when we go into hibernation. We can wake on the realtime clock, or we can wake on a pin.
There are 16 32-bit words of battery-backed memory for saving the processor state during hibernation. We have a five microamp hibernate current with GPIO retention, 1.7 microamps without. That's very, very low.
Serial connectivity on these parts, we have a USB 2.0 device port, as many as eight UARTs, depending on what you use the pins for, four I-squared C, four SSI spy ports, and a CAN port.

## Slide 9: LM4F120H5QR Peripherals
Two 1MSPS 12-bit SAR ADCs
  Twelve shared inputs
  Single ended and differential measurement
  Internal temperature sensor
  4 programmable sample sequencers
  Flexible trigger control: SW, Timers, Analog comparators, GPIO
  VDDA/GNDA voltage reference
  Optional hardware averaging
  2 analog and 16 digital comparators
  µDMA enabled
0 - 43 GPIO
  Any GPIO can be an external edge or level triggered interrupt
  Can initiate an ADC sample sequence or µDMA transfer directly
  Toggle rate up to the CPU clock speed on the Advanced High-Performance Bus
  5-V-tolerant in input configuration
  Programmable Drive Strength (2, 4, 8 mA or 8 mA with slew rate control)
  Programmable weak pull-up, pull-down, and open drain
More ...
New Pin Mux GUI Tool: www.ti.com/StellarisPinMuxUtility
Notes: Looking at some more of the peripherals, there are two one-mega sample per second, 12-bit successive approximation ADD converters. The two parts share 12 shared inputs. Any of those inputs can be single-ended or differential. There's an internal temperature sensor. Four programmable sample sequencers that we'll talk about later. Very flexible trigger control. You can trigger it with the processor through the software, with a timer, with an analog comparator, or directly from a GPIO pin.
The voltage reference on this device, since it's cost-reduced and we don't have as many pins to put an external reference, we're using the analog voltage and ground. There's optional hardware averaging. We have 2 analog comparators per device and 16 total digital comparators in the ADCs, and they're DMA enable.
On the GPIO side, depending on how you deal with the muxing of the pins, if you're using them for other purposes, you can have anywhere between none and 43 GPIO. Any GPIO can be configured edge or level-triggered to interrupt. You can initiate an ADC sample or a DMA transfer directly from a GPIO pin. The toggle rate can be as high as the CPU clock speed on the advanced high-performance BUS ports. On a standard port, it's half the CPU clock speed.
The inputs are five-volt tolerant. You can have a programmable drive strength of two, four, or eight milliamps. In the eight milliamp setting, you also get slew rate control, and there's a programmable pull-up, pull-down, and open-drain for every pin.

## Slide 10: LM4F120H5QR Peripherals
Memory Protection Unit (MPU)
  Generates a Memory Management Fault on incorrect access to region
Timers
  2 Watchdog timers with separate clocks
  SysTick timer. 24-bit high speed RTOS and other timer
  Six 32-bit and Six 64-bit general purpose timers
  PWM and CCP modes
  Daisy chaining
  User enabled stalling on CPU Halt flag from debugger for all timers
32 channel µDMA
  Basic, Ping-pong and scatter-gather modes
  Two priority levels
  8,16 and 32-bit data sizes
  Interrupt enabled
Nested-Vectored Interrupt Controller
  7 exceptions and 65 interrupts with 8 programmable priority levels
  Tail-chaining
  Deterministic: always 12 cycles or 6 with tail-chaining
  Automatic system save and restore
Board...
Notes: Finishing out the peripherals, we have a memory protection unit that generates a memory management fault on incorrect access to regions that you've configured. We have a series of timers, two watchdog timers with separate clocks and user-enabled stalling. Systic timer, it's a 24-bit, high-speed timer that's generally used for RTOSs, but it's also available as a general-purpose timing resource.
There are 6 32-bit and 6 64-bit, general-purpose timers. All of those timers can be split in half, and they all have PWM and capture and compare modes. They can also be daisy chained or combined together to generate longer periods, and all the timers listed there have user-enabled stalling. When you halt the processor in the debugger, you can halt these timers as well.
The micro DMA is a 32-channel DMA that offers basic ping-pong and scatter-gather modes. They have two priority levels on the transfers, and they can be 8, 16, or 32 bits in size. The DMA can also generate interrupts when it finishes the transfer.
We have a nested vectored interrupt controller on the device. We offer seven system level exceptions and 65 interrupts with eight programmable priority levels. So, your vector table is not set in stone. You can go in and reprogram the priority levels if you choose. We also offer a very interesting feature called tail chaining that we'll describe later. It's deterministic. It's always 12 cycles for an interrupt or 6 with tail chaining. And we have automatic system save and restore.

## Slide 11: Stellaris® LaunchPad
ARM® Cortex™-M4F 64-pin 80MHz LM4F120H5QR
On-board USB ICDI (In-Circuit Debug Interface)
Micro AB USB Device port
Device/ICDI power switch
BoosterPack XL pinout also supports existing BoosterPacks
2 user pushbuttons
Reset button
3 user LEDs (1 tri-color device)
Current measurement test points
16MHz Main Oscillator crystal
32kHz Real Time Clock crystal
3.3V regulator
Support for multiple IDEs:
Lab...
Notes: The Stellaris LaunchPad board has some impressive features for a small price. The onboard processor, there in the middle of the board, is a Texas Instruments Stellaris LM4F120H5QR microcontroller. It's a version of the ARM cortex M4F family with 64 pins and has a top speed of 80 megahertz. The LaunchPad has two USB ports, one at the top for emulation and one of the left side as a device mode user port. The board can be powered through either port using the power switch in the upper left.
There are two user push buttons at the bottom of the board. The one on the right is also connected to the wake pin on the microcontroller that will wake it from hibernation mode. A reset button is provided in the emulator area of the board in the upper right.
Just below the reset button is a tricolor LED that combines the red, green, and blue LEDs into a single package. To the right of the device USB port are two test points where you could measure the current draw of the microcontroller. They are currently connected by a jumper.
There are two crystals on the board, a 16-megahertz one that drives the main oscillator and a 32,768-hertz one that drives the realtime clock oscillator. Since many computer USB ports can deviate significantly from 3.3 volts, an onboard voltage regulator is provided.
Expandability is an important aspect of all TI's LaunchPad boards. The Stellaris LaunchPad features the booster pack XL pin out, which offers additional signals while still supporting existing booster packs.
All Stellaris devices offer support for multiple integrated development environments or IDEs. Mentor graphics, mentor-embedded, source recode bench, IAR systems embedded workbench, ARM, Keil Microvision IDE, and Texas Instruments Code Composer Student are all supported. Code Composer Studio, or CCS, will be our tool of choice in this video.

## Slide 12: Lab 1: Hardware and Software Setup
Install the software
Review the kit contents
Connect the hardware
Test the QuickStart application
USB Emulation Connection
Agenda ...
Notes: In lab one, you'll obtain and install all the needed hardware and software, as well as test out the pre-installed application software on the LaunchPad board.

## Slide 13: Agenda
IDEs...
Introduction to ARM® Cortex™-M4F and Peripherals
Code Composer Studio
Introduction to StellarisWare, Initialization and GPIO
Interrupts and the Timers
ADC12
Hibernation Module
USB
Memory
Floating-Point
BoosterPacks and grLib
Synchronous Serial Interface
UART
µDMA
Notes: Chapter two is an introduction to Code Composer Studio Version 5.2. Code Composer Studio is an Integrated Development Environment, or IDE, that combines the editing, debugging, and analysis tools into a single package. It's based on the Eclipse open source development tool. Before you can write code for the Stellaris LM4F, you need to get acquainted with the tool you'll be using. Stellaris devices are also supported by mentor graphics, mentor-embedded IDE, IAR systems embedded workbench, and ARMS Keil Microvision IDE.

## Slide 14: Development Tools for Stellaris MCUs
Eval Kit License | 30-day full function. Upgradeable | 32KB code size limited. Upgradeable | 32KB code size limited. Upgradeable | Full function. Onboard emulation limited
Compiler | GNU C/C++ | IAR C/C++ | RealView C/C++ | TI C/C++
Debugger / IDE | gdb / Eclipse | C-SPY / Embedded Workbench | µVision | CCS/Eclipse-based suite
Full Upgrade | 99 USD personal edition / 2800 USD full support | 2700 USD | MDK-Basic (256 KB) = €2000 (2895 USD) | 445 USD
JTAG Debugger |  | J-Link, 299 USD | U-Link, 199 USD | XDS100, 79 USD
What is CCS?...
Notes: 14
14
14
Stellaris microcontrollers are supported by four different integrated development environments: Mentor graphics Mentor-Embedded tools, IAR systems Embedded Workbench tools, the ARM Keil Microvision tool, and Texas Instruments Code Composer Studio tool. You can see the eval kit licenses there. Some of them offer 30-day full function. Some of them are code-size limited.
The Code Composer Studio version is full function, but it's onboard emulation limited. If you use and connect the LaunchPad board to your computer, you have full function capability of Code Composer Studio. Only if you go off to use a target board do you need to actually buy the tool.
For the compilers, you can see that some companies use the GNU tool. Some of them use their own tool. TI has their own C C-plus-plus compiler, although C-plus-plus is not supported on embedded microcontrollers because of the large sizes that it can generate.
For the debugger IDE, two of the tools offer Eclipse base support. Eclipse is the open source workbench tool that's been out there for quite some time. Full upgrade on these devices or rather on these tools for the mentor-embedded tool. 99 bucks for the personal addition, 2,800 if you want full support. For the IAR systems tool, about 2,700 dollars. For ARM Keil, about 2,900 dollars.
Code Composer Studio, the pricing is 445 dollars for the downloadable version. If you want the CD, it's 495 dollars. Most of the companies offer JTAG debuggers, and there are also third-party debuggers out there. IAR systems offer a J-link for about 300 bucks. ARM Keil for about 200 bucks. And Texas Instruments has the XDS100, an entry level tool, for about 80 bucks. We also offer the 200 and the 500 versions ... they have additional capabilities at an additional cost.

## Slide 15: What is Code Composer Studio?
Integrated development environment for TI embedded processors
  Includes debugger, compiler, editor, simulator, OS…
  The IDE is built on the Eclipse open source software framework
  Extended by TI to support device capabilities
CCSv5 is based on “off the shelf” Eclipse (version 3.7 in CCS 5.2)
  Uses unmodified version of Eclipse
    TI contributes changes directly to the open source community
  Drop in Eclipse plug-ins from other vendors or take TI tools and drop them into an existing Eclipse environment
  Users can take advantage of all the latest improvements in Eclipse
Integrate additional tools
  OS application development tools (Linux, Android, Sys/BIOS…)
  Code analysis, source control…
Runs under Windows and Linux
$445 single seat. $99/year subscription fee
User Interface Modes...
Notes: So, what is Code Composer Studio? Code Composer Studio is an Integrated Development Environment, or IDE, for all of TI's embedded processors. That includes the debugger, the compiler, the editor, the simulator, any OS support that you require. The IDE is built on the Eclipse open source software framework, and it's been extended by Texas Instruments to support additional device capabilities.
Code Composer Studio Version 5 is based on off-the-shelf Eclipse. It's Version 3.7 and Code Composer Studio Version 5.2. It's an unmodified version of Eclipse, and we contribute our changes directly to the open source community rather than just building it into our tool.
So, you can drop in Eclipse plug-ins from other vendors, or you can take TI tools and drop them into an existing Eclipse environment if you want to. So, you, the user, can take advantage of all the latest improvements in the Eclipse tool.
Of course, you can integrate additional tools. OS level application development, like for Linux, android, TI SYS/BIOS. Also, code analysis, third-party code analysis, source control. Those are all offered. Code Composer Studio runs under Windows, and it runs under Linux. 445 dollars for a single seat. It's a 99-dollar-a-year subscription fee for maintenance.

## Slide 16: User Interface Modes
Simple Mode
  By default CCS will open in simple/basic mode
  Simplified user interface with far fewer menu items, toolbar buttons
  TI supplied CCS Edit and CCS Debug Perspectives
Advanced Mode
  Uses default Eclipse perspectives (similar to what existed in CCSv4)
  Recommended for users integrating other Eclipse based tools into CCS
Switching Modes
  On the CCS menu bar, select Window  Open Perspective  Other… Check the “Show all” checkbox “C/C++” and “Debug” are the advanced perspectives
Common Tasks...
Notes: Code Composer Studio has two user interface modes. First, is a simple mode. By default, CCS opens up in a simple, basic mode. It's a simplified user interface to the standard Eclipse perspective with far fewer menu items and toolbar buttons. TI supplies these perspectives called CCS edit and CCS debug to the tool.
If you want to, you can switch back to the advance mode. That use the default Eclipse perspective, which is similar to what existed earlier in Code Composer Studio Version 4. If you are integrating other Eclipse-based tools into Code Composer Studio, that's the recommended way to go.
If you want to switch modes, on the Code Composer menu bar, select Window, open perspective, other, check the show-all checkbox, as you can see in the open perspective dialog down below. The C/C++ and the Debug that you see there, those are the advanced perspectives.

## Slide 17: Common Tasks
Creating New Projects
  Very simple to create a new project for a device using a template
Build options
  Simplified build options dialog from earlier CCS versions
  Updates to options are delivered via compiler releases and not dependent on CCS updates
Sharing projects
  Easy for users to share projects, including working with version control (portable projects)
  Setting up linked resources has been simplified from earlier CCS versions
Workspaces and Projects...
Notes: Some common tasks that you might perform would be creating a new project. It's very simple to create a new project for the device using templates. Build options. We have simplified build options dialog from earlier Code Composer versions that basically exposed thousands of different options. Those options are still available, but they're in sub-menus, which makes this much easier to walk through the first time. Updates to those options are delivered with compiler releases, and their not dependent upon installing an entirely new version of Code Composer.
If you want to share projects, it's easier for users to share projects, including working with version control and making sure that you have a portable project. You can set up link sources. Doing this has been very much simplified from earlier Code Composer versions.

## Slide 18: Workspaces and Projects
Project
Source files
Header Files
Library files
Build and
Project
Source files
Header Files
Library files
Build and tool se
Workspace
Project 1
Project 2
Project 3
Settings and preferences
A workspace contains your settings and preferences, as well as links to your projects. Deleting projects from the workspace deletes the links, not the files*
Project
Source files
Header files
Library files
Build and tool settings
A project contains your build and tool settings, as well as links to your input files. Deleting files from the workspace deletes the links, not the files*
Source files
Code and Data
Header files
Declarations/Defines
Library files
Code and Data
Link
Link
Link
Link
* Unless you have located or copied files into the workspace
Project Wizard...
Notes: The Eclipse idea of workspaces and projects can be a little odd at first. Workspaces contain your settings and preferences for the way that Eclipse looks, as well as links to your projects. When you go in and you delete a project from the workspace, that deletes the links, not the files. Now, this is unless you have located or copied your files into the workspace, which is possible. In most cases, you just link your project into the workspace and preserve your project.
As you can see, you can have multiple projects in the workspace. You can make your settings and preferences and save those and export those.
Your projects, when you work with a project, a project contains your build and your tool settings, as well as the links to your input files. Deleting files from the workspace deletes the links, not the files. Again, unless you've located or copied files into the workspace.
You can see on the far right, there are source files, our code and data, our header files with our declarations and defines, and any of our library files, which has code and data in them as well. The best practice way to do this is to link all of those into your project and then to link it into the workspace so that your original code is preserved for you, and when you delete any of these things, you don't actually delete the hard work code that you've achieved.

## Slide 19: Project Wizard
Single page wizard for majority of users
  Next button will show up if a template requires additional settings
Debugger setup included
  User chooses location, device and connection
  A modifiable ccxml file is created
Simple by default
  Compiler version, endianness… are under advanced settings
Add Files...
Notes: New projects are created through the project wizard. You can see the new project dialog on the left-hand side. So, it's a single page wizard for the majority of users. If you were to get to the bottom of this and rather than click the finish button you click the next button, it would show up if you have a template that requires additional settings. In this case, this one does not. The debugger setup is all included. You choose the location, the device, and the connection for this. This will create a modifiable CCXML file in your project.
The idea is that this is simple by default. The Compiler version, the endienness in this, all these other advance settings are all in the advance settings area and not exposed right here. So, you can see the project type at the top is, in this case, lab three. It's an executable project type. I've located it in this location. The family is ARM. The variant is the 120. That's the version that we're working with now. When you're in the labs, you just type into this variant space, and it will bring up your part out of a long list of Stellaris devices.
We've picked the LM4F120H5QR over there on the right. The connection type, if we're using the LaunchPad or any of the other Stellaris boards, it's Stellaris in-circuit debug interface. And you can see under the projects that we can pick empty project that has absolutely nothing in it, an empty project with a main.c already dropped in, assembly only, DSP bios, which is TI's realtime operating system, another type of project. You can also use some basic examples to start from if you like. So, this creates the project for you, drops it in, and all you have to do is get started editing main.c.

## Slide 20: Adding Files to Projects
Add Files to Project allows users to control how the file is added to the project
Linking Files using built-in macros allows easy creation of portable projects
Lab...
Notes: Once you've created a project, you'll probably want to add some additional files to the project. Here, I've picked Add Files to Project. I can select multiple files, if I like, rather than just one at a time. In this case, these files are going to support my activities in my project.
What is it that I want to do? Do I want to copy these files into my workspace? Or do I want to use these in multiple projects and just link them into my project as shown in the bottom window here?
In this case, I'm going to link to the files. Well, how do you want to link to them? Is this relative to where your project is located? Is it relative to where your tools are located? You can pick right out of here. So, the add files to project allows you to control how the file is added to the project. This is something you've probably never thought of in your integrated development environments that you've worked on in the past, but it's extremely important to know where those files are. Linking the files using the built-in macros allows you to easily create portable projects.

## Slide 21: Lab 2: Code Composer Studio
Create a new project
Experiment with some CCS features
Use the LM Flash Programmer
Agenda ...
USB Emulation Connection
Notes: In lab two, you'll start using Code Composer Studio. Don't get bogged down trying to understand the code. You'll get to that in the next lab. Here, just concentrate on the tool itself.

## Slide 22: Agenda
StellarisWare...
Introduction to ARM® Cortex™-M4F and Peripherals
Code Composer Studio
Introduction to StellarisWare, Initialization and GPIO
Interrupts and the Timers
ADC12
Hibernation Module
USB
Memory
Floating-Point
BoosterPacks and grLib
Synchronous Serial Interface
UART
µDMA
Notes: When you first start working with an evaluation board, like the Stellaris LaunchPad, you first want to do something simple, like making the LED blink. That implies you understand how to use the development tool, how to initialize the LM4F device and its clocks, and how to send data to the input/output pins. Chapter three and its lab will wrap all that together.

## Slide 23
Peripheral Driver Library
Graphics Library
USB Library
Ethernet stacks
In-System Programming
License-free and Royalty-free source code for TI Cortex-M devices:
Features...
StellarisWare®
Notes: 23
23
StellarisWare is a license-free and royalty-free source code and library for TI cortex M devices. It offers and includes the peripheral driver library, the graphics library, USB library, Ethernet stacks, and in-system programming. To look at little closer at the StellarisWare features, the peripheral driver library is a high-level, API interface to the complete peripheral set. It's license and royalty-free for use with TI's cortex M parts. It's available as object library and as source code, and as source code, it can also act to some pretty nice examples for you to write your own code from. This is programmed in the on chip ROM of all LM4F devices.
23

## Slide 24
Peripheral Driver Library
High-level API interface to complete peripheral set
License & royalty free use for TI Cortex-M parts
Available as object library and as source code
Programmed in the on-chip ROM
StellarisWare Features
Graphics Library
Graphics primitive and widgets
153 fonts plus Asian and Cyrillic
Graphics utility tools
USB Stacks and Examples
USB Device and Embedded Host compliant
Device, Host, OTG and Windows-side examples
Free VID/PID sharing program
Ethernet
lwip and uip stacks with 1588 PTP modifications
Extensive examples
Extras
SimpliciTI wireless protocol
IQ math examples
Bootloaders
Windows side applications
ISP...
Notes: 24
24
24
StellarisWare is a license-free and royalty-free source code and library for TI cortex M devices. It offers and includes the peripheral driver library, the graphics library, USB library, Ethernet stacks, and in-system programming. To look at little closer at the StellarisWare features, the peripheral driver library is a high-level, API interface to the complete peripheral set. It's license and royalty-free for use with TI's cortex M parts. It's available as object library and as source code, and as source code, it can also act to some pretty nice examples for you to write your own code from. This is programmed in the on chip ROM of all LM4F devices.
StellarisWare also includes the graphics library. That's graphics primitives for drawing shapes, text, images on the screen and widgets to tie touch-screen buttons to in-program actions. We have 153 fonts plus Asian and Cyrillic and a series of graphics utility tools for converting files and making buttons and some very interesting stuff that we'll go over later on.
We have USB stacks and examples. The device and its stack are USB device and embedded host compliant. We have device, host, on-the-go, and Windows side examples available. TI also has a free vid-pid (phonetic sp.) sharing program that I'll talk about later that can save you as much as 2,000 dollars.
Ethernet. We have lightweight IP and micro IP open source stacks with the 1588 precision time protocol modifications made to it and extensive examples on that. Some other extras. We have the simplicity wireless protocol available, IQ math examples, boot loaders, like I mentioned earlier, additional Windows side examples for you.

## Slide 25
In System Programming Options
Stellaris Serial Flash Loader
Small piece of code that allows programming of the flash without the need for a debugger interface.
All Stellaris MCUs ship with this pre-loaded in flash
UART or SSI interface option
The LM Flash Programmer interfaces with the serial flash loader
See application note SPMA029
Stellaris Boot Loader
Preloaded in ROM or can be programmed at the beginning of flash to act as an application loader
Can also be used as an update mechanism for an application running on a Stellaris microcontroller.
Interface via UART (default), I2C, SSI, Ethernet, USB (DFU H/D)
Included in the Stellaris Peripheral Driver Library with full applications examples
Fundamental Clocks...
Notes: 25
25
25
There are two in-system programming options for you provided through StellarisWare. The Stellaris serial flash loader is a small piece of code that allows programming of the flash without the need for a debugger interface without using Code Composer Studio. All Stellaris microcontrollers ship with this code preloaded in the flash. It uses the UART or SSI option. This is meant to be a production-level, low-cost way of programming the part.
The LM flash programmer interfaces with the serial flash loader, and the application node is there in SPMA029. The main idea with this is that when the new code is programmed into your flash, this piece of code that's sitting in flash will be wiped out. That's the way that you want it to happen. If you want to restore it, you can go into the programming examples in StellarisWare and restore it if you need to.
The Stellaris boot loader is preloaded in ROM, or it can be programmed at the beginning of flash to act as an application loader if you like. You can also use it as an update mechanism for an application running on a Stellaris microcontroller, a thing that's called paging.
You can interface to this by a UART, which is the default, through I-squared C, through SSI. On those parts that have Ethernet, you can attach to it through that. For USB, we can also do device firmware update as host and device on those devices that have host. The LM4F120 only has device. This is included in the Stellaris peripheral driver library with full applications examples.

## Slide 26: Fundamental Clock Sources
Precision Internal Oscillator (PIOSC)
  16 MHz ± 3%
Main Oscillator (MOSC) using…
  An external single-ended clock source
  An external crystal
Internal 30 kHz Oscillator
  30 kHz ± 50%
  Intended for use during Deep-Sleep power-saving modes
Hibernation Module Clock Source
  32,768Hz crystal
  Intended to provide the system with a real-time clock source
SysClk Sources...
Notes: There are four fundamental clock sources on the Stellaris devices. What do you want from a clock on your part? You would like them to be cheap. You would like them to be accurate. You'd like them to be easy. You don't get to pick all of those for every one of the oscillators on any part. So, what we offer you is a precision internal oscillator, which is a 16-megahertz oscillator, plus or minus three percent. You do not have to include any crystal or clock source on the outside of the device.
We have a main oscillator that uses an external, single-ended clock source, or it can use an external crystal. We have an internal, 30-kilohertz oscillator. This is a 30 kilohertz, plus or minus 50 percent oscillator. This is intended for use during deep sleep, power-savings modes when you really don't care what the ... exactly how fast the processor is running. All you want to do is kick it over and maybe poll for some activity.
We also have the hibernation module clock source, which runs off the 32768 hertz crystal. That's intended to provide the system with a realtime clock source.

## Slide 27: System (CPU) Clock Sources
The CPU can be driven by any of the fundamental clocks …
Internal 16 MHz
Main
Internal 30 kHz
External Real-Time
- Plus -
The internal PLL (400 MHz)
The internal 16MHz oscillator divided by four (4MHz ± 3%)
Clock Source | Drive PLL? | Used as SysClk?
Internal 16MHz | Yes | Yes
Internal 16Mhz/4 | No | Yes
Main Oscillator | Yes | Yes
Internal 30 kHz | No | Yes
Hibernation Module | No | Yes
PLL | - | Yes
Clock Tree...
Notes: The system clock, or the CPU clock, can be driven by any of the fundamental clocks. The internal, 16-megahertz, the main oscillator, the internal 30-kilohertz oscillator, and the external realtime oscillator. Plus, we have an internal phase lock loop that runs at 400 megahertz. No, you can't run the CPU at 400 megahertz. The dividers on there limit you to 80 megahertz and below. We also have the internal 16-megahertz oscillator divided by four, so that would be four megahertz plus or minus three percent.
You have one, two, three, four, five, six different clock sources that can drive the CPU. The internal 16 megahertz that can also drive the PLL, the internal 16 megahertz divided by four, the main oscillator 16 megahertz, the internal 30 kilohertz, the hibernation module, and the phase lock loop.

## Slide 28: Stellaris Clock Tree
driverLib API SysCtlClockSet() selects:
SYSDIV divider setting
OSC or PLL
Main or Internal oscillator
Crystal frequency
GPIO...
Notes: Let's take a look at the clock tree to fully understand it. This is the Stellaris clock tree. It's a very flexible implementation to provide you with all the different types of clocks that you'll need for low-power operation, for low-cost operation, for high-precision operation. Let's take a look at the system clock on the far right in the middle where it says, "System clock."
If we follow that back to the mux, it allows us to either divide by the SYSDIV or to bypass it. We also have a divider before that, and then you'll see the div (phonetic sp.) 400. That's divide by two or it bypasses there. Then you'll see the 400-megahertz PLL. That can be driven by the main oscillator or by the precision oscillator. Either one of those.
Let's say that we take a 16-megahertz crystal. There's a limitation on the part for what crystals you could use to drive the PLL. We use the main oscillator to drive the PLL. The PLL will run at 400 megahertz. There is a divide by two that divides it to 200 megahertz there for that very center mux. Our SYSDIV then will divide it further. Normally, you might divide it by let's say five. Five would give you 80 megahertz for your system clock.
How are you going to program all of those? There is a single driver-libe (phonetic sp.) API function call called sys control clock set. That sets the SYSDIV divider setting for you. It tells you whether you're running off the oscillator directly or if you're running off the PLL, whether you're running off the main or the internal oscillator, and what the crystal frequency is on the outside of the device. So, it's very easy to set up your system clock with this single API.

## Slide 29: General Purpose IO
  Any GPIO can be an interrupt:
    Edge-triggered on rising, falling or both
    Level-sensitive on high or low values
  Can directly initiate an ADC sample sequence or µDMA transfer
  Toggle rate up to the CPU clock speed on the Advanced High-Performance Bus. ½ CPU clock speed on the Standard.
  5V tolerant in input configuration
  Programmable Drive Strength (2, 4, 8mA or 8mA with slew rate control)
  Programmable weak pull-up, pull-down, and open drain
  Pin state can be retained during Hibernation mode
Masking...
New Pin Mux GUI Tool: www.ti.com/StellarisPinMuxUtility
Notes: Stellaris general-purpose IO is extremely capable. Any GPIO can be an interrupt, either edge-triggered on rising, falling, or both. It can be level-sensitive on high or low values. Any GPIO can directly initiate an ADC sample sequence or a DMA transfer. The toggle rate can be as high as the CPU clock speed on the advanced high-performance bus. Now, most of the ports on the LM4F120H5QR can be configured to be on either one of the buses, the advanced high-performance bus or the advanced performance bus.
If you're on the standard bus, the advanced-performance bus, you get half the CPU clock speed. That's what you'd generally expect where you toggle a GPIO. But you can achieve a higher rate at a slightly higher power cost on the advanced high-performance bus.
In input configuration, all of the GPIO are five-volt tolerant. You can program the drive strengths to be two, four, eight milliamps. The slew rate ... you have slew rate control for the eight-milliamp setting. You can imagine what would happen if you have 20 different GPIO all going to eight milliamps simultaneously. You really need a slew rate control on that.
The pins have programmable weak pull-up, pull-down, and open-drain modes, and the pin stabes (phonetic sp.) can be retained during hibernation mode. So, we could come right back up from hibernation, which is essentially from power up and remember what the pin states were of the device and set them.

## Slide 30: GPIO Address Masking
0
0
1
0
0
1
1
0
0
0
0
0
0
…
The register we want to change is GPIO Port D (0x4005.8000) Current contents of the register is:
0
0
0
1
1
1
0
1
Instead of writing to GPIO Port D directly, write to 0x4005.8098. Bits 9:2 (shown here) become a bit-mask for the value you write.
0
0
1
1
1
0
1
1
1
1
1
0
1
0
1
1
Only the bits marked as “1” in the bit-mask are changed.
GPIO Port D (0x4005.8000)
The value we will write is 0xEB:
Write Value (0xEB)
New value in GPIO Port D (note that only the red bits were written)
Each GPIO port has a base address. You can write an 8-bit value directly to this base address and all eight pins are modified. If you want to modify specific bits, you can use a bit-mask to indicate which bits are to be modified. This is done in hardware by mapping each GPIO port to 256 addresses. Bits 9:2 of the address bus are used as the bit mask.
GPIOPinWrite(GPIO_PORTD_BASE, GPIO_PIN_5|GPIO_PIN_2|GPIO_PIN_1, 0xEB);
Note: you specify base address, bit mask, and value to write. The GIPOPinWrite() function determines the correct address for the mask.
Lab...
Notes: GPIO address massing is a somewhat unusual application of the bit banding technique. Each GPIO port has a base address, and if you look in the diagram there, GPIO port D, that base address for that peripheral is at 40058000. So, that's the base address for that port. You can write an eight-bit value to the port directly to that base address, and all eight pins will be modified, just like you've done to port addresses since the beginning of the 6502 days, if you're that old.
If you want to modify specific bits in an older processor, you would have to read the value in the port, change the value that you want to, and write the values back out to the port, preserving the old ones. Here, you can use a bit mask to indicate which ones of the bits that you want to be modified. So, this is done in hardware by mapping each GPIO port address to 256 separate addresses. So, it's an addressing trick. Bits nine to two of the address bus are going to be used as a bit mask.
So, in this case, the register that we want to change is GPIO port D. There's it's address. The current contents of the register, and you can see it's 0011101. The value that we're going to write to it is EB. Now, if we had done this ... if we had wanted to preserve some of the values in the bits in an older style processor and we just wrote this value to the port, the port would now have EB, but that's not exactly what we want to do.
Instead of writing to the GPIO port directly, what we're going to do is we're going to use a bit mask, and we're going to specify that bit mask is shown. And you can see in the bit mask that bit ... the nine to two in the bit mask, the bottom one is a zero, and then the next one is a one and then a one, a zero, zero, and a one. Only the bits with ones in them will be changed in the final port. So, only the bits marked as ones in the bit mask get changed.
So, you can see right here that we have the one from EB matching up with the one in the bit mask writing a one, the zero in the EB matching up with the one in the bit mask and writing a zero. So, lastly, the one and the one matching a one. So, now the new value in GPIO port D, notice that only the red bits were written, so we did a read modify write as an atomic operation without having to read anything back from the port.
Down below is a specific example of that. Here, we're going to do a GPIO pin right to GPIO port D base. That's the port D base that we specified up here. We're going to write to GPIO pine five, to pine two, and to pin one. So, we will only write those values out of the data that we actually sent to it. This is an extremely powerful technique, and you're going to get to see that in detail in the lab.

## Slide 31: Lab 3: Initialization and GPIO
Configure the system clock
Enable and configure GPIO
Use a software delay to toggle an LED on the evaluation board
Agenda ...
USB Emulation Connection
Notes: Lab three is your first chance to write some real code from a blank page. If you don't understand what a StellarisWare API function call does or what a parameter means, pause the video and look it up in the user guides that you found in the first chapter of the workshop. We've provided plenty of explanation in the lab steps, but make sure you take the time to comprehend what's going on rather than skipping on to the solution. Your hard work will be rewarded.

## Slide 32: Agenda
NVIC...
Introduction to ARM® Cortex™-M4F and Peripherals
Code Composer Studio
Introduction to StellarisWare, Initialization and GPIO
Interrupts and the Timers
ADC12
Hibernation Module
USB
Memory
Floating-Point
BoosterPacks and grLib
Synchronous Serial Interface
UART
µDMA
Notes: Chapter four of the workshop is where you'll get familiar with interrupts and the timers. You'll use the timer to generate interrupts to the main routine. If you're not already familiar with the concept of microcontroller interrupts and interrupt service routines, now would be a good time to look up that topic online.

## Slide 33: Nested Vectored Interrupt Controller (NVIC)
Handles exceptions and interrupts
8 programmable priority levels, priority grouping
7 exceptions and 65 Interrupts
Automatic state saving and restoring
Automatic reading of the vector table entry
Pre-emptive/Nested Interrupts
Tail-chaining
  Deterministic: always 12 cycles or 6 with tail-chaining
t
Motor control ISRs (e.g. PWM, ADC)
Communication ISRs (e.g. CAN)
Main application (foreground)
Tail Chaining...
Notes: The LM4F Nested Vectored Interrupt Controller, or NVIC, is tightly coupled to the central processing unit. It handles all of the exceptions and interrupts that come into the CPU. There are eight programmable priority levels and priority grouping. In most interrupt vector tables, you'll see that the priority levels are already set by the manufacturer, and you have no input into what they are. That's not the case on this device. You can go in and reprogram the priorities as you like.
The device has seven system level exceptions and 65 interrupts that it handles. It also has a state machine driven automatic state saving and restoration for the state of the processor, as well as automatic reading of the vector table entry to very quickly facilitate going into interrupt service routines and back out.
One of the first rules that you learn when you're programming interrupts on a microcontroller is to not nest interrupts, and one of the first rules that you break is you nest the interrupts. You need to get to a very low latency motor control or a temperature sensor or some device. You need to get to it very quickly, and you have other interrupts that are too long. You have to do them on most microcontrollers in software. You have to go back in, reenable the interrupts you want to make preempt some other interrupt. You do that in software.
Here, you can do that in the NVIC. You can make interrupts preemptive, and you can nest them. You can also ... interrupts can also be tail-chained, which is something I'll explain in the next few slides. Interrupts are deterministic. They're always 12 cycles before they actually hit the interrupt service routine or 6 cycles if they're tail-chained.
So, taking a look at the diagram at the bottom, we can see here's a main application with a couple of interrupts going off. If you take a look from the left to the right, the first thing that goes off is motor control interrupt service routines. Something like the PWM, the ADC, something that's handling motor control. Motor control has to be extremely low latency. You can't wait. You must take them.
So, here comes along a second interrupt. This is a motor control ISR. You can see the second one occurring. That's fine. Well, here we are in the third instance here. A communication interrupt service routine like the CAN has started operation. We can't wait for the communications ISR to complete, so the motor control ISR preempts that. The interrupt interrupts the motor control interrupt, interrupts the communications ISR, and runs right in the middle of it.
At the end of that ISR, it transfers its control back to the original communication ISR. Remember, motor control ISRs cannot wait. They must be low latency. Communication ISRs, on the other hand, tend to have buffers associated with them, and they can generally wait.
In the fourth instance, another motor control ISR goes off. In the fifth instance here, a communications ISR goes off. In the next one, a motor control interrupt service routine went off, and then sometime in the middle of that, a communication ISR went off. You can see that the transfer of control went directly from interrupt service routine to interrupt service routine. That's called tail-chaining, and we're going to see more of that in just a moment.

## Slide 34: Interrupt Latency - Tail Chaining
PUSH
POP
ISR 1
POP
ISR 2
PUSH
ISR 1
POP
ISR 2
12 Cycles
IRQ1
IRQ2
Typical processor
Cortex-M4
Interrupt handling in HW
6 Cycles
12 Cycles
Highest Priority
Tail-chaining
Pre-emption …
PUSH
Notes: The first thing to look at in terms of improved interrupt latency is tail-chaining. Here in this situation, we have two interrupts that basically go off at the same time: IRQ1, which is the highest priority, and IRQ2. In a typical processor, the interrupts will go off. It would push the state of the processor, run the highest priority interrupt service routine, pop the state of the processor, see that there was another interrupt pending, push the state of the processor, run the second service routine, and then pop the state of the processor again.
Well, the pop and the push right there in the middle are doing the exact same thing in opposite directions, so there's no need to do those. The cortex M4 interrupt handling is all in hardware. So, we have a very short push at the beginning, and then we see that we run interrupt service routine one.
When the interrupt service routine is completed, the NVIC detects that there is another interrupt pending and does a six-cycle tail-chaining to then go to ... send the execution to the next interrupt service routine without having to come all the way back up to main. So, you can see a significant savings in terms of in between interrupt service routine, interrupt latency.

## Slide 35: Interrupt Latency – Pre-emption
ISR 1
ISR 2
ISR 1
POP
ISR 2
1-
12 Cycles
IRQ1
IRQ2
Cortex-M4
6 Cycles
Highest Priority
POP
12 Cycles
Typical processor
Late arrival...
PUSH
POP
POP
Notes: The next item in terms of NVIC interrupt latency is called pre-emption. Well, this isn't preemption in the typical thought. This is preemption of the pop or push process. So, you can see the diagram at the top shows the interrupt request for the highest priority interrupt going off. We service it. It's done, and then we have a second interrupt go off.
Take a look there where the typical processor is doing its thing. Interrupt service routine one is run. At the end of that, we do a pop, and then during the pop is where another interrupt goes off. The typical processor is unable to do anything about that. It continues its pop process. It then pushes the state of the processor because it detected another interrupt happening. It ran interrupt service routine two, and then it popped again. A lot of cycles being wasted.
On the Cortex M4, ISR one runs. Anytime during the pop process, if another interrupt request comes in, we can go right into a tail-chain. We can move the stack pointer back, grab interrupt service routine two, run interrupt service routine two, and then pop so that we can do as close to a tail-chain as possible and waste the least amount of cycles.

## Slide 36: Interrupt Latency – Late Arrival
ISR 2
IRQ1
IRQ2
ISR 2
ISR 1
PUSH
POP
Cortex-M4
Highest Priority
12 Cycles
6 Cycles
ISR 1
Typical processor
Interrupt handling...
PUSH
POP
PUSH
PUSH
POP
Notes: The next NVIC interrupt latency issue to look at is late arrival. In this case, we have the lower priority interrupt, IRQ2 going off before the higher priority. What we'd really like to do is we'd like the processor to transfer and handle interrupt request one before interrupt request two, if that's possible.
In a typical processor, it would be starting to push the status of the processor for IRQ2. As soon as it detected that there was a higher priority, it would finish the push, start a second push, and then go through an entire sequence where it did push, ISR1, pop, push, ISR2, and then pop. A significant amount of cycles wasted here.
The Cortex-M4, on the other hand, the NVIC will see during the push process that a second interrupt has happened. It will simply transfer the execution to ISR1 instead of ISR2 and run ISR1. At the end of the interrupt service routine, it will then tail-chain into ISR2 and then pop at the end of that. A significant savings in terms of interrupt latency.

## Slide 37: Cortex-M4® Interrupt Handling
Interrupt handling is automatic. No instruction overhead.
Entry
  Automatically pushes registers R0–R3, R12, LR, PSR, and PC onto the stack
  In parallel, ISR is pre-fetched on the instruction bus. ISR ready to start executing as soon as stack PUSH complete
Exit
  Processor state is automatically restored from the stack
  In parallel, interrupted instruction is pre-fetched ready for execution upon completion of stack POP
Exception types...
Notes: In the cortex M4 interrupt handling, it's totally automatic. There's no instruction overhead that on entry the machinery automatically pushes registers R0 through R3, R2, the LR, the PSR, and the program counter onto the stack. In parallel, the interrupt service routine, the address for it is pre-fetched onto the instruction bus. The ISR is then ready to start executing as soon as the last stack push is complete. Any further pushing of registers will be handled by the compiler.
On the exit side, the processor state is automatically restored from the stack. In parallel, the interrupted instruction, the address of it, is pre-fetched, ready for execution upon completion of the stack pop. Again, any other registers that the compiler has decided to save will have to be done by the compiler.

## Slide 38: Cortex-M4® Exception Types
Vector Number | Exception Type | Priority | Vector address | Descriptions
1 | Reset | -3 | 0x04 | Reset
2 | NMI | -2 | 0x08 | Non-Maskable Interrupt
3 | Hard Fault | -1 | 0x0C | Error during exception processing
4 | Memory Management Fault | Programmable | 0x10 | MPU violation
5 | Bus Fault | Programmable | 0x14 | Bus error (Prefetch or data abort)
6 | Usage Fault | Programmable | 0x18 | Exceptions due to program errors
7-10 | Reserved | - | 0x1C - 0x28 | 
11 | SVCall | Programmable | 0x2C | SVC instruction
12 | Debug Monitor | Programmable | 0x30 | Exception for debug
13 | Reserved | - | 0x34 | 
14 | PendSV | Programmable | 0x38 | 
15 | SysTick | Programmable | 0x3C | System Tick Timer
16 and above | Interrupts | Programmable | 0x40 | External interrupts (Peripherals)
Vector Table...
Notes: System level exception types on the cortex M4 include reset, the non-maskable interrupt, hard fault, memory management fault, bus faults, usage faults, and you can see the rest down here. You could see the priority levels of minus three, minus two, and minus one. Those are set. Those are programmed into the device and cannot be changed.
A hard fault is something that might happen as a bus fault. For example, if you fail to turn on a peripheral when you try to access it, you'll get a bus fault. If you get a memory protection unit violation, that'll happen in vector number four as a memory managed fault.
Now, all the rest of these, all the way down sys tic, pen desk v, all the rest of these are programmable. You can come in and configure these as you like. So, if you actually wanted one of your peripheral interrupts to be above a memory management fault, which is probably a mistake, you can do that. You can do that at configuration time. You can do that during run time if you choose to.
HardFault: All classes of fault, when the corresponding fault handler cannot be activated because it is currently disabled or masked by exception masking
MemManFault: Memory management fault; caused by MPU violation or invalid accesses (such as an instruction fetch from a nonexecutable region)
BusFault: Error response received from the bus system; caused by an instruction prefetch abort or data access error
UsageFault: Usage fault; typical causes are invalid instructions or invalid state transition attempts (such as trying to switch to ARM state in the Cortex-M3)
SVCall: System service call via SVC instruction

## Slide 39: Cortex-M4® Vector Table
After reset, vector table is located at address 0
Each entry contains the address of the function to be executed
The value in address 0x00 is used as starting address of the Main Stack Pointer (MSP)
Vector table can be relocated by writing to the VTABLE register (must be aligned on a 1KB boundary)
Open startup_ccs.c to see vector table coding
GPTM...
Notes: The cortex M4 vector table is shown here. After reset, the vector table is located at address zero. Each entry in the vector table contains the address of the function, the handler, the ISR, to be executed. If you look down at the bottom at the initial SP value, that value at address 00 is used as a starting address of the main stack pointer.
You can relocate the vector table if you need to. That's typically done by a boot loader by writing to the V table register. You have to align this on a 1K byte boundary. If you want to, you can open up a startup under CCS.c for editing in your lab to see the vector table coding and how that's done, but you can see this going from bottom to top for the entire vector table.

## Slide 40: General Purpose Timer Module
Six 16/32-bit and Six 32/64-bit general purpose timers
Twelve 16/32-bit and Twelve 32/64-bit capture/compare/PWM pins
Timer modes:
  One-shot
  Periodic
  Input edge count or time capture with 16-bit prescaler
  PWM generation (separated only)
  Real-Time Clock (concatenated only)
Count up or down
Simple PWM (no deadband generation)
Support for timer synchronization, daisy-chains, and stalling during debugging
May trigger ADC samples or DMA transfers
Lab...
Notes: The General Purpose Timer Module, or GPTM, has six 16 or 32-bit and six 32 or 64-bit general-purpose timers. They can be used for capture, compare, or PWM. The timer modes we have available, we have one shot. We have periodic. We can do an input edge count or a time capture. We can have a 16-bit prescaler on that if you want to count a number of counts before you actually count that number.
PWM generation with a software inversion. We also can do realtime clock. The timers can count up or down. We have simple PWM here on the general-purpose timer modules with no dead-band generation. If you need dead-band generation in your device, you need to get a device that has the PWM module, the motion control module that has a full set with dead-band generation as well.
There's support here for timer synchronization so that reloading the timers happen simultaneously for daisy-chaining the different timers together and for stalling during debugging. Now, these timers can also trigger ADC samples, ADD conversions, or DMA transfers.

## Slide 41: Lab 4: Interrupts and the GP Timer
Enable and configure the Timer
Enable and configure Interrupts
Write the ISR code and test
Generate an exception
Agenda ...
USB Emulation Connection
Notes: In lab four, we'll use the general-purpose timer to countdown from a preset value. When the timer reaches zero, it will generate an interrupt and reload the timer. The interrupt hardware on the LM4F device will then find the correct address of the interrupt service routine you've written and execute it. These are all real-world skills that you'll need over and over again when working with any microcontroller.

## Slide 42: Agenda
ADC...
Introduction to ARM® Cortex™-M4F and Peripherals
Code Composer Studio
Introduction to StellarisWare, Initialization and GPIO
Interrupts and the Timers
ADC12
Hibernation Module
USB
Memory
Floating-Point
BoosterPacks and grLib
Synchronous Serial Interface
UART
µDMA
Notes: Chapter five covers the 12-bit, analog-to-digital converter or ADC12. The LM4F120H5QR has two of them. Since most microcontroller projects measure and/or control things in the real analog world, the device needs to be able to monitor what's happening out there. One channel of the ADC12 is connected to an internal temperature sensor. You'll use that sensor in the lab to monitor the temperature of the LM4F120H5QR and experiment with the ADC12.

## Slide 43: Analog-to-Digital Converter
Stellaris LM4F MCUs feature two ADC modules (ADC0 and ADC1) that can be used to convert continuous analog voltages to discrete digital values
Each ADC module has 12-bit resolution
Each ADC module operates independently and can:
  Execute different sample sequences
  Sample any of the shared analog input channels
  Generate interrupts & triggers
ADC
VIN
VOUT
Input Channels
Triggers
Interrupts/ Triggers
Interrupts/ Triggers
12
VIN
VOUT
000
001
011
010
100
101
t
t
ADC1
ADC0
Features...
Notes: The Stellaris LM4F microcontrollers feature two ADC modules, ADC0 and ADC1, that can be used to convert continuous analog voltages to discrete digital values. Each one of those modules has 12 bits of resolution. Each one can operate independently. You can execute different sample sequences. You can sample any of the shared analog input channels, and you can generate interrupts and triggers with them.

## Slide 44: LM4F120H5QR ADC Features
Two 12-bit 1MSPS ADCs
12 shared analog input channels
Single ended & differential input configurations
On-chip temperature sensor
Maximum sample rate of one million samples/second (1MSPS).
Fixed references (VDDA/GNDA) due to pin-count limitations
4 programmable sample conversion sequencers per ADC
Separate analog power & ground pins
Flexible trigger control
  Controller/ software
  Timers
  Analog comparators
  GPIO
2x to 64x hardware averaging
8 Digital comparators / per ADC
2 Analog comparators
Optional phase shift in sample time, between ADC modules … programmable from 22.5 ° to 337.5°
ADC
VIN
VOUT
Sequencers...
Notes: The Analog to Digital Converters on the LM4F120H5QR are two 12-bit, one mega sample per second SAR-type with 12 shared analog input channels. Those inputs can be single-ended and differential. There is an on-chip temperature sensor. The maximum sample rate is one mega sample per second.
Due to the low-cost nature of the device and the pin count limitation, there is a fixed reference between the analog voltage and ground. There are four programmable sample conversion sequencers per ADC that we'll deal with on the next slide. Separate analog power and ground pins to keep the noise between the digital and analog sides. Flexible trigger control for the microprocessor. The software can trigger it. The timers can trigger it. The analog comparators can trigger it. GPIO can trigger a measurement.
We have hardware averaging that we can go between 2 and 64 samples that will be averaged together to generate a result. That's in powers of two.
Each ADC has eight digital comparators. There are two total analog comparators for the device. Optionally, you can phase, shift, and sample time between the ADC modules, and that's programmable from 22 and a half to 337.5 degrees.

## Slide 45: ADC Sample Sequencers
Stellaris LM4F ADC’s collect and sample data using programmable sequencers.
Each sample sequence is a fully programmable series of consecutive (back-to-back) samples that allows the ADC module to collect data from multiple input sources without having to be re-configured.
Each ADC module has 4 sample sequencers that control sampling and data capture.
All sample sequencers are identical except for the number of samples they can capture and the depth of their FIFO.
To configure a sample sequencer, the following information is required:
  Input source for each sample
  Mode (single-ended, or differential) for each sample
  Interrupt generation on sample completion for each sample
  Indicator for the last sample in the sequence
Each sample sequencer can transfer data independently through a dedicated μDMA channel.
Sequencer | Number of Samples | Depth of FIFO
SS 3 | 1 | 1
SS 2 | 4 | 4
SS 1 | 4 | 4
SS 0 | 8 | 8
Lab...
Notes: The Stellaris LM4F ADCs collect and sample their data using programmable sequencers. Each sample sequence in the sequencer is a fully programmable series of consecutive samples that allows the ADC to collect data from multiple input sources without having to be reconfigured. Each one of the modules has four sample sequencers that control the sampling and data capture. They're all identical except for the number of samples that they can capture and the depth of the FIFO that's associated with it.
In order to configure a sample sequencer, the following information is going to be required for each one of the samples that you want to make. So, you can figure a sample sequencer with one or four or eight different samples, or let's say on one that has four samples, you might only use two or three. That's all applicable.
You can configure the input source for each sample. What's the mode? Is it going to be single-ended or differential? Are you going to generate an interrupt on the sample completion? Are you going to indicate that this is a last sample in the sequence? And bear in mind you can do this for every single sample. As many as, for sample sequencer zero, eight total samples. So, each sample sequencer can then transfer its data from the FIFO independently using a dedicated DMA channel.

## Slide 46: Lab 5: ADC12
Enable and configure ADC and sequencer
Measure and display values from internal temperature sensor
Add hardware averaging
Use ROM peripheral driver library calls and note size difference
Agenda ...
USB Emulation Connection
Notes: In lab five, you'll write code to make measurements with the on-chip, 12-bit, analog-to-digital converter. To keep things simple, you'll use the internal temperature sensor as an input to the ADC12. You can then use your finger to warm the microcontroller on the LaunchPad board to see the temperature change.

## Slide 47: Agenda
Key Features...
Introduction to ARM® Cortex™-M4F and Peripherals
Code Composer Studio
Introduction to StellarisWare, Initialization and GPIO
Interrupts and the Timers
ADC12
Hibernation Module
USB
Memory
Floating-Point
BoosterPacks and grLib
Synchronous Serial Interface
UART
µDMA
Notes: Chapter six covers the hibernation model and low-power modes. This module manages the removal and restoration of power to the CPU and peripherals to provide a means of reducing the power consumption. Additional features include a realtime clock that can be used for wake events and battery-backed SRAM for storing and restoring the processor state.

## Slide 48: Key Features
Real Time Clock is a 32-bit seconds counter with a 15-bit sub seconds counter & add-in trim capability
Dedicated pin for waking using an external signal
RTC operational and hibernation memory valid as long as VBAT is valid
GPIO pins state retention provided during VDD3ON mode
Two mechanisms for power control
  System Power Control for CPU and other on-board hardware
  On-chip Power Control for CPU only
Low-battery detection, signaling, and interrupt generation, with optional wake on low battery
32,768 Hz external crystal or an external oscillator clock source
16 32-bit words of battery-backed memory are provided for you to save the processor state to during hibernation
Programmable interrupts for RTC match, external wake, and low battery events.
Low Power Modes...
Notes: Some key features of the hibernation module. The realtime clock is a 32-bit seconds counter with a 15-bit subseconds counter, so you can time much lower than single seconds. And it has an add-in trim capability for getting precision control over the time. We have a dedicated pin for waking up using an external signal. The realtime clock is operational, and the hibernation memory is valid as long as the battery voltage is valid.
On the LaunchPad board, the battery voltage is connected directly to the processor voltage. So, the battery voltage will never be bad, but in your design, you may have a separate battery and a separate battery holder. So, if that battery is dead or if that battery is not present, you don't want your part going into hibernation. The part will not go into hibernation if that battery isn't there or isn't valid.
We also have a VDD3 on mode that provides state retention of the GPIO pins during hibernation. Remember that what's going on here is we're actually shutting the part off at the very lowest power modes. When that happens, you're essentially coming back up from reset. This will allow you to keep the GPIO pins there as you come back up without resetting them.
So, if you're going to shut the part down, you need a mechanism for power control. We have an on-chip voltage regulator for power control for the CPU only. We also have a pin that comes out that provides system power control through a voltage regulator on your board for any other onboard hardware.
The part has low battery detection, signaling, and interrupt generation with optional wake on low battery. If that battery gets down to the point where it can't run anymore, it can't hold your memory in place, you probably want to wake up.
You can connect a 32,768-hertz external crystal or an external oscillator clock for the realtime clock. There are 16 32-bit words of battery-backed memory for you to save the processor state to during hibernation. It's important here. This is battery-backed SRAM.
Other types of memory, like EEPROM or flash, have significant issues. If you power down the device as you're trying to save things in them, one, it's slow to write to those things, and two, they eat a lot of memory. Three, there's a big problem if you power down in the middle of actually trying to write those things.
Battery-backed SRAM doesn't have any of those issues. It's extremely fast. It's extremely power efficient, and if you actually managed to power down in the middle of it, all you end up with is a corrupted saved piece of memory. You don't end up with corrupted memory.
We have programmable interrupts on the module for realtime clock match. You can wake every three seconds, ten seconds, and so on. We can wake on an external pin, and we can wake on low-battery events.

## Slide 49: Power Modes
  Run mode
  Sleep mode stops the processor clock
    2 SysClk wakeup time
  Deep Sleep mode stops the system clock and switches off the PLL and Flash
    1.25 – 350 µS wakeup time
  Hibernate mode with only hibernate module powered (VDD3ON, RTC and no RTC)
    ~500µS wakeup time
TBD
Power Mode Comparison...
1.05
Notes: The power modes on the LM4F are run mode, sleep mode, deep sleep mode, and then the hibernate modes below that. BDD3 on with the realtime clock running and without the realtime clock running.
Now, anytime you quote these kinds of numbers, you need to be asking, "Under what conditions are these numbers valid?" And these numbers were done at 40 megahertz with the PLL on for the run mode and the sleep mode. You'll take a look on the next page will give you some further details on this, but whenever you're looking at the strict numbers on what the current consumption is, you really need to be aware of under what conditions these numbers were derived.
So, the run mode we're looking at somewhere in the 32 milliamp range. When we go into sleep mode, that's going to stop the processor clock. Of course, turn off the ... that means basically the processor is not running. It's still powered. So, a two sys clock wake-up time, a significant power savings and a very fast wake-up time.
When you go into deep sleep mode, that stops the system clock and switches off the 400 megahertz phase lock loop and flash memory. You're still getting a 1.25 to 350 microsecond wake-up time, which is pretty fast. We're still coming up with the numbers on the exact current draw for those.
Hibernate modes, there are three different kinds of hibernate modes here. In the hibernate VDD3 on, this can be with the power on or on battery. The hibernate modes RTC and no RTC are only on battery. These are going to give you in the 500 microseconds wake-up time to come back up from very, very deep sleep. Down in the five microamps, 1.7 microamps, and 1.6 microamps. Let's take a look at a few more details about the power modes on the next slide.

## Slide 50: Power Mode Comparison
Mode → | Run Mode | Sleep Mode | Deep Sleep Mode | Hibernation (VDD3ON) | Hibernation (RTC) | Hibernation (no RTC)
Parameter ↓ |  |  |  |  |  | 
IDD | 32 mA | 10 mA | 1.05 mA | 5 μA | 1.7 μA | 1.6 μA
VDD | 3.3 V | 3.3 V | 3.3 V | 3.3 V | 0 V | 0 V
VBAT | N.A. | N.A. | N.A. | 3 V | 3 V | 3 V
System Clock | 40 MHz with PLL | 40 MHz with PLL | 30 kHz | Off | Off | Off
Core | Powered On | Powered On | Powered On | Off | Off | Off
 | Clocked | Not Clocked | Not Clocked | Not Clocked | Not Clocked | Not Clocked
Peripherals | All On | All Off | All Off | All Off | All Off | All Off
Code | while{1} | N.A. | N.A. | N.A. | N.A. | N.A.
LaunchPad Considerations ...
Box denotes power modes available on LaunchPad board
Notes: Next up is a power mode comparison. Now, critical to any power mode comparison is always the asterisk at the bottom. Right? Under what condition are you making these measurements? Here you can see we're taking a look at the run mode, sleep mode, deep sleep mode, the VDD3 on mode, and then we have hibernation mode with the realtime clock running and hibernation mode without the realtime clock.
So, as far as the power goes, we're running the part at 3.3 volts, and that applies all the way until you're in the deep hibernation, the two deep hibernation modes on the far right. In those, the VDD will be off. The VBAT doesn't matter until you've reached any of the hibernation modes. The battery voltages needs to be three volts.
The system clock down here when we're in run mode, it's 40 megahertz with the 400 megahertz phase lock loop running there and in the sleep mode. In deep sleep mode, we're running the part off of the low frequency oscillator on the part. In any of the hibernation modes, the system clock is off.
Take a look at the core parameter down here. In the run mode, sleep mode, and deep sleep, the core is powered on. In the others, it's off. The core is clocked in run mode, not clocked in any of the rest of the modes that we're using here. You can see that only in run mode will we have all the peripherals on.
And here, what are we doing during the run mode? We're actually in a while loop. We're actually running some code that's off and doing something. Be careful about what you see there. Some processors may be sitting there doing nothing. This is actually in a while loop. In the other ones, it doesn't matter because the core isn't clocked, so it can't run any code.
Now, this box, this red dotted box denotes the power modes that are available on the launchpad board. That's because we don't have a battery on the launchpad board. The VBAT is connected to the CPU voltage, which means we can't run those hibernation modes on the far right. Your system could run that. Certainly, the LM4F120H5QR could run that if that battery voltage pin was connected to a battery.
So, in run mode, we're seeing 32 milliamps at 40 megahertz core speed. In the sleep mode, 10 milliamps with 40 megahertz and the PLL running. The deep sleep mode, we have a ... we need to get a number on that. That's still under investigation. The hibernation mode is down in the five microamp range. We'll be able to measure that in the class.
Hibernation mode off the battery with a realtime clock running is somewhere in the 1.7 microamp range. Hibernation without the realtime clock running is somewhere in the 1.6 microamp range. Those are extremely good numbers for an ARM device.

## Slide 51: LaunchPad Considerations
  The low-cost LaunchPad board does not have a battery holder
  VDD and VBAT are wired together on the board (this disables battery-only powered low-power modes)
  Device current is measured between test points H24 and H25
Lab ...
Notes: The low-cost LaunchPad board doesn't have a battery holder. The VDD, the power to the CPU, and the V battery are wired together on the board. So, that's going to disable those battery-only powered low-power modes.
If you take a look at the diagram here on the bottom, you can see that the pin 37, the VBAT is connected to the analog voltage, as well as the four VDD pins. Now, those are connected to the pins H24 and H25. Right now, on the top of your board, you'll see a jumper. That jumper jumpers those pins together. R30 has been omitted. We will be able to use our meter to measure the current between those two pins.
I'd like to highlight though, most meters have a problem in terms of the equivalent series resistance. If you're in a very low power mode, say trying to measure 200 microamps or less, you usually can't get enough current, say 30 or 40 milliamps. You can't get that through the meter, so the equivalent series resistance is too high.
The other thing is that when you plug these things on there, you will probably want a set of leads that are able to go over top of the Molex connector or you have some kind of a clip. Trying to hold probes onto the top of these things just doesn't work.

## Slide 52: Lab 6: Low Power Modes
Place device in low power modes
Wake from pin
Wake from RTC
Measure current
No battery holder on board
Agenda ...
USB Emulation Connection
Power Measurement Jumper
Notes: In lab six, you're going to measure the current draw of the LM4F device when it is placed in run and hibernate modes. The low-cost Stellaris LaunchPad board does not have a battery holder, so the battery power input is connected to the power for the CPU. This will shorten our experiment somewhat, but you'll still see the device wake up from the realtime clock and wake pin events.

## Slide 53: Agenda
USB Basics...
Introduction to ARM® Cortex™-M4F and Peripherals
Code Composer Studio
Introduction to StellarisWare, Initialization and GPIO
Interrupts and the Timers
ADC12
Hibernation Module
USB
Memory
Floating-Point
BoosterPacks and grLib
Synchronous Serial Interface
UART
µDMA
Notes: The LM4F120H5QR is equipped with a 12 megabit per second, USB 2.0 compliant, USB device port. USB ports on other Stellaris devices have on-the-go and host modes, as well as device, but this LM4F part is cost-reduced to have just the device port. In chapter six, you'll look at the basics of USB and how the USB port is implemented on our device.

## Slide 54: USB Basics
Multiple connector sizes
4 pins – power, ground and 2 data lines (5th pin ID for USB 2.0 connectors)
Configuration connects power 1st, then data
Standards:
  USB 1.1
    Defines Host (master) and Device (slave)
    Speeds to 12Mbits/sec
    Devices can consume 500mA (100mA for startup)
  USB 2.0
    Speeds to 480Mbits/sec
    OTG addendum
  USB 3.0
    Speeds to 4.8Gbits/sec
    New connector(s)
    Separate transmit/receive data lines
USB Basics...
Notes: Reviewing some USB basics, USB connectors come in multiple sizes, as you can see on the top right there. Most of them have four pins: Power, ground, and two data lines called D plus and D minus. Some of the connectors have a fifth pin I.D. for USB 2.0 connectors. If you take a look down at the diagram on the bottom right, it'll show you that the pins for the power are slightly longer. That way the power will be connected first and then the data.
The different standards that are out there, USB 1.1 defines the host as the master and the device as the slave. Speeds to 12 megabits per second and the devices can consume 500 milliamps once they're enumerated, 100 milliamps for startup.
Stellaris USB ports are USB 2.0 compliant. The speeds are as high as 480 megabits per second, but you can be at full speed, which is 12 megabits per second and still be compliant. USB 2.0 also includes the on-the-go addendum where devices can be host device or they can decide which they're going to be during enumeration.
New out there is USB 3.0 with speeds to 4.8 gigabits per second. Of course, we're going to have new connectors to support that with split-up data, transmit and receive data lines.

## Slide 55: USB Basics
USB Device … most USB products are slaves
USB Host … usually a PC, but can be embedded
USB OTG … On-The-Go
  Dynamic switching between host and device roles
  Two connected OTG ports undergo host negotiation
Host polls each Device at power up. Information from Device includes:
  Device Descriptor (Manufacturer & Product ID so Host can find driver)
  Configuration Descriptor (Power consumption and Interface descriptors)
  Endpoint Descriptors (Transfer type, speed, etc)
  Process is called Enumeration … allows Plug-and-Play
LM4F120H5QR USB...
Notes: Most USB products that are sold are slaves. For instance, a USB flash drive. A USB host, normally that's some kind of a PC or computing device, but it can be embedded. USB on the go, that's dynamic switching between the host and device roles. You can connect two on-the-go ports together, and they'll undergo a host negotiation to figure out who's going to be in control.
For instance, if you hooked your computer to your digital camera, you'd certainly want your digital camera to be a slave to your PC's host. But if you take the digital camera and connect it to a printer, you would want the camera to be a host to the printer's slave so that you could print to it.
The host pulls each device at power up, and information from the device is going to include the device descriptor. That's the manufacturer and product I.D. so that the host can find the driver if it needs one. A configuration descriptor, that includes the power consumption and any interface descriptors that are required. The end point descriptors, that's the transfer types, whether it's bulk, isochronous, the rest of those, the speed and so on. The process of the host querying the device for all of these structures and then configuring itself is called enumeration, and that's what allows plug-and-play to operate.

## Slide 56: LM4F120H5QR USB
USB 2.0 Device mode full speed (12 Mbps) and low speed (1.5 Mbps) operation
Integrated PHY
Transfer types: Control, Interrupt, Bulk and Isochronous
Device Firmware Update (DFU) device in ROM
Stellaris collaterals
Texas Instruments is a member of the USB Implementers Forum.
Stellaris is approved to use the USB logo
Vendor/Product ID sharing
  http://www.ti.com/lit/pdf/spml001
FREE
Vendor ID/ Product ID
sharing program
Block Diagram...
Notes: 56
The USB port on the LM4F120H5QR is a USB 2.0 device that offers full speed. That's 12 megabits a second. And it goes down to low speed, which is one and a half megabit per second operation. The device has an integrated fi (phonetic sp.) on it, so the hardware connection to the USB port is very simple. We offer transfer types, all the major ones: control, interrupt, bulk, and isochronous.
We also offer device firmware update in ROM, so you can plug this LM4F12H5QR ... you can plug it into a host and do device firmware update across to it. On other Stellaris devices that have host mode, they can also offer that you can plug in say a flash drive with the correctly formatted files on it, and it will do a device firmware update from a device as a host. And all you have to do, like I said, is have the correct files in it.
Stellaris collaterals. TI is a member of the USB implementers' forum, and Stellaris is approved used USB logo. The stacks, the hardware and so on are certified USB compliant. We also offer vendor and product I.D. sharing. We have ... that's also called VID and PID. It costs a certain amount to go to the USB organization and buy the vendor I.D. and product I.D.s. We can have you, if you fill out a sharing agreement, you can utilize produce I.D.s underneath our vendor, and this is perfectly legal.

## Slide 57: USB Peripheral Block Diagram
Integrated USB Controller and PHY with up to 16 Endpoints
  1 dedicated control IN endpoint and 1 dedicated control OUT endpoint
  Up to 7 configurable IN endpoints and 7 configurable OUT endpoints
  4 KB dedicated endpoint memory (not part of device SRAM)
  Separate DMA channels (up to three IN Endpoints and three OUT Endpoints)
  1 endpoint may be defined for double-buffered 1023-bytes isochronous packet size
EP0 – 15 Control
USBLib...
Notes: The block diagram for the USB peripheral is shown at the top of this slide. This is a integrated USB controller and the fi, the physical connection that offers up to 16 endpoints. Now, anytime you connect a USB device to a host, there is one dedicated control in and one dedicated control out so that you can do the enumeration across there. And then there are up to seven configurable input endpoints and seven configurable output endpoints.
As a part of the controller, there's a 4K dedicated endpoint memory. That's a single 4K, not per endpoint, and that's not part of the device SRAM. That's inside this peripheral. There's separate DMA channels, up to three in endpoints and three out endpoints that you can use from the peripheral to transfer directly to memory. One of the endpoints can be defined for double-buffered, 1K byte asynchronous packet size to facilitate moving large groups of data across this port.

## Slide 58
StellarisWare USBLib
License-free & royalty-free drivers, stack and example applications for Stellaris MCUs
USBLib supports Host/Device and OTG, but the LM4F120H5QR USB port is Device only
Builds on DriverLib API
  Adds framework for generic Host and Device functionality
  Includes implementations of common USB classes
Layered structure
Drivers and .inf files included where appropriate
Stellaris MCUs have passed USB Device and Embedded Host compliance testing
  Device Examples
    HID Keyboard
    HID Mouse
    CDC Serial
    Mass Storage
    Generic Bulk
    Audio
    Device Firmware Upgrade
    Oscilloscope
  Windows INF for supported devices
    Points to base Windows drivers
    Sets config string
    Sets PID/VID
    Precompiled DLL saves development time
  Device framework integrated into USBLib
Abstraction Levels...
Notes: TI's StellarisWare USB library is a license-free and royalty-free set of drivers, a stack and example applications for Stellaris microcontrollers. Now, like a Ethernet port, like a CAN port, there is a stack that you interact with to send information back and forth across the USB port.
Of course, you can do it yourself. You can write your own peripheral driver code and write to the ports using just the peripheral driver library, but it's a lot easier just to talk to the stack. And we have a stack as part of StellarisWare. Now, that stack supports host device and on-the-go, but of course, the LM4F120H5QR, that USB port is device only.
The Texas Instruments® Stellaris® USB Library is a set of data types and functions for initializing & configuring USB module in host, device & OTG mode on Stellaris MCUs.
The capabilities and organization of the USB library functions are governed by the following design goals:
1) They are written entirely in C.
2) They are easy to understand.
3) They are reasonably efficient in terms of memory and processor usage.
4) They are as self-contained as possible.
5) Where possible, computations that can be performed at compile time are done there instead of at run time.
6) They can be built with more than one tool chain.
The USB lib is built over Driver lib APIs to provide a higher level support for USB. This includes implementations of common USB classes.
The layered structure of usb lib means that developers can choose the extent to which they use the library functions. To speed up & ease the application development, we also provide a number of examples for each of the three modes namely, Host, Device and OTG
TI is a member of USB implementers forums, this shows our strong commitment for usb in not just current devices, but also the devices going forward.

## Slide 59: USB API Abstraction Levels
USB DriverLib API
USB Host Controller API/USB Device API
Host Class Driver/Device Class Driver APIs
Host Class/ Device Class APIs
Application 4
Implements its own USB protocol using Driverlib.
(Third party USB stack)
Application 3
Uses existing API for generic host/device operation.
Uses DriverLib for features not covered by these APIs.
(Custom Classes)
Application 2
Passes key info to the Driver API.
Driver API handles all lower level functions for the chosen class.
(Custom HID device)
Application 1
Passes simplified data to a higher level API.
(Custom HID mouse)
Level of customization
Level of abstraction
LOW
HIGH
HIGH
LOW
Lab...
Notes: The stack software, etc. is built on top of the driver lib API. It adds a framework for a generic host and generic device functionality, and it includes implementations of the common USB classes that we talked about earlier. It has a layered structure, so you can go in and dial in the amount of control that you want to have over the software. I'll show that on the next page. The drivers and the INF files are included where that's appropriate so that you can communicate back to Windows with them.
I mentioned before, the Stellaris microcontrollers, the hardware, and the software have passed USB device and embedded host compliance testing. So, if you want to go off and get the certified USB certification from the USB organization, you can go do that and stamp your product with a certified USB decal.
Some of the device examples that are available are the human interface device for the keyboard. This is where this device, say the device it self will act as a keyboard. The device itself will act as a mouse. We can do mass storage to the device, audio, device firmware upgrade, the LM3S3748 and act as an oscilloscope. We have implementations for serial and for bulk to store, and that's one of the things that we're going to be doing is the bulk example.
We have Windows INF files for supported devices to point to the base Windows drivers. Some of these applications have drivers in Windows. You don't need to do anything. Those will also help you set the config (phonetic sp.) string, set the PID and VID, and there's a precompiled DLL that's going to save you development time. And all that device framework is integrated into the USB libe and the stack.
You can decide on what level of customization that you want to deal with when you're working with the USB APIs. If you take a look at the far left application one, you just want to pass simple data to a higher level API. For instance, the customized ... you want to customize the mouse human interface device, so you're going to build on top of the host and device class APIs, the class driver, device class driver APIs, the host controller device, and the driver libe API. This is what's going to implement the entire stack for you.
You can increase your level of customization as you move all the way over to the right where, for example, you would implement your own USB protocol using driver libe. This would be where you'd go off, and for instance, you might purchase a third-party USB stack. Or you might go off and write your own. Obviously, to the far left is less time spent developing your USB software, and the far right can be a lot if you're going to write it yourself or if you're going to purchase a third-party USB stack because it has some capability that you require.
Which APIs to use, when? The answer depends on the level of abstraction that is most suitable for your end application. Lets take a look at this slide in order to understand this a little better. Some example USB applications are listed in red blocks. Each application requires different level of customization. Application 1 is high customized and implements its own USB protocol i.e. a third party USB stack, where as Application 4 is relatively standard, passes data to a higher level APIs in a custom HID mouse.
Different layers/ or levels of abstractions are listed in the black blocks. for an application that involves passing simplified data to a higher level API, using host/ device class APIs will be a recommended approach. This provides highest level of abstraction, and speeds up the development time. This is represented in Application 1 in the diagram on the slide.
For an application that involves implementing its own usb protocol using driver lib, working with USB driver API will be a recommended approach. The provides lowest level of abstraction, giving user most amount of visibility & control. This is represented in Application 4 in the diagram on the slide.
For applications in between, like Example 2 and 3 shown, a user can pick and choose a level of abstraction that is not too low, high.
This is how applications fit into the API system. Note that devices that resemble existing applications require significantly less new code.

## Slide 60: Lab 7: USB
Run usb_bulk_example code and windows side app
Inspect stack setup
Observe data on device
Agenda ...
USB Device Connection
USB Emulation Connection
Notes: In lab seven, you'll use a StellarisWare code example to implement bulk transfers of data from your laptop host to and from the USB port on the LaunchPad. You'll use a small Windows side application to send and view data while also watching messages on the terminal display. You'll also use the emulator to view transferred data in the LM4F120H5QR memory.

## Slide 61: Agenda
Memory Control...
Introduction to ARM® Cortex™-M4F and Peripherals
Code Composer Studio
Introduction to StellarisWare, Initialization and GPIO
Interrupts and the Timers
ADC12
Hibernation Module
USB
Memory
Floating-Point
BoosterPacks and grLib
Synchronous Serial Interface
UART
µDMA
Notes: The LM4F120H5QR has four different types of memory: flash, SRAM, EEPROM, and ROM. In chapter eight, you'll learn about the different features and capabilities of the flash, SRAM, and EEPROM. You'll also learn how to use bit banding and how to use the Memory Protection Unit, or MPU.

## Slide 62: Flash, SRAM and ROM Control
Memory Blocks and Control Logic for:
SRAM
ROM
Flash
EEPROM Control...
Notes: This diagram shows you a little bit about the flash, SRAM, and ROM control. On the far left is the cortex M4F. You'll notice that there's a separate instruction code and decode bus for instructions and for data, so this is a Harvard architecture inside to the ROM and the flash. You'll notice the system bus goes down to the bridge to the SRAM array, yet up at the top, we have ROM control to the ROM array. We have all of these buffers and control-type logic and settings to talk to the flash array. There's also, down at the bottom, we have the flash protection and then a series of user registers.

## Slide 63: EEPROM Control
EEPROM Block and Control Logic
EEPROM block is connected to the AHB (Advanced High Performance Bus)
Flash Features...
Notes: The EEPROM control is separate because it's in peripheral space. You'll see the EPROM array with the separate blocks on the right-hand side, a security setting, a separate program once we've been able to go through the security, and then the control registers that control the size, the page, the offset, how we're writing to it and so on.
Remember, the EEPROM block is connected to the advanced, high-performance bus for maximum speed. Flash memory on the LM4F120H5QR is 256K long, and it's single cycle to 40 megahertz. That memory starts at all zeroes, as shown in the memory map below. It's organized into 1K independently-erasable blocks. Like I showed you in the previous slide, the code fetches and data accesses occur over separate buses. You don't have to worry about it being a Harvard architecture machine. This just speeds you up.

## Slide 64: Flash
256KB / 40MHz starting at 0x00000000
Organized in 1KB independently erasable blocks
Code fetches and data access occur over separate buses
Below 40MHz, Flash access is single cycle
Above 40MHz, the prefetch buffer fetches two 32-bit words/cycle. No wait states for sequential code.
Branch speculation avoids wait state on some branches
Programmable write and execution protection available
Simple programming interface
0x00000000 Flash
0x01000000 ROM
0x20000000 SRAM
0x22000000 Bit-banded SRAM
0x40000000 Peripherals & EEPROM
0x42000000 Bit-banded Peripherals
0xE0000000 Instrumentation, ETM, etc.
EEPROM...
Notes: Below 40 megahertz, that flash access is single-cycle. Above 40 megahertz, there's a pre-fetch buffer that fetches two 32-bit words per cycle. Remember that we're running thumb-to instruction code, which can be either 16 or 32, so at a minimum, we're able to grab two 32-bit instructions per cycle, and that's at a minimum. So, in straight line sequential code, there's no wait states involved.
So, the only problem is going to be if you hit a branch. We have branch speculation that on one direction of the branch, it does a speculate to see if you're going to go in that direction, and it's going to avoid a wait state in that direction. So, only in one branch, one side of the branch, are you going to incur a wait state.
The right and execution protection are available on the flash so that you can configure this so that people can't write into it without a password, and it has a very simple programming interface, as we'll see in the lab.

## Slide 65: EEPROM
2KB of memory starting at 0x400AF000 in Peripheral space
Accessible as 512 32-bit words
32 blocks of 16 words (64 bytes) with access protection per block
Built-in wear leveling with endurance of 500K writes
Lock protection option for the whole peripheral as well as per block using 32-bit to 96-bit codes
Interrupt support for write completion to avoid polling
Random and sequential read/write access (4 cycles max/word)
0x00000000 Flash
0x01000000 ROM
0x20000000 SRAM
0x22000000 Bit-banded SRAM
0x40000000 Peripherals & EEPROM
0x42000000 Bit-banded Peripherals
0xE0000000 Instrumentation, ETM, etc.
SRAM...
Notes: EEPROM is 2K of memory starting at ... and this is in the peripheral space, 0X400AF000. It's accessible as 512 32-bit words. That's broken up into 32 blocks of 16 words. That's 64 bytes in there with access protection per block. We get to an endurance level of 500,000 writes with built-in wear leveling on this, so you won't be wearing out a single bit. Lock protection is available for the whole peripheral, as well as per block using 32-bit to 96-bit codes if you like.
We have available interrupt support for write completions so that you don't have to pull to make sure that you've finished writing to the memory. Random and sequential rewrite access is possible, four cycles maximum per word. If you're doing random, that's four cycles. If you do sequential, it's less than that.

## Slide 66: SRAM
32KB / 80MHz starting at 0x20000000
Bit banded to 0x22000000
Can hold code or data
0x00000000 Flash
0x01000000 ROM
0x20000000 SRAM
0x22000000 Bit-banded SRAM
0x40000000 Peripherals & EEPROM
0x42000000 Bit-banded Peripherals
0xE0000000 Instrumentation, ETM, etc.
Bit-Banding...
Notes: There is 32K of SRAM on the device. It’s full speed 80 megahertz starting at 20,000,000. That physical memory is bit-banded into 22,000,000. And of course, SRAM can hold code or data. You can execute out of SRAM if you choose to do so.

## Slide 67: Bit-Banding
Reduces the number of read-modify-write operations
SRAM and Peripheral space use address aliases to access individual bits in a single, atomic operation
SRAM starts at base address 0x20000000 Bit-banded SRAM starts at base address 0x2200000
Peripheral space starts at base address 0x40000000 Bit-banded peripheral space starts at base address 0x42000000
The bit-band alias is calculated by using the formula:
bit-band alias = bit-band base + (byte offset * 0x20) + (bit number * 4)
For example, bit-7 at address 0x20002000 is:
0x20002000 + (0x2000 * 0x20) + (7 * 4) = 0x2204001C
MPU...
Notes: As we've mentioned before, all M4 devices have bit-banding. This reduces the number of read modify write operations. SRAM and peripheral space use an address alias to access the individual bits in a single atomic operation. So, SRAM, the physical memory, starts at a base address of 0X200000000. Call it 20,000,000. The bit-banded SRAM, the bit-banded address alias of that starts at base address 22,000,000. Peripheral space starts at a base address of 40,000,000. The bit-banded peripheral space starts at base address 42,000,000.
So, if you want to calculate the bit-banded alias, use this following formula. So, the bit-banded alias is whatever the base address is of the piece of memory that you're looking for, plus the byte offset times 0X20. That's 32. Plus the big number times four. So, if you're ... for example, if you're looking for to calculate the bit-banded address of bit seven of address 20,002,000, that's going to be that base address, 20,002,000, plus the offset, which is 2,000 hex times 0X20, that's times 32, plus bit 7 times 4. Add all that together, and you're going to get a bit-banded address of 0X2204001C. The LSB of that location will be bit seven of physical address 20002000

## Slide 68: Memory Protection Unit (MPU)
Defines 8 separate memory regions plus a background region accessible only from privileged mode
Regions of 256 bytes or more are divided into 8 equal-sized sub-regions
MPU definitions for all regions include:
  Location
  Size
  Access permissions
  Memory attributes
Accessing a prohibited region causes a memory management fault
Privilege Levels...
Notes: The memory protection unit defines eight separate memory regions, plus a background region that's accessible only from privilege mode. These regions of 256 bytes or more get divided into eight equal sized subregions. You can set up the definitions for every one of those regions, including ... that's going to include the location of the region, the size of the region.
What access permissions do you want to allow? Do you want to allow execution? Do you want to allow code? Do you want to allow data? Do you want to not have any access? And what other memory attributes do you want to specify? Accessing a prohibited region in memory is going to cause a memory management fault. We're going to see that in the lab. Accessing some of the registers that allow you to program the memory protection unit are protected by privilege level. We're going to talk about that in the next slide.

## Slide 69: Cortex M4 Privilege Levels
Privilege levels offer additional protection for software, particularly operating systems
Unprivileged : software has …
  Limited access to the Priority Mask register
  No access to the system timer, NVIC, or system control block
  Possibly restricted access to memory or peripherals (FPU, MPU, etc)
Privileged: software has …
  use of all the instructions and has access to all resources
ISRs operate in privileged mode
Thread code operates in unprivileged mode unless the level is changed via the Thread Mode Privilege Level (TMPL) bit in the CONTROL register
Lab...
Notes: The cortex M4 has two different privilege levels. Those levels offer additional protection for software, particularly if you're using operating systems. In unprivileged mode, your software has limited access to the priority mass register. No access to the system timer, the NVIC, or the system control block, and possibly restricted access to memory or peripherals. Privileged software has use of all the instructions and has access to all the resources.
ISRs operate in privilege mode. Threaded code, like in an operating system or standard, operates in unprivileged mode unless the level gets changed via the thread mode privilege level bit in the control register.

## Slide 70: Lab 8: Memory and the MPU
Create code to write to Flash
Create code to read/write EEPROM
Experiment with MPU and bit-banding
Agenda ...
USB Emulation Connection
Notes: In lab eight, you'll create code to write to flash and to rewrite EEPROM. You'll also experiment with bit banding. Then you'll configure and use the memory protection unit.

## Slide 71: Agenda
What is Floating-Point?...
Introduction to ARM® Cortex™-M4F and Peripherals
Code Composer Studio
Introduction to StellarisWare, Initialization and GPIO
Interrupts and the Timers
ADC12
Hibernation Module
USB
Memory
Floating-Point
BoosterPacks and grLib
Synchronous Serial Interface
UART
µDMA
Notes: In chapter nine, you'll learn about the floating point unit on the LM4F120H5QR. All of TI's M4 devices are equipped with a floating point unit. Although for code compatibility reasons, it switched off at reset. You'll learn about the basics of floating point numbers and how the LM4F devices implement them.

## Slide 72: What is Floating-Point?
Floating-point is a way to represent real numbers on computers
IEEE floating-point formats:
  Half (16-bit) 
  Single (32-bit) 
  Double (64-bit) 
  Quadruple (128-bit) 
What is IEEE-754?...
Notes: What is floating point? Floating point is a way to represent real numbers on computers. There are several IEEE floating point formats: the half precision at 16 bits, single precision at 32 bits, double precision at 64 bits, and quadruple at 128 bits. IEEE 754 is single precision. That's the 32-bit version there. Assign bit eight bits of exponent and 23 bits of fraction.

## Slide 73: What is IEEE-754?
FPU...
exponent = [10000110]2 = [134]10
fraction = [0.110100001000000000000000]2 = [0.814453]10
sign = (-1)0
= [1]10
Decimal Value = (-1)s x (1+f) x 2e-bias
= [1]10 x ([1]10 + [0.814453]10) x [2134-127]10
= [1. 814453]10 x 128
= [232.249]10
Symbol |  |  | s | e |  |  |  |  |  |  |  | f |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Example |  |  | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | X
Bit |  |  | 31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | X
Symbol |  |  | Sign (s) | Exponent (e) |  |  |  |  |  |  |  | Fraction (f) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 bits
23 bits
1 bit
Decimal Value = (-1)s (1+f) 2e-bias
where: f = ∑[(b-i)2-i] ∀ i ϵ (1,23)
bias = 127 for single precision floating-point
Notes: IEEE 754 defines a single-precision, floating point representation, like we just saw on the previous page. For example, right there's the sign bit, the exponent, and then there's the fractional representation. So, if we take this value, here's the minus one. Value equals minus one to the zero, so that's a zero there. We can see that the next portion is the fraction, the mantissa. And then the next part is two to the whatever number that we have there. 134 minus 127.
Calculated out, that gives us a value of 232.25 base ten. If you were to maximize and minimize this, you'd find that you had an effective range of plus and minus of about plus and minus ten to the 38.53 power.
The floating point unit on our devices provides floating point computation functionality that's fully compliant with the IEEE 754 standard. That means it enables conversions between fixed point and floating point data formats and floating point constant instructions.

## Slide 74: Floating-Point Unit (FPU)
The FPU provides floating-point computation functionality that is compliant with the IEEE 754 standard
Enables conversions between fixed-point and floating-point data formats, and floating-point constant instructions
The Cortex-M4F FPU fully supports single-precision:
  Add
  Subtract
  Multiply
  Divide
  Single cycle multiply and accumulate (MAC)
  Square root
Modes of Operation...
Notes: The Cortex M4F floating point unit fully supports single-precision adds, subtractions, multiplies, divides, single-cycle multiply and accumulate, Mac instruction, and square roots. You can see the instructions that the floating point unit supports in the diagram at the bottom of the screen.

## Slide 75: Modes of Operation
There are three different modes of operation for the FPU:
  Full-Compliance mode – In Full-Compliance mode, the FPU processes all operations according to the IEEE 754 standard in hardware. No support code is required.
  Flush-to-Zero mode – A result that is very small, as described in the IEEE 754 standard, where the destination precision is smaller in magnitude than the minimum normal value before rounding, is replaced with a zero.
  Default NaN (not a number) mode – In this mode, the result of any arithmetic data processing operation that involves an input NaN, or that generates a NaN result, returns the default NaN. ( 0 / 0 = NaN )
FPU Registers...
Notes: There are three different modes of operation for the floating point unit. There's full compliance mode. That's where the floating point unit processes all operations according to IEEE 754 in hardware. There's no additional support code required. It runs like that. The next mode is the flush-to-zero mode. If you have a result that's very, very small, as described in the IEEE 754 standard where the destination precision is smaller in magnitude than the minimum normal value before rounding, that gets replaced with a zero. In most cases, that's probably what you want to do.
The next mode is default Nan. That means “not a number” mode. In that mode, the result of any arithmetic data processing operation that involves an input that's not a number or that generates a result that's not a number, it will return the default NaN, meaning my result was not a number. If you do something like zero divided by zero or any number divided by zero, that's a Nan, or not a number.

## Slide 76: FPU Registers
Sixteen 64-bit double-word registers, D0-D15
Thirty-two 32-bit single-word registers, S0-S31
Usage...
Notes: To support its operations, the floating point unit has 16 64-bit, double-word registers, D0 through D15 and 32 32-bit, single-word registers, S0 through S31. The floating point unit is disabled from reset. You must enable it with a StellarisWare API function call before you can use any floating point instructions. The processor must be in a privilege mode to read and write from the code processor access control register. That's the one that's going to turn it on. That API does that.

## Slide 77: FPU Usage
The FPU is disabled from reset. You must enable it* before you can use any floating-point instructions. The processor must be in privileged mode to read from and write to the Coprocessor Access Control (CPAC) register.
Exceptions: The FPU sets the cumulative exception status flag in the FPSCR register as required for each instruction. The FPU does not support user-mode traps.
The processor can reduce the exception latency by using lazy stacking*. This means that the processor reserves space on the stack for the FPU state, but does not save that state information to the stack.
CMSIS...
* with a StellarisWare API function call
Notes: Some exceptions here. The floating point unit sets the accumulative exception status flag in the exception register as required for each instruction. The floating point unit does not support any user type traps that you might write. The processor can reduce the exception latency by using something called lazy stacking. We have a StellarisWare API function call to do that. Lazy stacking means that the processor reserves space on the stack for the state, but it doesn't save that state information to the stack unless it's necessary.

## Slide 78: CMSIS* DSP Library Performance
Source: ARM CMSIS Partner Meeting Embedded World, Reinhard Keil
  DSP Library Benchmark: Cortex M3 vs. Cortex M4 (SIMD + FPU)
  Fixed-point ~ 2x faster
  Floating-point ~ 10x faster
* - ARM® Cortex™ Microcontroller Software Interface Standard
Lab...
Notes: ARM has developed the Cortex Microcontroller Software Interface Standard, or CMSIS. Included in that is a DSP library that you could use to create your own DSP-type functions. If we benchmark the cortex M3 versus the cortex M4 with its floating point unit, the cortex M4, even in fixed point code, is about twice as fast as the cortex M3. In floating point, it's about ten times faster than the cortex M3.
If you look at the diagram down at the bottom for a Q15 fir, Q15 is where we have a sign bit and 15 bits of fraction. In fixed point, you can see we're operating about 75 percent faster on the M4. For a PID loop in the same Q15 style, we're about 35 percent faster. For an infinite impulse response filter and IAR, this one is a 32-bit sign bit and 31 fractional bits. We're about 69 percent faster on the cortex M4. For fixed point matrix multiplication, we're about 70 percent faster on the M4. And correlation in floating point, we're 91 percent faster.

## Slide 79: Lab 9: FPU
Experiment with the FPU
Profile floating-point code
Agenda ...
USB Emulation Connection
Notes: In lab nine, you'll experiment with using floating point code to generate a sign wave. You'll profile the code to determine how many CPU cycles it requires to execute.

## Slide 80: Agenda
LaunchPad Boards...
Introduction to ARM® Cortex™-M4F and Peripherals
Code Composer Studio
Introduction to StellarisWare, Initialization and GPIO
Interrupts and the Timers
ADC12
Hibernation Module
USB
Memory
Floating-Point
BoosterPacks and grLib
Synchronous Serial Interface
UART
µDMA
Notes: The LaunchPad design first implemented with the MSP430 has been a success because of two major factors. One, it's inexpensive, and two, it's expandable. Expansion is accomplished through the booster pack connector. The Stellaris LaunchPad implements an upgraded version called Booster Pack XL.
Texas Instruments offers some booster pack kits, but many more are offered by third parties. One of those third parties is Kentech, and you'll be using their LCD touchscreen booster pack in the lab. In order to get the most from the display, you'll learn about StellarisWare's graphics library. That library includes functions for drawing images, text, and shapes on the screen, as well as implementing touchscreen buttons.

## Slide 81: TI LaunchPad Boards
MSP430 $9.99US
Stellaris $12.99US
C2000 Piccolo $17.00US
BoosterPack Connectors...
Notes: TI currently makes three LaunchPad style evaluation boards: the MSP430 for $4:30, the Stellaris LaunchPad board for $12.99, and the C2000 Piccolo LaunchPad board for $17.

## Slide 82: BoosterPack Connectors
Original Format (MSP430)
  VCC and Ground
  14 GPIO
  Emulator Reset and Test
  Crystal inputs or 2 more GPIO
XL Format (Stellaris/C2000) is a superset of the original, adding two rows of pins with:
  USB VBUS and Ground
  18 additional GPIO
Available Boosterpacks...
Notes: Expandability is an important feature of the LaunchPad evaluation boards. This is done through the booster pack connectors. The original format of that connector was on the MSP430 board. That offered VCC and ground, as many as 14 GPIO pins. Emulator reset and test could come out to those pins. And you either connected to the crystal inputs, or there were two more GPIO.
The Stellaris and the C2000 Piccolo boards have the XL format. This is a superset of the original, which adds two more rows of pins. You can see the outside rows of pins that are noted by J1 on the outside left and J2 on the outside right. They're joined by J3 and J4 just to the insides of both of them. This adds the USB voltage and ground and 18 additional GPIO.

## Slide 83: Some of the Available BoosterPacks
TMP006 IR Temperature Sensor
C5000 Audio Capacitive Touch
Olimex 8x8 LED Matrix
Sub-1GHz RF Wireless
TPL0501 SPI Digital Pot.
TPL0401 SPI Digital Pot.
RF Module w/ LCD
Inductive Charging
Solar Energy Harvesting
Universal Energy Harvesting
Capacitive Touch
Proto Board
Available Boosterpacks...
Notes: To give you a flavor of some of the available booster packs, most of these are from third parties. Some of these are made by TI. Solar energy harvesting, universal energy harvesting, those are by EnerChip. We have RF modules with LCDs, inductive charging. The Olimex eight-by-eight LED matrix is stackable. The sub one gigahertz RF wireless module uses the simplicity protocol. That's from Anaren. We also have a protoboard down at the bottom from Joe's bytes.
TI makes the capacitive touch board. We make a couple of digital potentiometer boards. We have the C5000 audio capacitive touchboard and the TMP006 infrared temperature sensor board.

## Slide 84: Some of the Available BoosterPacks
Proto board
ZigBee Networking
OLED Display
LCD Controller Development Package
Click Board Adapter
MOD Board Adapter
Kentec LCD Display...
Notes: To round out the list, there's another protoboard with some additional capabilities out there. Anaren also makes a ZigBee networking booster pack. Kentech makes a nice OLED display if you're interested in working with OLEDs. There is a LCD controller development package available, and there's a couple of adaptors, one for mod boards and one for the click board type of modules that will plug right onto the top of the booster pack.

## Slide 85: KenTec TouchScreen TFT LCD Display
Part# EB-LM4F120-L35
Designed for XL BoosterPack pinout
3.5” QVGA TFT 320x240x16 color LCD with LED backlight
Driver circuit and connector are compatible with 4.3”, 5”, 7” & 9”displays
Resistive Touch Overlay
grLib Overview...
Notes: The booster pack we'll be using here in the class is the Kentech touchscreen TFTL CD display. There's the part number. This is the three-and-a-half-inch QVGA TFT. It's 320 by 240, and it's 16 colors with an LED backlight. And it's designed for the XL booster pack pinout.
The driver circuit and the connector are compatible with the 4.3-inch, 5-inch, 7-inch, and 9-inch displays, so you can use the same connector. If you turn your board over, you can see that the flat pin or the flat cable can be wiggled out of there, and you can use that to connect to any of these other displays. The board is covered with a resistive touch overlay, and we're going to get a chance to use the display and the touch overlay in the lab.

## Slide 86: Graphics Library Overview
The Stellaris Graphics Library provides graphics primitives and widgets sets for creating graphical user interfaces on Stellaris controlled displays.
Note that Stellaris devices do not have an LCD interface. The interface to smart displays is done through serial or EPI ports.
The graphics library consists of three layers to interface your application to the display:
Display Driver Layer*
Graphics Primitives Layer
Widget Layer
Your Application Code*
* = user written or modified
grLib Overview...
Notes: The Stellaris graphics library provides you with graphics, primitives, and widgets for creating an entire graphic user interface on Stellaris-controlled displays. A lot of folks will go all the way to using Linux on a machine just to get a better graphic user interface. Here, you can use a smaller, less expensive microcontroller and design your own.
Note that the Stellaris devices, none of the ones that we've covered, have an LCD interface. That's on the roadmap, but it's not there today. The interface to smart displays, it's either done through the serial port or through the EPI port on those parts that have them. The graphics library consists of three layers to interface your application to the display. At the very bottom is the display driver layer. You either have to write this, or you have to modify it for the target display that you're using.
We've had people do this, and it usually takes them in the two to three day range to modify their display driver to fit with the board that they're working with. This means you're either going to change the resolution, you're going to change the color, you're going to change the way that it's connected. We'll see some more about that in a second.
The next layer is the graphics primitives layer for drawing additional pieces to the screen. At the very top of that is the widget layer. The widgets are for tying touchscreen elements to code-based interaction. Your application code can interface with any one of these. You can interface with the display driver because the display driver is going to control things like the contrast and so on.
You may want to just send pictures and images to the screen. That'll be through the graphics primitives layer. Or if you want to use the touchscreen, that will be through the widget layer. So, your application code can access any of the layers of graphics library.

## Slide 87: Graphics Library Overview
The design of the graphics library is governed by the following goals:
Components are written entirely in C except where absolutely not possible.
Your application can call any of the layers.
The graphics library is easy to understand.
The components are reasonably efficient in terms of memory and processor usage.
Components are as self-contained as possible.
Where possible, computations that can be performed at compile time are done there instead of at run time.
Display Driver...
Notes: The design of the graphics library has been governed by the following goals: that the components have been written entirely in C except where absolutely not possible. Your application, like I mentioned on the previous slide, can call any of the layers. The graphics library is easy to understand, and the components are reasonable efficient in terms of memory and processor usage. Now, those two things can be slightly at odds with each other. It can be so efficient that you can't understand it, and if you can't understand it, you're not going to be able to use it.
The components are as self-contained as they can be, and where possible, any of the computations that need to be performed will be performed at compile time instead of using up cycles on your CPU at runtime.

## Slide 88: Display Driver
Routines for display-dependent operations like:
  Initialization
  Backlight control
  Contrast
  Translation of 24-bit RGB values to screen dependent color map
Drawing routines for the graphics library like:
  Flush
  Line drawing
  Pixel drawing
  Rectangle drawing
User-modified Hardware Dependent Code
  Connectivity of the smart display to the LM4F
  Changes to the existing code to match your display (like color depth and size)
Low level interface to the display hardware
Graphics Primitives...
Notes: Within the graphics library, the bottom layer is the display driver. That's the low-level interface to the display hardware. So, routines for display-dependent operations, like initializing the display, backlight control, contrast, translation of 24-bit RGB values to the screen-dependent color map. This means all the layers above will represent colors as 24-bit values. Your screen may only have 16 colors. It may be black and white. Whatever it is, we need to translate those values to whatever your screen can display.
The display driver also contains low-level drawing routines, like flush, lines, pixels, rectangle drawing, very simple type stuff. Your hardware-dependent code, the things that you have to modify are, for example, the connectivity of your smart display to the LM4F. Is this going to be through the serial port? Are you going to talk to it through the extended peripheral interphase? Currently, there's no EPIs on any of the LM4Fs, but who's to say they may be there in the future. Changes to the existing code to match your display, like the color depth, the size of it, and so on.

## Slide 89: Graphics Primitives
Low level drawing support for:
Lines, circles, text and bitmap images
Support for off-screen buffering
Foreground and background drawing contexts
Color is represented as a 24-bit RGB value (8-bits per color)
  ~150 pre-defined colors are provided
153 pre-defined fonts based on the Computer Modern typeface
Support for Asian and Cyrillic languages
Widgets...
Notes: The middle layer in the graphics library is graphics primitives. That gives you drawing support for lines, circles, text, and bitmap images. Support for off-screen buffering. Many times you don't want to write directly to the display and have people see you writing to the display. Instead, you'll write to an off-screen buffer and then swap and show that buffer. Being able to have foreground and background drawing context. So, you can put something behind something else.
Like I mentioned previously, the colors here and above are represented as 24-bit RGB values. That's eight bits per color. There are 150 predefined colors already provided in the map, and if you look in the Graphics Library User's Guide, you'll find those predefined colors in the back.
Also in the back of that are the 153 predefined fonts based on the computer modern typeface. In the lab, you can go in there and you can change the colors and you can change the typeface if you like to something else. All of those are listed in the back of the Graphics Library User's Guide. And as shown in the diagrams at the bottom of the screen, we have support for Asian and Cyrillic languages.

## Slide 90: Widget Framework
- Widgets are graphic elements that provide user control elements
- Widgets combine the graphical and touch screen elements on-screen with a parent/child hierarchy so that objects appear in front or behind each other correctly
  Canvas – a simple drawing surface with no user interaction
  Checkbox – select/unselect
  Container – a visual element to group on-screen widgets
  Push Button – an on-screen button that can be pressed to perform an action
  Radio Button – selections that form a group; like low, medium and high
  Slider – vertical or horizontal to select a value from a predefined range
  ListBox – selection from a list of options
Special Utilities...
Notes: Widgets are the top of the graphics library system. Widgets are graphic elements that provide user control elements. They combine the graphical and the touchscreen elements on screen in a parent-child hierarchy so that objects appear in front or behind each other as they're supposed to. So, you may have a canvas on the screen that's the grandparent, and then that will be followed by the parent that may be something like a rectangular element or some kind of color. And then in the front of that may be the child, which could be the widgets.
Now, that hierarchy can extend multiple layers. So, things like canvasses, that's a simple drawing surface with no interaction that you're going to put things on top of. You can have checkboxes to select or unselect things. You can have containers that will group on-screen widgets together. You can have pushbuttons, an on-screen button that can be pressed to perform an action. Radio buttons that are selections to form a group, like low, medium, and high. Sliders. We have sliders. Vertical or horizontal to select the value from a predefined range. And we can also do a list box, like a pull-down, which gives you a selection from a list of options.
And if you take a look there on the right-hand side, that's a pretty good representation of what you can see and what you can do with the graphics library and the widgets.

## Slide 91: Special Utilities
Utilities to produce graphics library compatible data structures
  ftrasterize
  Uses the FreeType font rendering package to convert your font into a graphic library format.
  Supported fonts include: TrueType®, OpenType®, PostScript® Type 1 and Windows® FNT.
  lmi-button
  Creates custom shaped buttons using a script plug-in for GIMP. Produces images for use by the pushbutton widget.
  pnmtoc
  Converts a NetPBM image file into a graphics library compatible file.
  NetPBM image formats can be produced by: GIMP, NetPBM, ImageMajik and others.
  mkstringtable
  Converts a comma separated file (.csv) into a table of strings usable by graphics library for pull down menus.
Lab...
Notes: We have some special utilities to produce graphics library compatible data structures. For instance, ftrasterize. It uses a free-type font rendering package to convert whatever font that you want into a graphic library format and you can see the supported font types there.
So, for instance, if your company uses a certain type of font in its documentation or in its logo, you could use that same font on the screen, even though the graphics library doesn't have it specifically in those 153. We can also do this LMI button and create a custom-shaped button using a plug-in for GIMP. It will produce an image for use by the pushbutton widget, so your pushbutton could, say, look exactly like your company headquarters. Or it could look exactly like your company logo.
The one we're going to use in the lab is PNM to C. This converts a net PBM imagine file. The net PBM imagine file is basically it looks like an array into a graphics library compatible file, which is an array. It's just a C file. The net PBM image formats, you can produce those with GIMP, with net PBM, with ImageMagick. There are others. In the lab, we're going to use GIMP.
There's also make string table. This converts a comma-separated file, a CSV, into a table of strings that's usable by the graphics library for those pull-down menus.

## Slide 92: Lab 10: Graphics Library
Connect Kentec Display
Experiment with demo project
Write graphics library code
USB Emulation Connection
Agenda ...
Notes: In lab ten, you'll use the Kentech LCD touchscreen display on the LaunchPad board to experiment with graphics library. You'll write code that places an image, text, and shapes on the LCD. Then you'll experiment with the touchscreen by adding a rectangular button widget that controls the LED on the LaunchPad board.

## Slide 93: Agenda
Features...
Introduction to ARM® Cortex™-M4F and Peripherals
Code Composer Studio
Introduction to StellarisWare, Initialization and GPIO
Interrupts and the Timers
ADC12
Hibernation Module
USB
Memory
Floating-Point
BoosterPacks and grLib
Synchronous Serial Interface
UART
µDMA

## Slide 94: LM4F120H5QR SSI Features
Block Diagram ...
Four SSI modules. Each with:
Freescale SPI, MICROWIRE or TI Synchronous Serial interfaces
Master or Slave operation
Programmable bit clock rate and pre-scaler
Programmable data frame size from 4 to 16-bits
Separate Tx and Rx FIFOs ( 8 x16-bits )
Interrupts and µDMA support

## Slide 95: SSI Block Diagram
Interrupts...
Signal Pinout (n = 0 to 3) …
SSInClk: SSI Module n Clock
SSInFss: SSI Module n Frame Signal
SSInRx: SSI Module n Receive
SSInTx: SSI Module n Transmit
Note that the LM4F120H5QR pins are extensively muxed with other signals.
The Pin Mux Utility can ease the programming. See:
www.ti.com/stellarispinmuxutility

## Slide 96: SSI Interrupts
Operation...
Single interrupt per module, cleared automatically
Interrupt conditions:
Transmit FIFO service (when the transmit FIFO is half full or less)
Receive FIFO service (when the receive FIFO is half full or more)
Receive FIFO time-out
Receive FIFO overrun
End of transmission
Receive DMA transfer complete
Transmit DMA transfer complete
Interrupts on these conditions can be enabled individually
Your handler code must check to determine the source of the SSI interrupt and clear the flag(s)

## Slide 97: SSI µDMA Operation
Separate channels for Tx and Rx
When enabled, the SSI will assert a DMA request on either channel when the Rx or Tx FIFO can transfer data
For Rx channel: A single transfer request is made when any data is in the Rx FIFO. A burst transfer request is made when 4 or more items is in the Rx FIFO.
For Tx channel: A single transfer request is made when there is at least one empty location in the Tx FIFO. A burst transfer request is made when 4 or more slots are empty.
Signal Formats...
1
2

## Slide 98: Freescale SPI Signal Formats
TI Signal Formats ...
Four wire interface. Full duplex.
SSIFss acts as chip select
Inactive state and clock phasing are programmable via the SPO and SPH bits (SSI_FRF_MOTO_MODE_0-3 parameter)
  SPO = 0: SSIClk low when inactive. SPO = 1: high
  SPH = 0: Data is captured on 1st SSIClk transition. SPH = 1: 2nd
SPO = 0
SPH = 0
Single
Transfer
SPO = 0
SPH = 1
Single
Transfer

## Slide 99: TI Synchronous Serial Signal Formats
Microwire Signal Formats...
Three wire interface
Devices are always slaves
SSIClk and SSIFss are forced low and SSITx is tri-stated when the SSI is idle
Single
Transfer
Continuous
Transfer

## Slide 100: Microwire Signal Formats
Lab...
Four wire interface
Similar to SPI, except transmission is half-duplex
Master – Slave message passing technique
Single
Transfer
Continuous
Transfer

## Slide 101: Lab 11 : SPI Bus and the Olimex LED Boosterpack
Carefully install pin-modified Olimex BoosterPack
Run faces program (SoftSSI)
Carefully install proto-board modified Olimex BoosterPack
Create program to utilize SSI SPI
USB Emulation Connection
Agenda ...

## Slide 102: Agenda
Introduction to ARM® Cortex™-M4F and Peripherals
Code Composer Studio
Introduction to StellarisWare, Initialization and GPIO
Interrupts and the Timers
ADC12
Hibernation Module
USB
Memory
Floating-Point
BoosterPacks and grLib
Synchronous Serial Interface
UART
µDMA
Features...

## Slide 103: UART Features
Separate 16x8 bit transmit and receive FIFOs
Programmable baud rate generator
Auto generation and stripping of start, stop, and parity bits
Line break generation and detection
Programmable serial interface
  5, 6, 7, or 8 data bits
  even, odd, stick, or no parity bits
  1 or 2 stop bits
  baud rate generation, from DC to processor clock/16
Modem control/flow control
IrDA and EIA-495 9-bit protocols
µDMA support
Block Diagram...

## Slide 104: Block Diagram
Basic Operation...

## Slide 105: Basic Operation
Initialize the UART
  Enable the UART peripheral, e.g.
    SysCtlPeripheralEnable(SYSCTL_PERIPH_UART0);
    SysCtlPeripheralEnable(SYSCTL_PERIPH_GPIOA);
  Set the Rx/Tx pins as UART pins
    GPIOPinConfigure(GPIO_PA0_U0RX);
    GPIOPinConfigure(GPIO_PA1_U0TX);
    GPIOPinTypeUART(GPIO_PORTA_BASE, GPIO_PIN_0 | GPIO_PIN_1);
  Configure the UART baud rate, data configuration
    ROM_UARTConfigSetExpClk(UART0_BASE, ROM_SysCtlClockGet(), 115200,
    UART_CONFIG_WLEN_8 | UART_CONFIG_STOP_ONE |
    UART_CONFIG_PAR_NONE));
  Configure other UART features (e.g. interrupts, FIFO)
Send/receive a character
  Single register used for transmit/receive
  Blocking/non-blocking functions in driverlib:
    UARTCharPut(UART0_BASE, ‘a’);
    newchar = UARTCharGet(UART0_BASE);
    UARTCharPutNonBlocking(UART0_BASE, ‘a’);
    newchar = UARTCharGetNonBlocking(UART0_BASE);
Interrupts...

## Slide 106: UART Interrupts
Single interrupt per module, cleared automatically
Interrupt conditions:
  Overrun error
  Break error
  Parity error
  Framing error
  Receive timeout – when FIFO is not empty and no further data is received over a 32-bit period
  Transmit – generated when no data present (if FIFO enabled, see next slide)
  Receive – generated when character is received (if FIFO enabled, see next slide)
Interrupts on these conditions can be enabled individually
Your handler code must check to determine the source of the UART interrupt and clear the flag(s)
FIFOs...

## Slide 107: Using the UART FIFOs
Both FIFOs are accessed via the UART Data register (UARTDR)
After reset, the FIFOs are enabled*, you can disable by resetting the FEN bit in UARTLCRH, e.g.
UARTFIFODisable(UART0_BASE);
Trigger points for FIFO interrupts can be set at 1/8, 1/4, 1/2,3/4, 7/8 full, e.g.
UARTFIFOLevelSet(UART0_BASE,
UART_FIFO_TX4_8,
UART_FIFO_RX4_8);
Transmit FIFO
UART_FIFO_TX4_8
UART_FIFO_TX1_8
UART_FIFO_TX2_8
UART_FIFO_TX6_8
UART_FIFO_TX7_8
FIFO Level Select
* Note: the datasheet says FIFOs are disabled at reset
stdio Functions...

## Slide 108: UART “stdio” Functions
StellarisWare “utils” folder contains functions for C stdio console functions:
  c:\StellarisWare\utils\uartstdio.h
  c:\StellarisWare\utils\uartstdio.c
Usage example:
  UARTStdioInit(0); //use UART0, 115200
  UARTprintf(“Enter text: “);
See uartstdio.h for other functions
Notes:
  Use the provided interrupt handler UARTStdioIntHandler() code in uartstdio.c
  Buffering is provided if you define UART_BUFFERED symbol
    Receive buffer is 128 bytes
    Transmit buffer is 1024 bytes
Other UART Features...

## Slide 109: Other UART Features
Modem control/flow control
IrDA serial IR (SIR) encoder/decoder
  External infrared transceiver required
  Supports half-duplex serial SIR interface
  Minimum of 10-ms delay required between transmit/receive, provided by software
ISA 7816 smartcard support
  UnTX signal used as a bit clock
  UnRx signal is half-duplex communication line
  GPIO pin used for smartcard reset, other signals provided by your system design
LIN (Local Interconnect Network) support: master or slave
µDMA support
  Single or burst transfers support
  UART interrupt handler handles DMA completion interrupt
EIA-495 9-bit operation
  Multi-drop configuration: one master, multiple slaves
  Provides “address” bit (in place of parity bit)
  Slaves only respond to their address
Lab...

## Slide 110: Lab 12: UART
Initialize UART and echo characters using polling
Use interrupts
Use stdio utility, e.g. UARTprintf()
USB Emulation Connection

## Slide 111: Agenda
Features...
Introduction to ARM® Cortex™-M4F and Peripherals
Code Composer Studio
Introduction to StellarisWare, Initialization and GPIO
Interrupts and the Timers
ADC12
Hibernation Module
USB
Memory
Floating-Point
BoosterPacks and grLib
Synchronous Serial Interface
UART
µDMA

## Slide 112: µDMA Features
Transfer types...
32 channels
SRAM to SRAM , SRAM to peripheral and peripheral to SRAM transfers (no Flash or ROM transfers are possible)
Basic, Auto (transfer completes even if request is removed), Ping-Pong and Scatter-gather (via a task list)
Two priority levels
8, 16 and 32-bit data transfer sizes
Transfer sizes of 1 to 1024 elements (in binary steps)
CPU bus accesses outrank DMA controller
Source and destination address increment sizes: size of element, half-word, word, no increment
Interrupt on transfer completion (per channel)
Hardware and software triggers
Single and Burst requests
Each channel can specify a minimum # of transfers before relinquishing to a higher priority transfer. Known as “Burst” or “Arbitration”

## Slide 113: Transfer Types
Basic
  Single to Single
  Single to Array
  Array to Single
  Array to Array
Auto
  Same as Basic but the transfer completes even if the request is removed
Ping-Pong
  Single to Array (and vice-versa). Normally used to stream data from a peripheral to memory. When the PING array is full the µDMA switches to the PONG array, freeing the PING array for use by the program.
Scatter-Gather
  Many Singles to an Array (and vice-versa). May be used to read elements from a data stream or move objects in a graphics memory frame.
Block diagram...

## Slide 114: µDMA Block Diagram
Channels...

## Slide 115: µDMA Channels
Each channel has 5 possible assignments made in the DMACHMAPn register
S = Single
B = Burst
SB = Both
Configuration...

## Slide 116: Channel Configuration
Channel control is done via a set of control structures in a table
The table must be located on a 1024-byte boundary
Each channel can have one or two control structures; a primary and an alternate
The primary structure is for BASIC and AUTO transfers. Alternate is for Ping-Pong and Scatter-gather
Control Structure Memory Map
Channel Control Structure
Control word contains:
Source and Dest data sizes
Source and Dest addr increment size
# of transfers before bus arbitration
Total elements to transfer
Useburst flag
Transfer mode
Lab...

## Slide 117: Lab 13: Transferring Data with the µDMA
Perform an array to array memory transfer
Transfer data to and from the UART
USB Emulation Connection
Wrap-up ...
Notes: In lab one, you'll obtain and install all the needed hardware and software, as well as test out the pre-installed application software on the LaunchPad board.

## Slide 118: Thanks for Attending!
Make sure to take your kits and workbooks with you
Please leave the TTO flash drives and meters here
Please fill out the feedback form
Have safe trip home!

## Slide 119
Presented by
Texas Instruments
Technical Training Organization
www.ti.com/training