G722 on TMS320C55X Version 1.20.00

Release Notes

May 2009

The ITU G.722 converts digitized, linear PCM input signals (15 bits) sampled at 16 KHz sampling rate into a 64Kbps SB-ADPCM bit-stream. Encoder Compresses linear PCM input signals (15 bits) sampled at 16 kHz sampling rate into a 64Kbps SB-ADPCM bit-stream and Decoder expands 48/56/64Kbps bitstream into PCM samples of 15 bits each at 16 KHz.

Salient features of this product are described below.

Bit Compliant with ITU-T G.722 specifications

Optimized for TI C55x DSP

C callable interface for encoder and decoder

Re-entrant multi channel implementation

eXpressDSP™ compliant

Supports ITU-T G.722 Appendix IV for Packet Loss Concealment (PLC)

Fully interruptible Code

Relocatable tables

This release supports both Large and Small Memory Models

Efficient Scratch memory management with reduced stack requirements

The implementation support run time data buffers relocation & table relocation

Fully validated on TMS320C5510 DSK, using CCS version 3.3 with the code generation tools version 3.3.1

TABLE OF CONTENTS

1	New In This Release	3

2	System Requirements	3

3	Building G722 on TMS320C64X	3

4	Release Contents	3

5	Fixed In This Release	3

6	Known Issues	3

# New In This Release

- This release supports packet loss concealment of lost or corrupted frames as defined by ITU-T G722 Appendix IV.

# System Requirements

Refer to section 2.1 of G722_XDAIS_UserManual_C55x.doc

# Building G722 on TMS320C64X

Refer to chapter 2.3 of G722_XDAIS_UserManual_C55x.doc

# Release Contents

Refer to chapter 2.2 of G722_XDAIS_UserManual_C55x.doc

# Fixed In This Release

- None

# Known Issues

- None