## Slide 1: VHWA (Vision Hardware Accelerator)

## Slide 2: Agenda
VHWA Drivers in PDK
  Driver Architecture
  FVID2 Interface
  Application Flow
VPAC Overview
  Multi-Scalar
  NF
  LDC
  VISS
DMPAC Overview
  DOF
  SDE

## Slide 3: VHWA Drivers in PDK

## Slide 4: VHWA Driver Architecture
LDC
Hardware
FVID2 API
Application (TI – RTOS)
MSC
NF
VISS
DOF
DOF
HTS
LSE
UTC
SL2
CSL
LDC
MSC
NF
DOF
SDE
RFE
FCC
NSF4
GLBCE
H3A
HTS
LSE
VTOP
DTOP
M2M
LDC
M2M
MSC
2 INST
M2M
NF
M2M
VISS
M2M
DOF
M2M
SDE
RES
MNGR
OSAL
INTR
MNGR
Q
M
N
G
R
OpenVX Nodes

## Slide 5: VHWA FVID2 Driver: Understanding FVID2 Interface
FVID2 APIs:
  FVID2_init
    Initializes the drivers and the hardware. Should be called before calling any of the FVID2 functions
  FVID2_deInit
    Un-initializes the drivers and the hardware
  FVID2_create
    Opens a instance/channel video driver
  FVID2_delete
    Closes a instance/channel of a video driver
  FVID2_control
    To send standard (set/get format, alloc/free buffers etc..) or device/driver specific control commands to video driver
  FVID2_processRequest
    Submit a pixel processing request to the driver. Used in memory to memory drivers
  FVID2_getProcessRequest
    Get back the completed pixel processing request from the driver

## Slide 6: VHWA FVID2 Driver: Application Flow
FVID2 Init
UDMA Init
VHWA Driver Init
Open Driver
FVID2_Create
SET Params
SET_PARAMS IOCTL
SET Config
SET_CONFIG IOCTL
Submit Process Request
FVID2_processRequest
Wait for Completion
Get processed Request
FVID2_getProcesedReq
Close Driver
FVID2_Delete
Frame Completion Callback – Signals Task
Sets path, Selects number of input/output, their frame size and format etc,
Sets IP specific configuration
Init/DeInit Sequence
Task Context
ISR Context
Based on timeout value Blocks until HW is free.
Triggers the HW
Returns the last completed request
FVID2 DeInit
UDMA DeInit
VHWA Driver DeInit
Closes Instance handle, release resources

## Slide 7: VPAC (Vision Pre-Processing Accelerator)

## Slide 8: VPAC Block Diagram
HTS: Hardware Thread Scheduler
UTC: Universal Transfer Controller
NF: Noise Filter
LDC: Lens Distortion Correction
VISS: Vision Image signal Processing
SL2: Level-2 Memory
Video Imaging Sub-System (VISS)
Noise Filter (NF)
Multi-Scalar (MSC)
Lens Distortion Correction (LDC)
Shared Memory (SL2)
Interrupt Distributor (INTD)
Unified Transfer Controller (UTC) x2
CTSET
SCR
CSI-Rx_IF0
Hardware Thread Scheduler

## Slide 9: Typical Functional Flow in VPAC
DDR
DSP
& ARM
CSI2Rx
Image
Sensors
SDE-Depth
DOF-Motion
Depth, Confidence
Motion, Confidence
DMPAC
RFE
FCP
LDC
SCALER
Lens Corrected Base Image
Pyramids
VISS
VPAC
NF

## Slide 10: Scalar: Introduction
Downscaling ratio is between 1x and 0.25x
Programmable kernel sizes for vertical/horizontal filter (3,4, or 5)
4 sets of 5 tap-32 phase coefficients
  Two set can be combined to support 5-tapx64-phase filters
2 additional sets of 5-tap Gaussian filter coefficients (single-phase) dedicated for Pyramid (Octave) generation
12 bit input & output
Programmable ROI for input and output for each scalar
Performance: 1pixel/cycle
Data Format | Input Bit Depth | Output Bit Depth | Data Format | Input Bit Depth | Output Bit Depth
Luma | 8Bit | 8Bit | Chroma | 8Bit | 8Bit
 |  | 12Bit |  |  | 12Bit
 | 12bit | 8Bit |  | 12bit | 8Bit
 |  | 12Bit |  |  | 12Bit
Supported DataFormats
Video Imaging Sub-System (VISS)
Noise Filter (NF)
Multi-Scalar (MSC)
Lens Distortion Correction (LDC)
Shared Memory (SL2)
Interrupt Distributor (INTD)
Unified Transfer Controller (UTC) x2
CTSET
SCR
Hardware Thread Scheduler

## Slide 11: MSC: Multiple Scaling
Down Scalar #1
Down Scalar #2
Down Scalar #3
Down Scalar #10
Input Thread #1
Input Thread #2
SCALER HW
Downscale o/p#1
Downscale o/p#2
Downscale o/p#3
Downscale o/p#10

## Slide 12: Bilateral Noise Filter
Support for bilateral and general filtering
Supports filter size upto 5x5
LUT based Bilateral weights generation
  8 bits for weight
  5 zones x 256 coefficients
Performance : 1 pixel/cycle
Supported formats: one plane (interleaved plane and non-interleaved) YUV 420, 12-bit
Data Format | Input Bit Depth | Output Bit Depth | Data Format | Input Bit Depth | Output Bit Depth
Luma | 8Bit | 8Bit | Chroma | 8Bit | 8Bit
 |  | 12Bit |  |  | 12Bit
 | 12bit | 8Bit |  | 12bit | 8Bit
 |  | 12Bit |  |  | 12Bit
Supported DataFormats
Video Imaging Sub-System (VISS)
Noise Filter (NF)
Multi-Scalar (MSC)
Lens Distortion Correction (LDC)
Shared Memory (SL2)
Interrupt Distributor (INTD)
Unified Transfer Controller (UTC) x2
CTSET
SCR
Hardware Thread Scheduler

## Slide 13: Mesh LDC
Purpose
  Remap pixels from a distorted input space to an undistorted output space.
  Apply perspective transform/homography operations.
Mechanism
  Perspective transform applied to output coordinates.
  Remap function described by a 2D offset table (Dx/Dy).
  Offsets are added to perspective output coordinates to locate input pixels.
  Interpolation applied to input data to compute output pixels.
Supported Formats
  YUV 420 & YUV422
  Up to 12 bits/component
Interpolation Type
  Bicubic (2 cyc/Pixel)
  Bilinear (1 cyc/Pixel)
Video Imaging Sub-System (VISS)
Noise Filter (NF)
Multi-Scalar (MSC)
Lens Distortion Correction (LDC)
Shared Memory (SL2)
Interrupt Distributor (INTD)
Unified Transfer Controller (UTC) x2
CTSET
SCR
Hardware Thread Scheduler

## Slide 14: Mesh Warp (LDC)
LDC &
Perspective Warp HW
FISHEYE LENS
Supports fisheye lenses upto 180/3600
PERSPECTIVE TRANFORM
Changing user view point
PERSPECTIVE TRANFORM
Stereo Rectification
14

## Slide 15: Mesh LDC: Data Formats
Input |  | Output | 
Data Mode | Data format | Data Mode | Data format
YUV420 (NV12) | 8bit | YUV420(NV12) | 8bit
 |  |  | 12bit - packed
 | 12bit - packed |  | 12bit - packed
 | 12bit - unpacked |  | 12bit - unpacked
Luma Only | 8bit | Luma Only | 8-bit
 |  |  | 12bit - packed
 | 12bit - packed |  | 12bit - packed
 | 12bit - unpacked |  | 12bit - unpacked
YUV420(NV12) Chroma Ony | 8bit | YUV420(NV12) Chroma Only | 8bit
 |  |  | 12bit packed
 | 12bit - packed |  | 12bit - packed
 | 12bit - unpacked |  | 12bit - unpacked
YUV422 (UYVY) | 8bit | YUV420(NV12) | 8bit
 |  |  | 12bit - packed

## Slide 16: Mesh LDC: Multi-Region
R-0
R-1
R-2
R-3
R-4
R-5
R-6
R-7
R-8
RW2
RW3
RH1
RH2
RH3
RW1
Solution in New LDC: Multi-Region LDC
Divide the frame into multiple slicing regions based on pattern of the transformation.
  Frame will be divided into up to 3 horizontal slices and 3 vertical slices-Total of 9 regions
Each region can be programmed with independent output block size and optimal pixel pad.
LDC can be programmed with bigger block size for region with less spatial variation (i.e. scaling factor) and smaller block size for region with high spatial variation
This improves the band width as well as performance as portion of the image with bigger block size increases
Ratio of Fetched block to output block size
No. of blocks
Distribution of fetched block sizes compared to output block size in ratio
Ideally the output block width (OBW) and output block height (OBH) should be sufficiently large but with the constraint that input block must fit into available internal memory.
Distortion in wide angle lenses causes block size to be very small due to extreme scaling in particular regions of the image in some cases specially the surround-view cases. This affects the performance of the LDC hardware and overall memory bandwidth.

## Slide 17: VISS Block Diagram
Input format : 16b unpacked (RAW10/12/14/16) , 12b packed
Output format : 12b yuv420, 8b yuv420, 8b RGB, 8b S8
Supports On-the-fly processing  Low latency DDR path (QoS through NavSS and MSMC)
Supports M2M processing
VISS
RAW Front End (RFE)
NSF4
GLBCE
FLEX Color Proc (FCP)
Input-0
Y12
UV12
Y8
UV8
S8
H3A
Input-1
Input-2

## Slide 18: VISS Features
Performance : 1 pixel/cycles
Support for 12/16 bit input RAW format
Support for 8/12 bit YUV output
Support for multiple RAW formats (e.g. Bayer, RCCC)
  Flexible to handle any 2x2 RAW format
Enables Support for other color spaces
  Support other color spaces e.g. Support for Color saturation and Gray scale for HSV/HSL etc (Hue is not supported)
  Enables RGB output
Support for Multiple WDR /HDR Formats and Up-to 3 Exposures
  Compounded format (12 & 14 bit formats)
  Stagger format of WDR
  Rest of WDR Format
Support of statistics for 3A (Auto-Exposure, Auto-white-balance and Auto-Focus)
Dual Output (Vision and Visual)
TI’s proven Visual Processing with proven Noise filter and GLBCE (Local Tone Mapping)

## Slide 19: RAW Front End (Processing in RAW Domain)
WDR Pre-processing, : To decompress sensor’s companded data
WDR Merge : Merge up to 3 RAW images into a WDR image
LSC : Lens Shading Correction using a pre-computed LUT read from memory
Digital WB Gain : Applies WB gains computed by AWB algorithm
H3A : Statistics generator for 3A (AWB, AE, AF) Algos.
GTM : Global Tone Map – Maps output of WDR merge block from 20->16 bpp
DPC : Defect Pixel Correction – OTF & LUT (256 entries) based

## Slide 20: Wide Dynamic Range
Consumer cameras have limited Dynamic Range (60 dB)
  Leads to clipped highlights or/and underexposed shadows
  Human visual system has a much higher dynamic range
WDR Sensor
  Capture Multiple exposures using time multiplexing and/or sensor architecture
  Combine multiple exposures or transmit them separately

## Slide 21: Flexible Color Processing
State-of-the-art TI’s 5th Generation Flexible CFA
  Can support any 2x2 RAW Sensor Pattern
Flexible Color Conversion Scheme
  Color Correction Matrix
  Flexible HSV color plane generation (S &V) only to support different standards
  12 bit/Component YUV 420 output generation
  Full color RGB (24 bits/pixel) output
VISS
RAW Front End (RFE)
NSF4
GLBCE
FLEX Color Proc (FCP)
Input-0
Y12
UV12
Y8
UV8
S8
H3A
Input-1
Input-2

## Slide 22: Flexible Color Processing
Low latency, On-The-Fly (OTF) operation of 3 key blocks
Global Tone Map (16 to 12)
  Used when locally adaptive Tone Map is disabled
Flexible CFA
  Generates 12 bit up to 4 color planes output (Eg Full Resolution RGBC or RGB IR)
Flexible Color Conversion
  Implements multiple color conversion schemes for both analytics / visual use cases

## Slide 23: Flexible Color Conversion
  Flexible architecture for supporting multiple data flows
  Color Correction Matrix (CCM) for supporting accurate color reproduction
  LUT Based Gamma correction / Contrast Stretch Module
  Flexible RGB-HSV Color generation (No Hue)
  RGB-YUV with programmable coefficients
  12 bit native output with option 8 bit using LUT based tone map.
23
  Supports RGB output / Supports Saturation outputs
  Supports Grayscale/Luma/IR/Clear Output
  Single cycle/pixel performance
  Support for flexible output format generation including YUV as well as custom

## Slide 24: DMPAC (Depth and Motion Perception Accelerator)

## Slide 25: DMPAC Block Diagram
DOF: Dense Optical Flow
SDE: Stereo Disparity Engine
UTC: Universal Transfer Controller
HTS: Hardware Thread Scheduler
SL2: Level-2 Memory
Dense Optical Flow (DOF)
Stereo Disparity Engine (SDE)
Shared Memory (SL2)
Interrupt Distributor (INTD)
Unified Transfer Controller (UTC)
CTSET
SCR
Hardware Thread Scheduler

## Slide 26: Dense Optical Flow (DOF)
Dense Optical Flow HWA
Input Video Frame
Input Video Frame
Dense Optical Flow
Object Tracking
Moving Object Segmentation
Applications

## Slide 27: DOF: Feature Set
Overview
  Optical Flow estimates 2D motion vector field given two images
  Pyramidal approach based coarse-to-fine search strategy
  Can estimate Large motions with fractional pixel precision
Features
  Input Image resolution: upto 2MPix (max)
  Max resolution 2048H x 1024V
  Input Image Frame Rate: upto 60fps
  Allows Scalability of input image resolution vs frame rate
    eg. higher fps at lower resolution
  12bit/pixel input and output format
  Other bit depths can be supported using Format Conversion Module
  Large Motion search range
  Dense flow vector map generated for each input pixel
  Confidence score generated for each flow vector output
  Supports Sparse optical flow
Dense Optical Flow (DOF)
Stereo Disparity Engine (SDE)
Shared Memory (SL2)
Interrupt Distributor (INTD)
Unified Transfer Controller (UTC)
CTSET
SCR
Hardware Thread Scheduler

## Slide 28: Stereo Disparity Engine (SDE)
Stereo Disparity Engine HWA
Input Video Frame: Left Camera
Input Video Frame: Right Camera
Depth Map
Object Distance Measurement
Large range applications
Collision Warning
Path Plannng
Applications

## Slide 29: SDE: Features Set
Overview
  Stereo estimates depth by measuring disparity from 2 different views
  Can run in parallel with Optical Flow
Feature set
  Input Image resolution: 2MPix (max)
  Max resolution 2048H x 1024V
  Input Image Frame Rate: 60fps (max with 2MPix)
  Allows Scalability of input image resolution vs frame rate
    eg. higher fps at lower resolution
  12bit/pixel input and output format
  Other bit depth can be supported using Format Conversion Module
  Disparity Search range of -3/+188 (far object)
  Dense disparity map for each input pixel
  Confidence score assigned for each disparity output
Dense Optical Flow (DOF)
Stereo Disparity Engine (SDE)
Shared Memory (SL2)
Interrupt Distributor (INTD)
Unified Transfer Controller (UTC)
CTSET
SCR
Hardware Thread Scheduler

## Slide 30
Questions? Thank You

## Slide 31
© Copyright 2019 Texas Instruments Incorporated. All rights reserved.
This material is provided strictly “as-is,” for informational purposes only, and without any warranty.
Use of this material is subject to TI’s Terms of Use, viewable at TI.com