## Slide 1: Capture on J7 through CSI2RX Controller – Deep Dive
13th March 2019
Camera
Serial
Interface

## Slide 2: Agenda
Capture Use-cases on J7
What’s CSI2?
CSI2RX Controller
CSI2RX FVID2 Driver

## Slide 3: Acronyms
CMS – Camera Mirror Systems
OTF – On the fly
WDR – Wide Dynamic Range
VC – CSI2 Virtual Channel
DT – CSI2 Data Type
VISS – Vision Imaging Sub System
ISP – Image Signal Processing
bpp – bits per pixel
ECC – Error Correction Code
I2C – Inter-Integrated Circuit
UDMA – Unified DMA Controller
PSI – Packet Streaming Interface
EMI – Electro Magnetic Interference
CRC – Cyclic Redundancy Check
DDR – Dual Data Rate
SoC – System on Chip

## Slide 4: Capture Use-case on J7

## Slide 5: Capture Use-case(1/3): Multi-Sensor (e.g. Surround View, CMS, Radar)
Sensor 1
Sensor 2
Sensor 3
Sensor 4
UB96x
FPDLink
CSI2RX-1
UDMA
CSI2
VBUS-M
PSI-L
De-serializer
Sensor
UB953
Serializer
CSI2
FPDLink
SoC
Sensor 1
Sensor 2
Sensor 3
Sensor 4
UB96x
FPDLink
CSI2RX-2
CSI2
De-serializer
DDR
CSI2RX-1 VC1 on UDMA RX
CH-0
DDR
CSI2RX-1 VC2 on UDMA RX
CH-1
DDR
CSI2RX-1 VC3 on UDMA RX
CH-2
DDR
CSI2RX-1 VC4 on UDMA RX
CH-3
DDR
CSI2RX-2 VC1 on UDMA RX
CH-4
DDR
CSI2RX-2 VC2 on UDMA RX
CH-5
DDR
CSI2RX-2 VC3 on UDMA RX
CH-6
DDR
CSI2RX-2 VC4 on UDMA RX
CH-7
Key Points,
4 sensors multiplexed on a single CSI2 port
De-multiplexing done using VC field
Each VC frame output to a separate buffer via a separate UDMA RX CH

## Slide 6: Capture Use-case(2/3): Single-Sensor (e.g. Front Camera, CMS, Radar)
Sensor
CSI2
CSI2RX-1
UDMA
VBUS-M
PSI-L
SoC
CSI2RX-2
DDR
CSI2RX-1 DT1 on UDMA RX
CH-0
DDR
CSI2RX-1 DT2 on UDMA RX
CH-1
DDR
CSI2RX-1 DT3 on UDMA RX
CH-2
DDR
CSI2RX-2 DT1 on UDMA RX
CH-3
DDR
DDR
Sensor
CSI2
High Exposure Frame
Normal Exposure Frame
Low Exposure Frame
High Exposure Frame
Normal Exposure Frame
Low Exposure Frame
DT1 = RAW10
DT2 = RAW12
DT3 = RAW14
Key Points,
Single sensor on a single CSI2 port
Single sensor can output multiple exposure frames using distinct “Data Type (DT)”
De-multiplexing done using DT field
Each DT frame output to a separate buffer via a separate UDMA RX CH
CSI2RX-2 DT2 on UDMA RX
CH-4
CSI2RX-2 DT3 on UDMA RX
CH-5

## Slide 7: Capture Use-case(3/3): Single-Sensor OTF (e.g. Front Camera, CMS)
VPAC
Sensor
CSI2
CSI2RX-1
VISS-1
VBUS-M
VPORT
SoC
DDR
CSI2RX-1, VISS-1 on UTC CH-0
UTC
CSI2TX-1
PSI-L
FPGA
CSI2
Storage
Raw Data Capture Card
Key Points,
Single camera on a single CSI2 port
CSI2RX output directly connects to VISS in VPAC
CSI2TX loopback to record raw data in real-time for offline analysis
Allows lower latency, lower DDR BW (some features like multi-exposure WDR not possible)

## Slide 8: What’s CSI2?

## Slide 9: Quick Facts
  Widely used in mobile and automotive applications
  High performance with low power and low EMI
  Compatible with MIPI D-PHY and/or MIPI C-PHY
  Unidirectional differential serial interface with high speed data and clock lanes
  Packet based protocol for data transmission
  Uses bi-directional control interface compatible with I2C standard

## Slide 10: CSI2 Standard
Up to 16 Virtual Channels(with v2.0)
Data formats supported:
  RAW6/7/8/9/10/12/14/(with v2.0)16/20
  RGB444/555/565/666/888
  YUV420 8/10 bit
  YUV422 8/10 bit
MIPI D-PHY: 2.5 Gbps per lane and 4 lanes in total

## Slide 11: CSI2RX Controller

## Slide 12: CSI2RX Controller: Features
Compliant with MIPI CSI‑2 v1.3
Virtual channel extension and RAW16/20 for MIPI CSI2 v2.0 support
Support of the MIPI CSI-2 protocol over DPHY PPI interface up to maximum 4*2.5 Gbps
Configurable Data Lane positions
Programmable Interrupt Events
Protocol Error Detection
Virtual Channel / Data type de-interleaving
Processing of data on 4 independently configurable Streams
Payload FIFO operation

## Slide 13: CSI2RX FVID2 Driver

## Slide 14: CSI2RX FVID2 Driver: Features
FVID2 Interface for applications
Capture of following formats:
  RAW8/10/12/14/16/20
  YUV422-10 bit
  RGB888
Up to 32 capture channels per CSI2RX controller instance
OTF mode and loop-back mode to re-transmission pads of CSI2TX controller
Error Handling and Recovery
FIFO handling
D-PHY configuration
Configurable number of Data Lanes to use and their ordering
Frame drop buffer programming in case of Queue did not happen in time

## Slide 15: CSI2RX FVID2 Driver: Overview(1/2)
Capture Application Layers
CSIRX Driver Directory Structure
Application Layer
UDMA Driver
CSL
Common
CSIRX
SHIM
External Serdes and Camera sensors
Capture Driver
FVID2 Interface

## Slide 16: CSI2RX FVID2 Driver: Overview(2/2)
Interface files:
  pdk/packages/ti/drv/csirx/csirx.h
    It is a capture driver interface file. Application should only include this file.
  pdk/packages/ti/drv/csirx/include/csirx_cfg.h
    It is a capture drivers configuration file.
Implementation files:
  pdk/packages/ti/drv/csirx/src
SoC files:
  pdk/packages/ti/drv/csirx/soc

## Slide 17: CSI2RX FVID2 Driver: Understanding FVID2 Interface
FVID2 APIs:
  FVID2_init
    Initializes the drivers and the hardware. Should be called before calling any of the FVID2 functions
  FVID2_deInit
    Un-initializes the drivers and the hardware
  FVID2_create
    Opens a instance/channel video driver
  FVID2_delete
    Closes a instance/channel of a video driver
  FVID2_control
    To send standard (set/get format, alloc/free buffers etc..) or device/driver specific control commands to video driver
  FVID2_queue
    Submit a video buffer to video driver. Used in display/capture drivers
  FVID2_dequeue
    Get back a video buffer from the video driver. Used in display/capture drivers
  FVID2_start
    Start video capture or display operation.
  FVID2_stop
    Stop video capture or display operation.

## Slide 18: CSI2RX FVID2 Driver: Usage - Application(1/3)
Building CSI2RX Driver:
gmake.exe -s -j csirx BOARD=j721e_sim CORE=mcu2_0 BUILD_PROFILE=release
Building CSI2RX Driver Sample Application:
gmake.exe -s -j csirx_capture_testapp BOARD=j721e_sim CORE=mcu2_0 BUILD_PROFILE=release
Application Calling Sequence

## Slide 19: CSI2RX FVID2 Driver: Usage-Configurations(2/3)
Create parameters(Csirx_CreateParams):
  numCh
    Number of channels to be configured/processed
  chCfg
    Channel configuration
  instCfg
    Instance configuration
  frameDropBuf
    Address of Frame Drop buffer
  frameDropBufLen
    Frame Drop buffer length in bytes
Channel configuration(Csirx_ChCfg):
  chId
    Unique channel ID
  chType
    Channel type: Capture, OTF, loop-back
  vcNum
    Virtual channel number
  inCsiDataType
    CSI2 data format for capturing
  outFmt
    Frame attributes like dimension, storage format specifier
Instance configuration(Csirx_InstCfg):
  enableCsiv2p0Support
    Optional CSI2 v2.0 support enable control
  numDataLanes
    Number of data lanes used for capturing
  dataLanesMap
    Position of data lanes
  enableErrbypass
    Error bypass mode control

## Slide 20: CSI2RX FVID2 Driver: Usage-Example(3/3)
Two channels RGB888 (1920 x 1080) capture configuration:
Code Snippet:
createPrms.numCh = 2U;
createPrms.chCfg[0U].chId = 0U;
createPrms.chCfg[0U].chType = CSIRX_CH_TYPE_CAPT;
createPrms.chCfg[0U].vcNum = 0U;
createPrms.chCfg[0U].inCsiDataType = FVID2_CSI2_DF_RGB888;
createPrms.chCfg[0U].outFmt.width = 1920U;
createPrms.chCfg[0U].outFmt.height = 1080U;
createPrms.chCfg[0U].outFmt.pitch[0U] = (1920U * 4U);
createPrms.chCfg[0U].outFmt.dataFormat = FVID2_DF_BGRX32_8888;
createPrms.chCfg[1U].chId = 1U;
createPrms.chCfg[1U].chType = CSIRX_CH_TYPE_CAPT;
createPrms.chCfg[1U].vcNum = 1U;
createPrms.chCfg[1U].inCsiDataType = FVID2_CSI2_DF_RGB888;
createPrms.chCfg[1U].outFmt.width = 1920U;
createPrms.chCfg[1U].outFmt.height = 1080U;
createPrms.chCfg[1U].outFmt.pitch[0U] = (1920U * 4U);
createPrms.chCfg[1U].outFmt.dataFormat = FVID2_DF_BGRX32_8888;

## Slide 21: CSI2RX FVID2 Driver: Un-supported Features
Capture of following formats:
  RAW6/7
  YUV420-8 bit
  RGB565/RGB666
Dynamic Stream configuration
Lane Polarity Position change
Clock Lane position configuration

## Slide 22
Questions? Thank You

## Slide 23
© Copyright 2019 Texas Instruments Incorporated. All rights reserved.
This material is provided strictly “as-is,” for informational purposes only, and without any warranty.
Use of this material is subject to TI’s Terms of Use, viewable at TI.com

## Slide 24: Backup

## Slide 25: CSI2RX Controller: Top-level Block Diagram

## Slide 26: CSI2RX Controller: J721E Integration
J721E Integration Overview
CSI2RX Functional Block Diagram